## Slide 1: Core Experiment Viewing Test Procedure and Results
JVET-O1118
Mathias Wien
Status: 2019-07-07 13:00h

## Slide 2: Test Setup
Procedure as CE11 test at last meeting [JVET-N0835]
LG OLED 55” display used, three test subjects per session at 1.6 × screen height distance
A-B-A-B presentation, assessment:
  “A was much better than B”
  “A was better than B”
  “B was better than A”
  “B was much better than A”.
Test cell design
  “A” – Video A – “B” – Video B – “A” – Video A – “B” – Video B – “Vote N”
  “A” / “B” presentation for 0.5sec
  Voting for 5sec

## Slide 3: Test Design
Placement of anchor and proposal as “A” and “B” randomized over test cells
Fixed order of sequences, looped over available test cells
Cell order (QP values, sub-CEs) randomized
Mix of (few) sequences which have various resolutions
  Decision to present all sequences up-scaled to UHD screen resolution using nearest neighbor interpolation

## Slide 4: Test Evaluation
Viewing votes mapping
  +3 : “Proposal much better than anchor”
  +1 : “Proposal better than anchor”
  -1 : “Anchor better than proposal”
  -3 : “Anchor much better than proposal”
Calculation of Mean Opinion Score (MOS) on this scale
Calculation of 95% confidence intervals based on MOS and standard deviation

## Slide 5: Overview on viewing sessions
CE05-3 (15 viewers, 12 cases) [completed]
CE05-2 (12 viewers, 60 cases) [completed]
Bilateral Filtering (12 cases) [completed]
NN-Filtering: Demo only – TBD

## Slide 6: CE05-3 Viewing Results
Test conducted on Fri. 2019-07-05
CE5-3 results assessed in one session only ALF-On tested as per Track-B decision from Thu 2019-07-04 morning
  12 test cases (cells)
  15 test subjects
  5 groups of three experts
Presentation in one session of 12 test cells
  9:30min viewing time per test cell (and group)

## Slide 7: CE05-3 Sequences under test
CE-description JVET-N1025
Num | Name | Resolution | fps | Frames | Mode | QP
01 | FoodMarket | 3840x2160p | 60fps | 600 | RA | 37, 32
02 | Campfire | 3840x2160p | 30fps | 300 | RA | 37, 32
03 | Cactus | 1920x1080p | 50fps | 500 | LDB | 32, 37
04 | KristenAndSara | 1280x720p | 60fps | 600 | LDP | 32, 37
05 | Red Kayak | 1920x1080p | 30fps | 300 | RA | 32, 37
06 | Johnny | 1280x720p | 60fps | 600 | LDB | 32, 37

## Slide 14: CE05-2 Viewing Results
Test conducted Fri. 2019-07-05 19:00, 07-06 09:00h, 07-06 19:30h
CE5-2 results assessed with ALF-On tested as per Track-B decision from Thu 2019-07-04 morning
  5 sub-CEs, inducing 60 test cases (cells)
  12 test subjects
  4 groups of three experts
Presentation in four session with 15 test cells each
  11:45 min viewing time per test cell (and group)
  Two times interleaved viewing of two groups, total time about 2h each

## Slide 15: CE05-2 Sequences under test
CE-description JVET-N1025
Num | Name | Resolution | fps | Frames | Mode | QP
01 | Redkayak | 1920x1080p | 30fps | 300 | RA | 32, 37
02 | Cactus | 1920x1080p | 50fps | 500 | LDB | 32, 37
03 | FourPeople | 1280x720p | 60fps | 600 | LDP | 32, 37
04 | KristenAndSara | 1280x720p | 60fps | 600 | LDP | 32, 37
05 | Kimono YCbCr 4:4:4 | 1920x1080p | 24fps | 240 | RA | 32, 37
06 | EBULupoAndCandleLight YCbCr 4:4:4 | 1920x1080p | 50fps | 500 | LDB | 32, 37

## Slide 16: CE05-2 Viewing Results

## Slide 17: CE05-2 Viewing Results

## Slide 18: CE05-2 Viewing Results

## Slide 19: CE05-2 Viewing Results

## Slide 20: CE05-2 Viewing Results

## Slide 21: CE05-2 Viewing Results