## Slide 1
Decoding Energy Assessment of VTM-6.0 (JVET-P0084)

## Slide 2: Motivation
Online video content: 1% of global greenhouse gas emissions [1]
  Civil aviation has a share of 4%
Mobile devices with limited battery lifetime
[1] M. Efoui-Hess, “Climate Crisis: The Unsustainable Use of Online Video. The Practical Case for Digital Sobriety”, Jul. 2019.

## Slide 3: Outline
Energy Measurement
Comparison of VTM and HM
Comparison of Different Implementations of HEVC
Conclusion

## Slide 4: Energy Measurement
Measurement of the decoding energy:
  1st Setup:
    Desktop PC
      Intel i7-8700 CPU
      OS: CentOS 7
    External power meter ZES ZIMMER, LMG95
  2nd Setup:
    Desktop PC
    Measurement with integrated power meter of Intel CPU: Running Average Power Limit (RAPL)
      Energy Counter is accessable via:
        /sys/class/powercap/intel-rapl/intel-rapl:0/energy_uj

## Slide 5: Energy Measurement
Time t [s]
Power Consumption P(t) [W]

## Slide 6: Comparison of VTM and HM
Software set:
  VVC:
    Encoding and decoding with VTM-6.0
    Configuration: intra, lowdelay, randomaccess
  HEVC:
    Encoding and decoding with HM-16.20
    Configuration: intra_main10, lowdelay_main10, randomaccess_main10
Sequence set:
  Based on JVET common test conditions for SDR sequences (JVET-N1010)
  Sequences of Class A1 and A2 are encoded with only 100 frames

## Slide 7: Comparison of VTM- and HM-decoder with LMG and RAPL
Measured decoding energy with RAPL is 1.87% higher than with LMG
Metric for decoding-energy-distortion-efficiency: Bjøntegaard-Delta-Decoding-Energy (BDDE) [2]
BDDE(HM RAPL, VTM RAPL) for this example: 68.6%
DaylightRoad2, lowdelay
+68.6%
[2] C. Herglotz, A. Heindel, and A. Kaup. Decoding-Energy-Rate-Distortion Optimization for Video Coding. IEEE Transactions on Circuits and Systems for Video Technology, Vol. 29(1), 2019.

## Slide 8: Comparison of VTM- and HM-decoder with RAPL
Evaluation of Bjøntegaard-Delta-Decoding-Energy (BDDE):
  Significantly higher decoding energy demand of VTM decoder
  BDDE-values depend on applied configuration
 | BDDE (RAPL)
Intra Lowdelay | +76.11%
 | +62.08%
Randomaccess | +77.85%

## Slide 9: Comparison of VTM- and HM-decoder with RAPL
Analysis for sequence CatRobot1:

## Slide 10: Comparison of VTM- and HM-decoder with RAPL
Analysis of each sequence and configuration:

## Slide 11: Comparison of Different Implementations of HEVC
Evaluation of BDDE compared to the HM-decoder on Intel-PC:
  FFmpeg has higher energy efficiency than HM-decoder
  BDDE is approximately -80%
 | BDDE Intel FFmpeg
Intra | -82.2%
Lowdelay | -78.1%
Randomaccess | -78.1%

## Slide 12: Comparison of Different Implementations of HEVC
Evaluation of the relative decoding energy demand compared to the HM-decoder on Intel-PC:
Chart: 
| HM | FFmpeg HEVC | VTM | FFmpeg VVC
Datenreihe 1 | 1 | 0.21 | 1.72 | 0.35
?

## Slide 13: Summary
VTM currently needs 70% more decoding energy than HM
A practical implementation (FFmpeg) saves 80% of decoding energy for HEVC
For implementations of VTM, a similar amount is expected

## Slide 14: Outlook
Precise knowledge about VTM decoding energy could finally be used to optimize the energy demand using the decoding-energy-rate-distortion optimization (DERDO) as suggested in [2]
[2] C. Herglotz, A. Heindel, and A. Kaup. Decoding-Energy-Rate-Distortion Optimization for Video Coding. IEEE Transactions on Circuits and Systems for Video Technology, Vol. 29(1), 2019.

## Slide 15
Thank you very much!

## Slide 16: Energy Measurement – Confidence Interval
m: number of measurements (min: 5)
σ : standard deviation of the measurement
: the critical t-value of the Student’s t-distribution
β: allowed deviation of the actual decoding energy value 0.02
α: probability that the actual decoding energy is within the allowed deviation
0.99

## Slide 17: Literature
[1] M. Efoui-Hess, “Climate Crisis: The Unsustainable Use of Online Video. The Practical Case for Digital Sobriety”, Jul. 2019.
[2] C. Herglotz, A. Heindel, and A. Kaup. Decoding-Energy-Rate-Distortion Optimization for Video Coding. IEEE Transactions on Circuits and Systems for Video Technology, Vol. 29(1), 2019.

## Slide 18: Energy Measurement
Measurement of the decoding energy on different devices
  3rd Setup:
    Raspberry Pi 3B+
      ARM Cortex A53, Quad-Core CPU with 1.4 GHz
      OS: Raspbian Stretch
    External power meter ZES ZIMMER, LMG95

## Slide 19: Comparison of Different Implementations of HEVC on Different Devices
Evaluation of BDDE compared to the HM-decoder on Intel-PC.
  FFmpeg has higher energy efficiency than HM-decoder on both devices
  BDDE for both devices is approximately -80%
  Similiar energy demand for ARM- and Intel-CPU
   Further implementations of VVC could also achieve similar results
 | BDDE Intel FFmpeg | BDDE Raspberry FFmpeg
Intra | -82.23% | -87.55%
Lowdelay | -78.11% | -78.09%
Randomaccess | -78.11% | -76.44%
Mean | -79.48% | -80.69%

## Slide 20: Comparison of VTM and HM
Bjøntegaard-Delta-Rate (BDR) is used as scale for rate-distortion-efficiency
BDR-value for this example: -29.11%
FoodMarket4, randomaccess

## Slide 21: Comparison of VTM- and HM-decoder with RAPL
Evaluation of Bjøntegaard-Delta-Rate (BDR) and Bjøntegaard-Delta-Decoding-Energy (BDDE)
  General observation: significantly higher decoding energy demand of VTM decoder
  BDR- and BDDE-values depend on applied configuration
 | BDR | BDDE (RAPL)
Intra | -23.70% | +76.11%
Lowdelay | -27.05% | +62.08%
Randomaccess | -31.91% | +77.85%