## Slide 1
JVET-P0196
CE6-related: Latency reduction for LFNST signalling
Jani Lainema

## Slide 2: JVET-P0196 / Latency reduction for LFNST signalling
LFNST index is currently signaled in the CU “footer”
  Depends on the last coefficient positions of all transform blocks in the CU
Creates latency in both encoder and decoder
  What one can do in luma depends on what chroma will do
  E.g. if luma LFNST block has only the “DC coefficient” surviving, need to encode chroma and have at least one “AC coefficient” to enable LFNST for luma
It is proposed to break luma’s dependency from chroma
  Moving LFNST index after last coefficient position syntax in a transform block
    Make the validity check based on last position of current transform block
  Moving MTS index to the same place for doing all transform mode signaling in a single place
Introduction

## Slide 3: JVET-P0196 / Latency reduction for LFNST signalling
Proposed signaling order
 | VTM-6.0 | Proposed
TU data | Transform skip flag | Transform skip flag
 | MTS index | 
 | Last coefficient position | Last coefficient position
 |  | If lastPos ok: LFNST index
 |  | MTS index
 | Coefficient values | Coefficient values
CU footer | If all lastPos in CU ok: LFNST index | 

## Slide 4: JVET-P0196 / Latency reduction for LFNST signalling
Granularity of enabling LFNST is kept unchanged
Proposal
 | VTM-6.0 | Proposed
Single tree | LFNST signalled for CU, applied to all components | LFNST signalled for luma, applied to all components
Dual-tree luma | LFNST signalled for luma CU, applied to luma | LFNST signalled for luma, applied to luma
Dual-tree chroma | LFNST signalled for chroma CU, applied to both chroma | LFNST signalled for first coded chroma, applied to both chroma

## Slide 5: JVET-P0196 / Latency reduction for LFNST signalling
Coding efficiency impact
 |  |  | AI |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.14 % | -0.10 % | 0.10 % | 100 % | 99 %
Class A2 | -0.08 % | -0.05 % | 0.05 % | 100 % | 99 %
Class B | -0.10 % | -0.11 % | -0.05 % | 100 % | 99 %
Class C | -0.09 % | -0.18 % | 0.05 % | 100 % | 101 %
Class E | -0.13 % | -0.35 % | -0.19 % | 100 % | 100 %
Overall | -0.11 % | -0.15 % | -0.01 % | 100 % | 100 %
Class D | -0.10 % | 0.16 % | 0.00 % | 100 % | 101 %
Class F | -0.06 % | -0.09 % | -0.12 % | 99 % | 100 %
 |  |  | RA |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.07 % | 0.12 % | -0.13 % | 100 % | 100 %
Class A2 | -0.03 % | 0.12 % | 0.13 % | 100 % | 100 %
Class B | -0.08 % | 0.13 % | 0.02 % | 101 % | 99 %
Class C | -0.08 % | -0.16 % | -0.05 % | 99 % | 99 %
Class E |  |  |  |  | 
Overall | -0.07 % | 0.05 % | 0.00 % | 100 % | 100 %
Class D | -0.15 % | -0.25 % | 0.04 % | 99 % | 98 %
Class F | -0.05 % | -0.37 % | 0.07 % | 100 % | 100 %

## Slide 6: JVET-P0196 / Latency reduction for LFNST signalling
Coding efficiency impact
 |  |  | LD-B |  | 
 | Y | U | V | EncT | DecT
Class B | 0.00 % | 0.17 % | -0.05 % | 101 % | 101 %
Class C | -0.04 % | -0.03 % | -0.13 % | 100 % | 100 %
Class E | -0.02 % | 0.60 % | 0.13 % | 100 % | 100 %
Overall | -0.02 % | 0.21 % | -0.04 % | 100 % | 100 %
Class D | 0.00 % | -0.04 % | 0.33 % | 100 % | 99 %
Class F | 0.03 % | -0.25 % | 0.10 % | 100 % | 100 %

## Slide 7: JVET-P0196 / Latency reduction for LFNST signalling
Proposed to break the chroma to luma dependency in LFNST signaling
  Latency improvement
  Less inter-component dependencies
  Both LFNST and MTS indexes signaled in the same location
  Positive impact on coding efficiency
    AI: -0.11 %, RA: -0.07 %
Summary