## Slide 1: MIP Simplification
JVET-P0289
Sharp Corporation
Yukinobu Yasugi
Tomohiro Ikai

## Slide 2: MIP process overview
Matrix-based intra prediction (MIP)
  Generates intermediate prediction predMip[][]
    input: p[i] (inSize x 1)
    output: predMip[][] (predW x predH)
    matrix; mWeight[][] (predC x predC x inSize)
  Upscales the predMip[][] to predSamples
    input: predMip[][] (predW x predH)
    output mWeight[][] (nTbW x nTbH)
refSamples(p)
inSize
predMip predW * predH
predSamples nTbW * nTbH
upscaling
matrix calculation
mWeight (predC * predC) * inSize

## Slide 3: Problem statement
For 4x16 or 16x4 blocks
  predMip is PredW x PrecH (4x8 and 8x4)
  mWeight size is for 8x8
  => matrix operation becomes complicated
    needs incH and incW decimation process
Table 8-4 in WD6
incW = ( predC > mipW ) ? 2 : 1 (8‑65)
incH = ( predC > mipH ) ? 2 : 1 (8‑66)
predMip[ x ][ y ] = ( ( ( ) + oW ) >> sW ) + pTemp[ 0 ] (8‑67)
MipSizeId | numModes | boundarySize | predW | predH | predC
0 | 35 | 2 | 4 | 4 | 4
1 | 19 | 4 | 4 | 4 | 4
2 | 11 | 4 | Min(nTbW, 8) | Min(nTbH, 8) | 8
predMip size
mWeight size
Here predMip size and mWeight size can be different

## Slide 4: Proposed solution
Modify the SizeId classification
Original
Proposed
 | w=4 | 8 | 16 | 32 | 64
h=4 | 0 | 1 | 2 | - | -
8 | 1 | 1 | 2 | 2 | -
16 | 2 | 2 | 2 | 2 | 2
32 | - | 2 | 2 | 2 | 2
64 | - | - | 2 | 2 | 2
 | w=4 | 8 | 16 | 32 | 64
h=4 | 0 | 1 | 1 | - | -
8 | 1 | 1 | 2 | 2 | -
16 | 1 | 2 | 2 | 2 | 2
32 | - | 2 | 2 | 2 | 2
64 | - | - | 2 | 2 | 2
Mip SizeId | num Modes | boundary Size | predW | predH | predC
0 | 35 | 2 | 4 | 4 | 4
1 | 19 | 4 | 4 | 4 | 4
2 | 11 | 4 | Min ( nTbW, 8 ) | Min ( nTbH, 8 ) | 8
Mip SizeId | num Modes | boundary Size | predW= predH= predC
0 | 35 | 2 | 4
1 | 19 | 4 | 4
2 | 11 | 4 | 8

## Slide 5: Simplified scaling process
The variables mipW and mipH are derived as follows:
mipW = isTransposed ? predH : predW (8‑57)
mipH = isTransposed ? predW : predH (8‑58)
The matrix-based intra prediction samples predMip[ x ][ y ], with x = 0..mipW − 1, y = 0..mipH − 1 are derived as follows:
oW = ( 1 << ( sW − 1 ) ) − fO * () (8‑64)
incW = ( predC > mipW ) ? 2 : 1 (8‑65)
incH = ( predC > mipH ) ? 2 : 1 (8‑66)
predMip[ x ][ y ] = ( ( ( ) + oW ) >> sW ) + pTemp[ 0 ] (8‑67)
The matrix-based intra prediction samples predMip[ x ][ y ], with x = 0..predC − 1, y = 0..predC − 1 are derived as follows:
oW = ( 1 << ( sW − 1 ) ) − fO * () (8‑64)
predMip[ x ][ y ] = ( ( ( ) + oW ) >> sW ) + pTemp[ 0 ] (8‑67)
Original
Proposed

## Slide 6: Complexity reduction
Proposed method reduces number of multiplications.
 | Original |  |  | Proposed |  | 
Size(WxH) | SizeId | #mul. | #mul./sample | SizeId | #mul. | #mul./sample
4x4 | 0 | 64 | 4 | 0 | 64 | 4
4x8/8x4 | 1 | 128 | 4 | 1 | 128 | 4
8x8 | 1 | 128 | 2 | 1 | 128 | 2
4x16/16x4 | 2 | 448/2 | 3.5 | 1 | 128 | 2
8x16/16x8 | 2 | 448 | 3.5 | 2 | 448 | 3.5
W*H=256 | 2 | 448 | 1.75 | 2 | 448 | 1.75
W*H=512 | 2 | 448 | 0.875 | 2 | 448 | 0.875
32x32 | 2 | 448 | 0.4375 | 2 | 448 | 0.4375
16x64/64x16 | 2 | 448x2 | 0.875 | 2 | 448x2 | 0.875
32x64/64x32 | 2 | 448x2 | 0.4375 | 2 | 448x2 | 0.4375
64x64 | 2 | 448x4 | 0.4375 | 2 | 448x4 | 0.4375

## Slide 7: Experimental results
Anchor: VTM-6.0 (CTC)
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 (sharp) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.01% | -0.01% | 100% | 100%
Class A2 | 0.02% | 0.02% | 0.01% | 100% | 100%
Class B | 0.01% | -0.01% | 0.00% | 100% | 100%
Class C | 0.02% | -0.05% | 0.06% | 101% | 100%
Class E | 0.01% | -0.02% | 0.06% | 101% | 100%
Overall | 0.01% | -0.01% | 0.02% | 100% | 100%
Class D | 0.02% | 0.02% | 0.06% | 100% | 100%
Class F | 0.01% | -0.01% | -0.11% | 100% | 100%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 (sharp) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.03% | 0.16% | 100% | 100%
Class A2 | 0.03% | 0.06% | 0.10% | 100% | 100%
Class B | 0.00% | 0.05% | 0.05% | 100% | 100%
Class C | 0.03% | 0.00% | -0.09% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.01% | 0.04% | 0.05% | 100% | 100%
Class D | -0.07% | -0.23% | 0.19% | 100% | 100%
Class F | 0.01% | -0.02% | -0.02% | 100% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 (sharp) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.13% | 0.15% | 100% | 100%
Class C | 0.03% | 0.01% | -0.05% | 100% | 99%
Class E | -0.19% | 1.01% | 0.70% | 100% | 100%
Overall | -0.04% | 0.31% | 0.22% | 100% | 100%
Class D | -0.03% | 0.17% | -0.32% | 100% | 100%
Class F | -0.08% | -0.34% | 0.66% | 100% | 100%