## Slide 1: JVET-P0331 Non-CE5: CC-ALF design simplification
Jonathan Taquet Patrice Onno Christophe Gisquet Guillaume Laroche

## Slide 2: Proposed changes in JVET-P0331 (1/2)
Proposal 1: Signal CC-ALF at the CTB level.
  Removal of the activation map signalling CC-ALF at subblock level
Results over VTM6_CE5-2.1

## Slide 3: Proposed changes in JVET-P0331 (2/2)
Proposal 2: Remove of the temporal mechanism to reuse previous filter for the CC-ALF
Results over VTM6_CE5-2.1

## Slide 4: Proposed changes in JVET-P0331 (1/3)
Proposal 3: Combination of both
Results over VTM6_CE5-2.1

## Slide 5: Proposed syntax changes in JVET-P0331
Syntax removal:
  And the associated semantics
slice_header( ) { | Descriptor
… | 
if( sps_cross_component_alf_enabled_flag ) { | 
slice_cross_component_alf_cb_enabled_flag | u(1)
if( slice_cross_component_alf_cb_enabled_flag ) { | 
slice_cross_component_alf_cb_reuse_temporal_layer_filter | u(1)
if (!slice_cross_component_alf_cb_reuse_temporal_layer_filter) | 
slice_cross_component_alf_cb_aps_id | u(5)
slice_cross_component_alf_cb_log2_control_size_minus4 | ue(v)
} | 
slice_cross_component_alf_cr_enabled_flag | u(1)
if( slice_cross_component_alf_cr_enabled_flag ) { | 
slice_cross_component_alf_ct_reuse_temporal_layer_filter | u(1)
if (!slice_cross_component_alf_cr_reuse_temporal_layer_filter) | 
slice_cross_component_alf_cr_aps_id | u(5)
slice_cross_component_alf_cr_log2_control_size_minus4 | ue(v)
} | 
} | 
… | 
} | 

## Slide 6: Conclusion
The proposed changes simplifies the CC-ALF while preserving the good coding gains of CC-ALF
  Removal of the activation map: CC-ALF signaling at CTB level
  Removal of the temporal prediction mechanism.
We suggest to consider these simplifications in the next VVC draft for the CC-ALF design.
Thanks to Sharp for cross-checking

## Slide 7: Thank you for your attention.