## Slide 1: JVET-P0371 Signalling of corrective values for chroma residual scaling (CRS)

## Slide 2: Derivation of CRS values in VVC draft6
Signalling of up to 16 Fwd Luma Mapping slope values  lmcsCW[ i ]
CRS values inferred as the inverse of Fwd Luma Mapping slopes values
lmcs_data () { | Descriptor
… | 
lmcs_delta_cw_prec_minus1 | ue(v)
for ( i = lmcs_min_bin_idx; i <= LmcsMaxBinIdx; i++ ) { | 
lmcs_delta_abs_cw[ i ] | u(v)
if ( lmcs_delta_abs_cw[ i ] ) > 0 ) | 
lmcs_delta_sign_cw_flag[ i ] | u(1)
} | 
} | 

## Slide 3: Comments
No control flexibility on ChromaScaleCoeff[ i ]
  More flexibility can be beneficial for finer encoder control
CRS / QP controls are in different dimensions
  scaling factors are derived based on luma brightness
  QP is spatially controlled
Granularity of scaling different using delta QP or CRS factors
  delta QPs  ( 2^(1/6) – 1 )  0.122
  CRS factors  1/64 (10-bit signal)  0.016 (8 times finer)

## Slide 4: Proposal: signal corrective CRS values
Signalling of up to 16 CRS corrective values  lmcsCW[ i ]
CRS values inferred as the inverse of Fwd Luma Mapping slopes values
lmcs_data () { | Descriptor
… | 
lmcs_delta_crs_prec_minus1 | ue(v)
for ( i = lmcs_min_bin_idx; i <= LmcsMaxBinIdx; i++ ) { | 
lmcs_delta_abs_crs[ i ] | u(v)
if ( lmcs_delta_abs_crs[ i ] ) > 0 ) | 
lmcs_delta_sign_crs_flag[ i ] | u(1)
} | 
} | 

## Slide 5: Experiments
Simple algorithm: add an offset (CRS_offset) to the luma slope values
  lmcsCW[ i ] > 64  lmcsCW[ i ] = lmcsCW[ i ] + CRS_offset
  Otherwise  lmcsCW[ i ] = lmcsCW[ i ]  CRS_offset
VTM6.0 as anchor (LMCS on) – RA
 |  | AI |  |  |  | RA | 
CRS_offset | PsnrY | PsnrU | PsnrV |  | PsnrY | PsnrU | PsnrV
CRS_offset = 3 | 0.09% | -0.46% | -0.43% |  | 0.10% | -1.09% | -1.04%
CRS_offset = 1 | 0.03% | -0.16% | -0.14% |  | 0.03% | -0.36% | -0.34%
CRS_offset = -1 | -0.01% | 0.26% | 0.26% |  | -0.03% | 0.46% | 0.42%
CRS_offset = -2 | -0.03% | 0.43% | 0.45% |  | -0.06% | 0.84% | 0.65%
CRS_offset = -3 | -0.05% | 0.65% | 0.69% |  | -0.09% | 1.28% | 1.09%
chr QP set to 1(1) | -2.70% | 26.45% | 25.69% |  | -2.08% | 23.93% | 23.54%
chr QP set to -1(-1) | 3.68% | -19.99% | -19.51% |  |  |  | 

## Slide 6: Experiments – tool-off test (RA)
VTM6.0
Ref: “LMCS on” Test: “LMCS off” (AHG13)
 | Y | U | V
Class A1 | 1.06% | -2.71% | -2.09%
Class A2 | 2.29% | -4.02% | -3.99%
Class B | 1.75% | 0.84% | 0.69%
Class C | 1.41% | -0.89% | -1.62%
Class E |  |  | 
Overall | 1.63% | -1.30% | -1.42%
Class D | 0.96% | -0.64% | -1.05%
Class F | 1.29% | 0.17% | -0.07%
VTM6.0 with CRS correction
Ref: “LMCS on CRS_offset=3” Test: “LMCS off”
 | Y | U | V
Class A1 | 0.97% | -1.29% | -0.83%
Class A2 | 2.18% | -3.25% | -3.21%
Class B | 1.69% | 1.39% | 1.25%
Class C | 1.25% | 0.71% | -0.14%
Class E |  |  | 
Overall | 1.53% | -0.22% | -0.39%
Class D | 0.87% | 0.37% | -0.16%
Class F | 1.06% | 1.07% | 0.80%

## Slide 7: Conclusion
Propose signalling of a corrective CRS table
Offers more flexible encoder scaling control
  QP  spatial control
   scaling granularity ( 2^(1/6) – 1 )  0.122
  CRS  control based on luma (brightness)
   scaling granularity 1/64 (10-bit)  0.016 (8x finer)

## Slide 8: Additional results HDR PQ

## Slide 9: Experiments on HDR PQ
An encoder tuning algorithm taking into account the chroma QP mapping table is used
The algorithm is controled by a QP offset value (offset) added to the slice QP
offset | DE100 | L100 | wPSNRY | wPSNRU | wPSNRV
0 | 1.26% | -0.19% | -0.19% | 3.34% | 3.22%
1 | 0.98% | -0.09% | -0.09% | 2.11% | 1.57%
2 | 0.10% | -0.10% | -0.10% | 0.19% | -2.51%
3 | -0.75% | 0.05% | 0.05% | -3.09% | -7.67%
4 | -1.43% | 0.09% | 0.09% | -5.11% | -9.27%
chr QP set to 1 |  |  |  |  |