## Slide 1: JVET-P0371 Signalling of corrective values for chroma residual scaling (CRS)

## Slide 2: Derivation of CRS values in VVC draft6
Signalling of up to 16 Fwd Luma Mapping slope values  lmcsCW[ i ]
CRS values inferred as the inverse of Fwd Luma Mapping slopes values
lmcs_data () { | Descriptor
… | 
lmcs_delta_cw_prec_minus1 | ue(v)
for ( i = lmcs_min_bin_idx; i <= LmcsMaxBinIdx; i++ ) { | 
lmcs_delta_abs_cw[ i ] | u(v)
if ( lmcs_delta_abs_cw[ i ] ) > 0 ) | 
lmcs_delta_sign_cw_flag[ i ] | u(1)
} | 
} | 

## Slide 3: Comments
No control flexibility on ChromaScaleCoeff[ i ]
  More flexibility can be beneficial for finer encoder control
CRS / QP controls are in different dimensions
  Chroma res. scaling values are derived based on luma brightness
  QP is spatially controlled
Granularity of scaling different using delta QP or CRS factors
  delta QPs  ( 2^(1/6) – 1 )  0.122
  CRS factors  1/64 (10-bit signal)  0.016 (8 times finer)
SDR CTCs - RA | BDR-Y | BDR-U | BDR-V
VTM6.0 LMCS tool-off (AHG13) | 1.63% | -1.30% | -1.42%

## Slide 4: Proposal: signal corrective CRS values
Signalling of up to 16 CRS corrective values  lmcsDeltaCRS[ i ]
lmcs_data () { | Descriptor
lmcs_min_bin_idx | ue(v)
lmcs_delta_max_bin_idx | ue(v)
lmcs_delta_cw_prec_minus1 | ue(v)
for ( i = lmcs_min_bin_idx; i <= LmcsMaxBinIdx; i++ ) { | 
lmcs_delta_abs_cw[ i ] | u(v)
if ( lmcs_delta_abs_cw[ i ] ) > 0 ) | 
lmcs_delta_sign_cw_flag[ i ] | u(1)
} | 
lmcs_delta_crs_prec_minus1 | ue(v)
for ( i = lmcs_min_bin_idx; i <= LmcsMaxBinIdx; i++ ) { | 
lmcs_delta_abs_crs[ i ] | u(v)
if ( lmcs_delta_abs_crs[ i ] ) > 0 ) | 
lmcs_delta_sign_crs_flag[ i ] | u(1)
} | 
} | 

## Slide 5: Simpler variant: signal 1 corrective CRS value
Signalling 1 CRS corrective value  lmcsDeltaCRS
lmcs_data () { | Descriptor
lmcs_min_bin_idx | ue(v)
lmcs_delta_max_bin_idx | ue(v)
lmcs_delta_cw_prec_minus1 | ue(v)
for ( i = lmcs_min_bin_idx; i <= LmcsMaxBinIdx; i++ ) { | 
lmcs_delta_abs_cw[ i ] | u(v)
if ( lmcs_delta_abs_cw[ i ] ) > 0 ) | 
lmcs_delta_sign_cw_flag[ i ] | u(1)
} | 
lmcs_delta_crs_prec_minus1 | ue(v)
lmcs_delta_abs_crs | u(v)
if ( lmcs_delta_abs_crs ) > 0 ) | 
lmcs_delta_sign_crs_flag | u(1)
} | 

## Slide 6: Proposal: CRS table derivation
VVC draft 6
  It is a requirement of bitstream conformance that lmcsCW[ i ] is in the range of (OrgCW>>3) to (OrgCW<<3 − 1), inclusive.
Proposal
  It is a requirement of bitstream conformance that ( lmcsCW[ i ] + lmcsDeltaCrs ) is in the range of (OrgCW>>3) to (OrgCW<<3 − 1), inclusive.

## Slide 7: Experiments
Simple algorithm: add an offset (CRS_offset) to the luma slope values
  lmcsCW[ i ] > 64  lmcsCW[ i ] = lmcsCW[ i ] + CRS_offset
  Otherwise  lmcsCW[ i ] = lmcsCW[ i ]  CRS_offset
VTM6.0 as anchor (LMCS on) – AI / RA
 |  | AI |  |  |  | RA | 
CRS_offset | PsnrY | PsnrU | PsnrV |  | PsnrY | PsnrU | PsnrV
CRS_offset = 3 | 0.09% | -0.46% | -0.43% |  | 0.10% | -1.09% | -1.04%
CRS_offset = 1 | 0.03% | -0.16% | -0.14% |  | 0.03% | -0.36% | -0.34%
CRS_offset = -1 | -0.01% | 0.26% | 0.26% |  | -0.03% | 0.46% | 0.42%
CRS_offset = -2 | -0.03% | 0.43% | 0.45% |  | -0.06% | 0.84% | 0.65%
CRS_offset = -3 | -0.05% | 0.65% | 0.69% |  | -0.09% | 1.28% | 1.09%
chr QP set to 1(1) | -2.70% | 26.45% | 25.69% |  | -2.08% | 23.93% | 23.54%
chr QP set to -1(-1) | 3.68% | -19.99% | -19.51% |  | 2.69% | -17.75% | -17.50%
CbQpOffset/CrQpOffset,
CbQpOffsetDualTree/CrQpOffsetDualTree
set to +1/-1

## Slide 8: Experiments – tool-off test (RA)
VTM6.0
Ref: “LMCS on” Test: “LMCS off” (AHG13)
 | Y | U | V
Class A1 | 1.06% | -2.71% | -2.09%
Class A2 | 2.29% | -4.02% | -3.99%
Class B | 1.75% | 0.84% | 0.69%
Class C | 1.41% | -0.89% | -1.62%
Class E |  |  | 
Overall | 1.63% | -1.30% | -1.42%
Class D | 0.96% | -0.64% | -1.05%
Class F | 1.29% | 0.17% | -0.07%
VTM6.0 with CRS correction
Ref: “LMCS on CRS_offset=3” Test: “LMCS off”
 | Y | U | V
Class A1 | 0.97% | -1.29% | -0.83%
Class A2 | 2.17% | -3.05% | -2.99%
Class B | 1.69% | 1.39% | 1.25%
Class C | 1.25% | 0.71% | -0.14%
Class E |  |  | 
Overall | 1.53% | -0.22% | -0.39%
Class D | 0.87% | 0.37% | -0.16%
Class F | 1.06% | 1.07% | 0.80%

## Slide 9: Conclusion
Propose signalling of a corrective CRS table
Gives more flexible encoder scaling control, with finer granularity, and in an orthogonal dimension to QP control (brightness vs spatial)
  QP  spatial control
   scaling granularity ( 2^(1/6) – 1 )  0.122
  CRS  control based on luma (brightness)
   scaling granularity 1/64 (10-bit)  0.016 (8x finer)

## Slide 10: Additional results HDR PQ

## Slide 11: Experiments on HDR PQ
An encoder tuning algorithm taking into account the chroma QP mapping table is used
  The algorithm is controled by a QP offset value (offset) added to the slice QP
VTM6.0 as anchor (LMCS off, LQP on) – Test LMCS on, LQP off – RA
offset | DE100 | L100 | wPSNRY | wPSNRU | wPSNRV
0 | 1.26% | -0.19% | -0.19% | 3.34% | 3.22%
1 | 0.98% | -0.09% | -0.09% | 2.11% | 1.57%
2 | 0.10% | -0.10% | -0.10% | 0.19% | -2.51%
3 | -0.75% | 0.05% | 0.05% | -3.09% | -7.67%
4 | -1.43% | 0.09% | 0.09% | -5.11% | -9.27%
chr QP set to 1(1) | 26.65% | -1.97% | -2.06% | 75.17% | 206.47%