## Slide 1: Non-CE8: IBC chroma mode with dual-tree (JVET-P0456)
X. Xu, X. Li, S. Liu (Tencent)
2019/10

## Slide 2: Summary
Currently in VVC CD text/VTM-6.0, chroma IBC mode under dual-tree is disabled:
  Due to the use of subblock derivation
  About 1.8% TGM AI loss was observed
In this contribution, a block level IBC chroma mode under dual-tree is proposed, where only 1 single block vector is used for the entire chroma CU
Simulation results show 1.21% TGM AI gain can be achieved, which is roughly 2/3 of the benefit from uisng subblock based chroma IBC mode

## Slide 3: Proposed methods
For a chroma CU, a block level flag is signaled
Encoder constraints for the proposed chroma IBC mode under dual-tree
  The samples in the collocated luma area shall be all coded in IBC mode and with the same luma BV
For chroma CU, a flag is used to signal if IBC mode is chosen
  if coded in IBC mode, the top-left corner’s collocated luma BV is used for BV derivation
  Only when the encoder constraint is met can the chroma CU choose IBC mode

## Slide 4: Results
The proposed method is compared with two anchors: VTM-6.0 (no chroma IBC under dual-tree) and the subblock based chroma IBC under dual-tree

## Slide 5: Conclusion
In this contribution, chroma IBC mode under dual-tree condition is proposed as a block level mode
Coding efficiency improvement of 1.21%/0.53%/0.00% for TGM class is observed
  About 2/3 of the benefit from subblock based chroma IBC mode is back
  Assertion that no decoder complexity is added
Thanks Alibaba for performing the crosscheck!