## Slide 1: CE4 Related Viewing Test Procedure and Results
Mathias Wien
Conducted 2019-10-08

## Slide 2: Test Setup
Procedure as tests at last meeting [JVET-O1118]
LG OLED 55” display used, three test subjects per session at 1.6 × screen height distance
A-B-A-B presentation, assessment:
  “A was much better than B”
  “A was better than B”
  “B was better than A”
  “B was much better than A”.
Test cell design
  “A” – Video A – “B” – Video B – “A” – Video A – “B” – Video B – “Vote N”
  “A” / “B” presentation for 0.5sec
  Voting for 5sec

## Slide 3: Test Design
Placement of anchor and proposal as “A” and “B” randomized over test cells
Fixed order of sequences, looped over available test cells
Mix of (few) sequences which have resolutions 480p, 720p, 1080p
  Decision to present all sequences up-scaled to UHD screen resolution using nearest neighbor interpolation
  Viewing performed at 3.2xh distance from screen

## Slide 4: Test Evaluation
Viewing votes mapping
  +3 : “Proposal much better than anchor”
  +1 : “Proposal better than anchor”
  -1 : “Anchor better than proposal”
  -3 : “Anchor much better than proposal”
Calculation of Mean Opinion Score (MOS) on this scale
Calculation of 95% confidence intervals based on MOS and standard deviation

## Slide 5: Sequences under test for both sessions
Sequence name |  | Resolution | Fps | Frames | Mode | QP
Cactus | S01 | 1920x1080 | 50fps | 500 | RA | 32, 37
ParkScene | S02 | 1920x1080 | 24fps | 240 | RA | 32, 37
BQMall | S03 | 832x480 | 60fps | 600 | LDB | 32, 37
RaceHorsesC | S04 | 832x480 | 30fps | 300 | RA | 32, 37
Johnny | S05 | 1280x720 | 60fps | 600 | LDB | 32, 37

## Slide 6: Session Setup
Tests conducted Tue. 2019-10-08 15:00h
  Session 1: JVET-P0884/JVET-P0885
  Session 2: JVET-P0071
Sequences selected by proponents
6 groups of three experts = 18 test subjects
Presentation of 10 test cells per session
  Less than 9 min viewing time each
Interleaving of two groups each
  One testing, one resting / entering results

## Slide 7: Session 1: JVET-P0884/P0885

## Slide 8: Session 1: JVET-P0884/P0885

## Slide 9: Session 2: JVET-P0071

## Slide 10: Session 2: JVET-P0071

## Slide 11: Closing
Thanks to all volunteers who participated in the tests
Thanks to Andrew Segall for providing the test PC, video player, and support
Thanks to Kenneth Andersson and Andrey Norkin for review and help
Thanks to EBU for providing OLED display
Thanks to Vittorio Baroncini for his guidance