## Slide 1
Analysis of the Energy-Time Relationship for VVC and HEVC Software Video Decoders (JVET-Q0051)

## Slide 2: Motivation
Online video content: 1% of global greenhouse gas emissions [1]
  Civil aviation has a share of 4%
Mobile devices with limited battery lifetime
[1] M. Efoui-Hess, “Climate Crisis: The Unsustainable Use of Online Video. The Practical Case for Digital Sobriety”, Jul. 2019.

## Slide 3: Motivation
Is there a linear relationship between the decoding time and energy demand?

## Slide 4: Outline
Motivation
Energy Measurement & Test Set
Decoding Time and Energy Dependency
Conclusion

## Slide 5: Energy Measurement & Test Set
Measurement of the decoding energy:
  Desktop PC
    Intel i7-8700 CPU
    OS: CentOS 7
  Integrated power meter of Intel CPU: Running Average Power Limit (RAPL)
  Time measurement of real elapsed time
Test Set:
  Based on JVET common test conditions for SDR sequences (JVET-N1010) for VVC and HEVC

## Slide 6: Decoding Time and Energy Dependency
Modeling of the decoding energy demand by:
Estimation accuracy is described by:
Training of and with least-square curve fitting

## Slide 7: Decoding Time and Energy Dependency
Modeling for different software video decoders:
  HEVC:
    HM-16.20
  VVC:
    VTM-7.0
Evaluation:
 | P | 
HM-16.20 | 21.26 W | 1.41%
VTM-7.0 | 22.09 W | 1.05%
 | P | 
HM-16.20 | 21.26 W | 1.41%
VTM-7.0 | 22.09 W | 1.05%

## Slide 8: Decoding Time and Energy Dependency
Modeling for different software video decoders:
  FFmpeg:
    51.02%
    Inaccurate estimation of decoding energy with decoding time
    Alternative approach is necessary for the modeling of the decoding energy demand, e.g. bit stream feature-based models

## Slide 9: Summary
Sufficiently high accuracy for reference software video decoders such as VTM or HM (
For practical implementations such as FFmpeg, the modeling is highly inaccurate ()

## Slide 10
Thank you!

## Slide 11: Literature
[1] M. Efoui-Hess, “Climate Crisis: The Unsustainable Use of Online Video. The Practical Case for Digital Sobriety”, Jul. 2019.