## Slide 1
JVET-Q0055
On MTS index signalling
Jani Lainema

## Slide 2: JVET-Q0055: On MTS index signalling
MTS transform coefficients are allowed only inside the lowest frequency 16x16 area of a transform block
Signalling of the mts_idx is conditioned to the last coefficient position
  If last_pos is outside 16x16 area mts_idx is not signaled
  Even if last_pos is inside the 16x16, diagonal scan can still go outside that area
Currently handled as a bitstream restriction
  Reflector discussions indicated a syntax based approach is preferable
Proposal:
  Check on coefficient subblock level if there is a subblock violating the MTS condition and if so, don’t signal mts_idx
Introduction

## Slide 3: JVET-Q0055
Spec text
residual_coding( x0, y0, log2TbWidth, log2TbHeight, cIdx ) {
…
if( ( LastSignificantCoeffX > 15 ¦ ¦ LastSignificantCoeffY > 15 ) && cIdx = = 0 )
MtsZeroOutSigCoeffFlag = 0
QState = 0
for( i = lastSubBlock; i >= 0; i− − ) {
…
if( i < lastSubBlock && i > 0 ) {
coded_sub_block_flag[ xS ][ yS ]
inferSbDcSigCoeffFlag = 1
}
if( coded_sub_block_flag[ xS ][ yS ] && ( xS > 3 ¦ ¦ yS > 3 ) && cIdx = = 0 ) {
MtsZeroOutSigCoeffFlag = 0
}
…
mts_idx specifies which transform kernels are applied along the horizontal and vertical direction of the associated luma transform blocks in the current coding unit.
When mts_idx is not present, it is inferred to be equal to 0.
It is a requirement of bitstream conformance that mts_idx shall be equal to 0 if in the current coding unit at least one coded_sub_block_flag[ xS ][ yS ] in the residual_coding( x0, y0, log2TbWidth, log2TbHeight, cIdx ) syntax structure is not equal to 0 for cIdx equal to 0 and xS or yS greater than 3.

## Slide 4: JVET-Q0055: On MTS index signalling
Impact on coding efficiency
 |  |  | All Intra |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00 % | -0.03 % | 0.01 % | 99 % | 100 %
Class A2 | -0.01 % | -0.01 % | 0.00 % | 99 % | 100 %
Class B | 0.00 % | 0.01 % | -0.03 % | 99 % | 100 %
Class C | 0.00 % | 0.00 % | 0.00 % | 100 % | 100 %
Class E | 0.00 % | 0.00 % | -0.03 % | 100 % | 101 %
Overall | 0.00 % | 0.00 % | -0.01 % | 100 % | 100 %
Class D | 0.00 % | 0.03 % | 0.00 % | 100 % | 101 %
Class F | 0.00 % | 0.01 % | 0.00 % | 100 % | 103 %
 |  |  | RA |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01 % | -0.07 % | 0.00 % | 100 % | 99 %
Class A2 | -0.05 % | 0.02 % | -0.02 % | 100 % | 99 %
Class B | 0.02 % | 0.02 % | 0.06 % | 100 % | 98 %
Class C | 0.00 % | -0.04 % | 0.03 % | 100 % | 98 %
Class E |  |  |  |  | 
Overall | 0.00 % | -0.01 % | 0.02 % | 100 % | 98 %
Class D | 0.00 % | 0.01 % | -0.03 % | 100 % | 100 %
Class F | 0.00 % | -0.02 % | -0.02 % | 100 % | 99 %
 |  |  | LD-B |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00 % | -0.15 % | 0.01 % | 101 % | 101 %
Class C | 0.01 % | -0.12 % | -0.05 % | 101 % | 101 %
Class E | 0.01 % | -0.01 % | -0.07 % | 101 % | 100 %
Overall | 0.00 % | -0.10 % | -0.03 % | 101 % | 101 %
Class D | 0.01 % | -0.05 % | 0.04 % | 101 % | 100 %
Class F | -0.01 % | -0.03 % | 0.01 % | 101 % | 101 %