## Slide 1
JVET-Q0123
Ce4-related: Modifications for GEO
Li Jingya, Lim Chong Soon

## Slide 2
Introduction
Geometrical partitioning (GEO)
JVET-J1030/JVET-K0146 which applied to both AMVP and merge mode.
JVET-O0489, GEO was proposed for merge mode with 140 supported partitioning modes and 19 supported block size (8x8 to 128x128).
JVET-P0884/0885, efforts were made to remove multiplication of weight mask calculation and number of modes was reduced to 82.
JVET-Q0059, number of modes is further reduced to 64.
 | Total # of cases | # modes per block size | # of supported block sizes
TPM | 50 | 2 | 25
Wedge mode (in other standard) | 144 | 16 | 8
GEO (JVET-O0489, Gothenburg) | 2,660 | 140 | 19
GEO (JVET-P0884/JVET-Q0079, CE4 common base, Geneva) | 1,558 | 82 | 19
GEO (JVET-Q0059, CE4-1, Brussels) | 1,216 | 64 | 19

## Slide 3
Proposal
Remove 64x8 and 8x64 sized GEO block
It is proposed not to allow 64x8 and 8x64 sized coding block for GEO.

## Slide 4
Simulation results
Anchor: CE4-common base
Test: disallowing 64x8 and 8x64 (encoder setting is changed same as CE4-2.1, implemented over CE4 common base).
 | Random Access Main 10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | -0.01% | -0.05% | -0.06% | 104% | 100%
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | -0.01% | -0.09% | -0.15% | 104% | 101%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | 0.03% | 0.04% | 105% | 101%
Class C | 0.03% | -0.04% | -0.16% | 105% | 99%
Class E | 0.11% | -0.14% | 0.02% | 102% | 99%
Overall | 0.03% | -0.04% | -0.03% | 104% | 100%
Class D | -0.10% | -0.29% | -0.63% | 106% | 102%
Class F | 0.00% | -0.25% | -0.07% | 102% | 99%
*This aspect can also be combined with CE4-2.1 so that the complexity can be reduced more efficiently.

## Slide 5
Proposal
Scalable geo by signaling number of valid modes in SPS
Encoder is allowed to choose either 16 valid geo modes or 64 valid geo modes.
A flag is signaled in SPS level to switch between 16 and 64 modes.
If 16 mode is selected, only the first 16 modes of GEO mode table are valid.
If 64 mode is selected, all 64 modes of GEO mode table are valid.
(This affects coding of merge_geo_parititon_idx with cmax set to 16 and 64 respectively)
 | Total # of cases | # modes per block size | # of supported block sizes
TPM | 50 | 2 | 25
GEO (JVET-Q0059, CE4-1) | 1,216 | 64 | 19
Proposal (64 mode) | Same as above | Same as above | Same as above
Proposal (16 mode) | 304 | 16 | 19

## Slide 6
Simulation results
Anchor: VTM7.0
Test: Left - scalable coding with 16 valid modes; Right – scalable coding with 64 valid modes. (implemented over CE4-1, GEO mode table is reordered according to statistics)
 | Random Access Main 10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | -0.09% | 0.00% | 102% | 101%
Class A2 | -0.06% | 0.04% | 0.05% | 101% | 100%
Class B | -0.06% | 0.03% | -0.04% | 101% | 101%
Class C | -0.21% | -0.34% | -0.28% | 101% | 100%
Class E |  |  |  |  | 
Overall | -0.09% | -0.09% | -0.08% | 101% | 100%
Class D | -0.16% | -0.32% | -0.25% | 101% | 100%
Class F | -0.22% | -0.21% | -0.19% | 100% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.16% | -0.28% | -0.17% | 101% | 100%
Class C | -0.25% | -0.42% | -0.09% | 101% | 99%
Class E | -0.52% | 0.22% | -0.38% | 99% | 99%
Overall | -0.28% | -0.20% | -0.20% | 100% | 99%
Class D | -0.33% | 0.12% | -0.53% | 100% | 100%
Class F | -0.34% | -0.49% | 0.01% | 100% | 100%
Random Access Main 10 |  |  |  | 
Over VTM-7.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.13% | -0.20% | -0.18% | 103% | 101%
-0.19% | -0.14% | -0.02% | 103% | 100%
-0.14% | -0.11% | -0.09% | 102% | 100%
-0.61% | -0.97% | -0.86% | 102% | 100%
-0.28% | -0.36% | -0.30% | 102% | 100%
-0.41% | -0.64% | -0.52% | 102% | 100%
-0.33% | -0.34% | -0.35% | 101% | 100%
Low delay B Main10 |  |  |  | 
Over VTM-7.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.32% | -0.44% | -0.26% | 103% | 100%
-0.81% | -1.15% | -0.96% | 103% | 99%
-1.18% | -0.21% | -0.77% | 101% | 99%
-0.70% | -0.62% | -0.62% | 102% | 99%
-0.68% | -0.56% | -0.76% | 102% | 99%
-0.53% | -0.75% | 0.05% | 102% | 99%

## Slide 7
Simulation results (additional information)
8 valid modes 32 valid modes 48 valid modes
 | Random Access Main 10 |  | 
 | Over VTM-7.0 |  | 
 | Y | U | V
Class A1 | 0.09% | 0.18% | 0.21%
Class A2 | 0.03% | 0.17% | 0.23%
Class B | 0.06% | 0.21% | 0.13%
Class C | 0.06% | 0.15% | 0.13%
Class E |  |  | 
Overall | 0.06% | 0.18% | 0.16%
Class D | -0.03% | -0.01% | 0.00%
Class F | -0.11% | -0.03% | -0.08%
 | Low delay B Main10 |  | 
 | Over VTM-7.0 |  | 
 | Y | U | V
Class A1 |  |  | 
Class A2 |  |  | 
Class B | 0.09% | -0.09% | 0.26%
Class C | 0.18% | 0.09% | 0.40%
Class E | -0.14% | 0.57% | 0.08%
Overall | 0.06% | 0.14% | 0.26%
Class D | 0.00% | 0.32% | 0.48%
Class F | -0.03% | -0.47% | 0.43%
Random Access Main 10 |  | 
Over VTM-7.0 |  | 
Y | U | V
-0.10% | -0.19% | -0.07%
-0.13% | -0.12% | 0.02%
-0.12% | -0.08% | -0.11%
-0.41% | -0.60% | -0.53%
-0.19% | -0.25% | -0.19%
-0.31% | -0.46% | -0.52%
-0.29% | -0.32% | -0.27%
Low delay B Main10 |  | 
Over VTM-7.0 |  | 
Y | U | V
-0.29% | -0.34% | -0.17%
-0.59% | -0.80% | -0.48%
-0.84% | -0.24% | -0.49%
-0.53% | -0.47% | -0.35%
-0.54% | -0.46% | -0.64%
-0.41% | -1.17% | -0.22%
Over VTM-7.0 |  | 
Y | U | V
-0.11% | -0.15% | -0.18%
-0.17% | -0.07% | 0.02%
-0.15% | -0.11% | -0.10%
-0.55% | -0.79% | -0.74%
-0.25% | -0.29% | -0.27%
-0.41% | -0.53% | -0.60%
-0.33% | -0.36% | -0.29%
Low delay B Main10 |  | 
Over VTM-7.0 |  | 
Y | U | V
#VALUE! | #VALUE! | #VALUE!
-0.76% | -1.14% | -0.81%
-0.93% | -0.30% | -1.11%
#VALUE! | #VALUE! | #VALUE!
-0.64% | -0.42% | -0.44%
-0.51% | -1.04% | -0.09%

## Slide 8
Mode number-BD curve (LDB) (additional information)
Chart: mode number - coding impact curve (LDB)
| 8 | 16 | 32 | 48 | 64
 | 0.0006 | -0.0028 | -0.0053 | -0.007
 | 0.0006 | -0.0028 | -0.0053 | -0.007

## Slide 9
Other tests (additional information)
Encoder uses only first 16 modes (cmax of merge_geo_parititon_idx = 64, w/o mode table reordering, implemented on CE4-1)
RA (YCbCr): 0.19%, 0.30%, 0.30%
LDB(YCbCr): 0.44%, 0.62%, 0.69%
Encoder uses only first 16 modes (cmax of merge_geo_parititon_idx = 16, w/o mode table reordering, implemented on CE4-1)
RA (YCbCr): 0.04%, 0.06%, 0.14%
LDB(YCbCr): 0.07%, 0.31%, 0.47%
Encoder uses only first 16 modes (cmax of merge_geo_parititon_idx = 16, with mode table reordering, implemented on CE4-1)
RA (YCbCr): -0.09%, -0.09%, -0.08%
LDB(YCbCr): -0.28%, -0.20%, -0.20%
It can be observed that both signaling max value of cmax of merge_geo_partition_idx and geo mode table reordering contribute to coding efficiency.

## Slide 10
Proposal
Fix number of modes to 32
From aspect 1.2, having number of modes equal to 32 gives a relatively good trade off. It is proposed to fix number of mode to 32.

## Slide 11
Proposal
4 Reduce number of modes per block to 14
In this aspect, it is proposed to reduce number of modes per block to 14. For each block, only diagonal and invert diagonal directions are valid. GEO weight mask calculation process is reused. And 64x8 and 8x64 blocks are disallowed.
14 valid modes per block
 | Total # of cases | # modes per block size | # of supported block sizes
TPM | 50 | 2 | 25
GEO (JVET-Q0059, CE4-1) | 1,216 | 64 | 19
Aspect 1.4 | 238 | 14 | 17

## Slide 12
Simulation results
Anchor: VTM7.0
Test: 14 modes per block (implementation is based code of CE4-1)
 | Random Access Main 10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.05% | -0.08% | -0.07% | 100% | 101%
Class A2 | -0.05% | 0.02% | 0.10% | 99% | 100%
Class B | -0.06% | 0.04% | 0.08% | 100% | 100%
Class C | -0.25% | -0.37% | -0.25% | 100% | 100%
Class E |  |  |  |  | 
Overall | -0.11% | -0.10% | -0.03% | 100% | 100%
Class D | -0.18% | -0.24% | -0.18% | 100% | 100%
Class F | -0.10% | -0.07% | -0.04% | 100% | 100%
TGM | -0.17% | -0.22% | -0.17% | 101% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.17% | -0.36% | -0.03% | 100% | 100%
Class C | -0.31% | -0.57% | -0.36% | 100% | 100%
Class E | -0.64% | -0.24% | -0.26% | 98% | 99%
Overall | -0.33% | -0.40% | -0.20% | 99% | 100%
Class D | -0.30% | -0.26% | -0.51% | 100% | 99%
Class F | -0.17% | -0.50% | 0.06% | 99% | 100%

## Slide 13
13
Conclusion
This contribution proposes following changes GEO and solve concern regarding hardware validation efforts:
Disable 64x8 and 8x64 sized GEO block
  coding impact (anchor CE4 common base): 0.**% (RA), 0.03% (LDB)
Scalable number of modes (encoder chooses to use either 16 or 64 modes, cmax of merge_geo_partition_idx coding is set to 16 and 64 respectively)
  16 modes (anchor VTM7.0): -0.09% (RA) and -0.28% (LDB)
  64 modes (anchor VTM7.0): -0.28% (RA) and -0.70% (LDB)
(3) Set total number of modes to 32.
  coding impact (anchor VTM7.0): -0.19% (RA) and -0.53% (LDB)
(4) Fix number of modes per block to 14
coding impact (anchor VTM7.0): -0.11% (RA) and -0.23% (LDB)

## Slide 14
14
Thank Bytedance for cross-check