## Slide 1
JVET-Q0123
Ce4-related: Modifications for GEO
Li Jingya, Lim Chong Soon

## Slide 2
Introduction
Geometrical partitioning (GEO)
JVET-J1030/JVET-K0146 which applied to both AMVP and merge mode.
JVET-O0489, GEO was proposed for merge mode with 140 supported partitioning modes and 19 supported block size (8x8 to 128x128).
JVET-P0884/0885, efforts were made to remove multiplication of weight mask calculation and number of modes was reduced to 82.
JVET-Q0059, number of modes is further reduced to 64.
 | Total # of cases | # modes per block size | # of supported block sizes
TPM | 50 | 2 | 25
Wedge mode (in other standard) | 144 | 16 | 8
GEO (JVET-O0489, Gothenburg) | 2,660 | 140 | 19
GEO (JVET-P0884/JVET-Q0079, CE4 common base, Geneva) | 1,558 | 82 | 19
GEO (JVET-Q0059, CE4-1, Brussels) | 1,216 | 64 | 19

## Slide 3
Proposal
Remove 64x8 and 8x64 sized GEO block
It is proposed not to allow 64x8 and 8x64 sized coding block for GEO.

## Slide 4
Simulation results
Anchor: CE4-common base
Test: disallowing 64x8 and 8x64 block sizes for geo mode (encoder setting is changed same as CE4-2.1, implemented over CE4 common base).
*This aspect can also be combined with CE4-2.1 so that the complexity can be reduced more efficiently.
 | Random Access Main 10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.09% | 0.02% | 101% | 98%
Class A2 | 0.02% | 0.06% | -0.05% | 103% | 99%
Class B | -0.01% | 0.01% | 0.00% | 103% | 100%
Class C | -0.01% | -0.05% | -0.06% | 104% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | -0.02% | -0.02% | 103% | 99%
Class D | -0.01% | -0.09% | -0.15% | 104% | 101%
Class F | 0.00% | 0.01% | -0.02% | 101% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | 0.03% | 0.04% | 105% | 101%
Class C | 0.03% | -0.04% | -0.16% | 105% | 99%
Class E | 0.11% | -0.14% | 0.02% | 102% | 99%
Overall | 0.03% | -0.04% | -0.03% | 104% | 100%
Class D | -0.10% | -0.29% | -0.63% | 106% | 102%
Class F | 0.00% | -0.25% | -0.07% | 102% | 99%

## Slide 5
Proposal
2 Reduce number of modes per block to 14
In this aspect, it is proposed to reduce number of modes per block to 14. For each block, only diagonal and invert diagonal directions are valid. 64x8 and 8x64 blocks are disallowed.
14 valid modes per block
 | Total # of cases | # modes per block size | # of supported block sizes
TPM | 50 | 2 | 25
GEO (JVET-Q0059, CE4-1) | 1,216 | 64 | 19
Aspect 1.4 | 238 | 14 | 17

## Slide 6
Simulation results
Anchor: VTM7.0
Test: 14 modes per block (implementation is based code of CE4-1)
 | Random Access Main 10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.05% | -0.08% | -0.07% | 100% | 101%
Class A2 | -0.05% | 0.02% | 0.10% | 99% | 100%
Class B | -0.06% | 0.04% | 0.08% | 100% | 100%
Class C | -0.25% | -0.37% | -0.25% | 100% | 100%
Class E |  |  |  |  | 
Overall | -0.11% | -0.10% | -0.03% | 100% | 100%
Class D | -0.18% | -0.24% | -0.18% | 100% | 100%
Class F | -0.10% | -0.07% | -0.04% | 100% | 100%
TGM | -0.17% | -0.22% | -0.17% | 101% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.17% | -0.36% | -0.03% | 100% | 100%
Class C | -0.31% | -0.57% | -0.36% | 100% | 100%
Class E | -0.64% | -0.24% | -0.26% | 98% | 99%
Overall | -0.33% | -0.40% | -0.20% | 99% | 100%
Class D | -0.30% | -0.26% | -0.51% | 100% | 99%
Class F | -0.17% | -0.50% | 0.06% | 99% | 100%

## Slide 7
7
Conclusion
This contribution proposes following changes GEO and solve concern regarding hardware validation efforts:
Disable 64x8 and 8x64 sized GEO block
  coding impact (anchor CE4 common base): 0.00% (RA), 0.03% (LDB)
(2) Fix number of modes per block to 14
coding impact (anchor VTM7.0): -0.11% (RA) and -0.33% (LDB)

## Slide 8
8
Thank Bytedance for cross-check