## Slide 1: JVET-0166 On the adaptive color transform
Han Huang, Adarsh Krishnan Ramasubramonian, Chun-Chi Chen, Vadim Seregin, Ted Hsieh, Yung-Hsuan Chao, Wei-Jung Chien, Geert Van der Auwera, Marta Karczewicz
Location
Date
@qualcomm

## Slide 2: Summary of proposed
Add ACT QP offset before clipping of QP to avoid QP out of range;
Align the chroma QP at the deblocking stage to that at the dequantization stage as in as in adopted JVET-P1001;
CU-level switching of QP offset values according to the ACT CU-level flag.
Clip the input and output of inverse ACT to 16 bits dynamic range.
Signal ACT QP offset in PPS and slide header;
Use a separate chroma ACT QP offset for JointCbCr mode 2.

## Slide 3: Text change
Item 1-3: QP clipping, CU level switching of QP offset, alignment for DB,
If cu_act_enabled_flag[xCb][yCb] is equal to 1, variable QpY is derived as follows:
QpY = ( ( qPY_PRED + CuQpDeltaVal + 64 + 2 * QpBdOffset ) % ( 64 + QpBdOffset ) ) – QpBdOffset+ pps_act_y_qp_offset+ slice_ act_y_qp_offset
Otherwise, the variable QpY is derived as follows:
QpY = ( ( qPY_PRED + CuQpDeltaVal + 64 + 2 * QpBdOffset ) % ( 64 + QpBdOffset ) ) − QpBdOffset (1116)
If cu_act_enabled_flag[xCb][yCb] is equal to 1, The chroma quantization parameters for the Cb and Cr components, Qp′Cb and Qp′Cr, and joint Cb-Cr coding Qp′CbCr are derived as follows:
Qp′Cb = Clip3( −QpBdOffset, 63, qPCb + pps_act_cb_qp_offset + slice_ act_cb_qp_offset + CuQpOffsetCb ) + QpBdOffset (1122)
Qp′Cr = Clip3( −QpBdOffset, 63, qPCr + pps_ act_cr_qp_offset + slice_ act_cr_qp_offset + CuQpOffsetCr ) + QpBdOffset (1123)
Qp′CbCr = Clip3( −QpBdOffset, 63, qPCbCr + pps_act_cbcr_qp_offset + slice_act_cbcr_qp_offset +CuQpOffsetCbCr ) + QpBdOffset
Otherwise, the chroma quantization parameters for the Cb and Cr components, Qp′Cb and Qp′Cr, and joint Cb-Cr coding Qp′CbCr are derived as follows:
Qp′Cb = Clip3( −QpBdOffset, 63, qPCb + pps_cb_qp_offset + slice_cb_qp_offset + CuQpOffsetCb ) + QpBdOffset (1122)
Qp′Cr = Clip3( −QpBdOffset, 63, qPCr + pps_cr_qp_offset + slice_cr_qp_offset + CuQpOffsetCr ) + QpBdOffset (1123)
Qp′CbCr = Clip3( −QpBdOffset, 63, qPCbCr + pps_joint_cbcr_qp_offset + slice_joint_cbcr_qp_offset +CuQpOffsetCbCr ) + QpBdOffset (1124)
Luma QP
Chroma QP

## Slide 4: Text change
Item 4: clipping of input and output of ACT
The (nTbW)x(nTbH) arrays of residual samples rY, rCb and rCr are modified as follows:
rY[ x ][ y ] = Clip3( CoeffMin, CoeffMax, rY[ x ][ y ])
rCb[ x ][ y ] = Clip3( CoeffMin, CoeffMax, rCb[ x ][ y ])
rCr[ x ][ y ] = Clip3( CoeffMin, CoeffMax, rCr[ x ][ y ])
tmp = rY[ x ][ y ] − rCb[ x ][ y ] (1191)
rY[ x ][ y ] = rY[ x ][ y ] + rCb[ x ][ y ] (1192)
rCb[ x ][ y ] = tmp − rCr[ x ][ y ] (1193)
rCr[ x ][ y ] = tmp + rCr[ x ][ y ] (1194)
rY[ x ][ y ] = Clip3( CoeffMin, CoeffMax, rY[ x ][ y ])
rCb[ x ][ y ] = Clip3( CoeffMin, CoeffMax, rCb[ x ][ y ])
rCr[ x ][ y ] = Clip3( CoeffMin, CoeffMax, rCr[ x ][ y ])

## Slide 5: Text change
if( sps_act_enabled_flag ) { | 
pps_slice_act_qp_offset_present_flag | u(1)
pps_act_y_qp_offset_plus5 | se(v)
pps_act_cb_qp_offset_plus5 | se(v)
pps_act_cr_qp_offset_plus3 | se(v)
if( pps_joint_cbcr_qp_offset_present_flag ) | 
pps_act_cbcr_qp_offset_plus5 | se(v)
} | 
Item 5-6: Signaling of ACT offset at SPS and slice header
if(pps_slice_act_qp_offset_present_flag && !( slice_type == I && qtbtt_dual_tree_intra_flag) ) { | 
slice_act_y_qp_offset | se(v)
slice_act_cb_qp_offset | se(v)
slice_act_cr_qp_offset | se(v)
if( pps_joint_cbcr_qp_offset_present_flag ) | 
slice_act_cbcr_qp_offset | se(v)
} | 
SPS ACT offset:
Slice header ACT offset:

## Slide 6: Test results
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.0% | -0.3% | -0.2%
RGB, mixed content, 1440p & 1080p | 0.0% | -0.7% | -0.5%
RGB, Animation, 720p | 0.0% | -1.5% | -1.0%
RGB, camera captured, 1080p | -0.1% | -0.5% | -0.4%
Enc Time[%] | 97% |  | 
Dec Time[%] | 104% |  | 
 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.0% | -0.4% | -0.3%
RGB, mixed content, 1440p & 1080p | -0.1% | -1.0% | -0.6%
RGB, Animation, 720p | -0.1% | -1.3% | -0.7%
RGB, camera captured, 1080p | 0.1% | -0.3% | -0.2%
Enc Time[%] | 97% |  | 
Dec Time[%] | 101% |  | 
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.0% | -0.3% | -0.4%
RGB, mixed content, 1440p & 1080p | -0.2% | -0.9% | -0.7%
RGB, Animation, 720p | -0.1% | -0.6% | -0.5%
RGB, camera captured, 1080p | -0.1% | 0.0% | -0.4%
Enc Time[%] | 99% |  | 
Dec Time[%] | 102% |  | 
Applying item 1-5
 | All Intra |  | 
 | G/Y | B/U | R/V
YUV444, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0%
YUV444, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0%
YUV444, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV444, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 95% |  | 
Dec Time[%] | 101% |  | 
 | Random Access |  | 
 | G/Y | B/U | R/V
YUV444, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0%
YUV444, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.1%
YUV444, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV444, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 99% |  | 
Dec Time[%] | 100% |  | 
 | Low delay B |  | 
 | G/Y | B/U | R/V
YUV444, text & graphics with motion, 1080p & 720p | 0.0% | -0.2% | -0.3%
YUV444, mixed content, 1440p & 1080p | 0.0% | -0.1% | -0.1%
YUV444, Animation, 720p | 0.1% | 0.1% | -0.1%
YUV444, camera captured, 1080p | 0.1% | 0.0% | 0.1%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 

## Slide 7: Test results
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.0% | -0.3% | -0.2%
RGB, mixed content, 1440p & 1080p | 0.0% | -0.7% | -0.5%
RGB, Animation, 720p | 0.0% | -1.5% | -1.0%
RGB, camera captured, 1080p | -0.1% | -0.5% | -0.4%
Enc Time[%] | 104% |  | 
Dec Time[%] | 94% |  | 
 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.0% | -0.4% | -0.3%
RGB, mixed content, 1440p & 1080p | -0.1% | -1.0% | -0.6%
RGB, Animation, 720p | -0.1% | -1.4% | -0.7%
RGB, camera captured, 1080p | 0.0% | -0.3% | -0.2%
Enc Time[%] | 97% |  | 
Dec Time[%] | 91% |  | 
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.1% | -0.3% | -0.4%
RGB, mixed content, 1440p & 1080p | -0.2% | -0.9% | -0.7%
RGB, Animation, 720p | -0.1% | -0.7% | -0.5%
RGB, camera captured, 1080p | 0.0% | 0.0% | -0.3%
Enc Time[%] | 98% |  | 
Dec Time[%] | 93% |  | 
Applying item 1-6
 | All Intra |  | 
 | G/Y | B/U | R/V
YUV444, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0%
YUV444, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0%
YUV444, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV444, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 99% |  | 
Dec Time[%] | 93% |  | 
 | Random Access |  | 
 | G/Y | B/U | R/V
YUV444, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0%
YUV444, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.1%
YUV444, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV444, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 97% |  | 
Dec Time[%] | 91% |  | 
 | Low delay B |  | 
 | G/Y | B/U | R/V
YUV444, text & graphics with motion, 1080p & 720p | 0.0% | -0.1% | -0.1%
YUV444, mixed content, 1440p & 1080p | -0.1% | -0.1% | -0.1%
YUV444, Animation, 720p | 0.1% | 0.0% | 0.0%
YUV444, camera captured, 1080p | 0.1% | 0.0% | 0.1%
Enc Time[%] | 98% |  | 
Dec Time[%] | 91% |  |