## Slide 1: JVET-Q0251: CE5-related: Unified cross component adaptive loop filter
Nan Hu, Vadim Seregin, Marta Karczewicz

## Slide 2
 | Filters in an APS | APS id in SH/PH
Chroma ALF in VVC | Up to 8 chroma ALF filters | One chroma APS id
CCALF in CE5 anchor | Up to 4 Cb CCALF filters + Up to 4 Cr CCALF filters | One Cb APS id + One Cr APS id
Proposed | Up to 8 chroma CCALF filters | One chroma APS id
 | Filters usage in a slice
Chroma ALF in VVC | Cb and Cr CTBs use the same chroma ALF filter set from an APS
CCALF in CE5 anchor | Cb CTBs use Cb CCALF filters in an APS Cr CTBs use Cr CCALF filters in an APS (Separated sets)
Proposed | Cb and Cr CTBs use the same chroma CCALF filter set from an APS
Thank Ericsson for cross-checking
 | Y | U | V | EncT | DecT
AI | -0.01% | 0.05% | -0.17% | 100% | 100%
RA | 0.02% | -0.04% | -0.06% | 100% | 100%
LDB |  |  |  |  | 
LDP | 0.04% | -0.12% | -0.40% | 100% | 100%

## Slide 3: Results
Thank Ericsson for cross-checking
 | All Intra Main10 |  |  |  | 
 | Over VTM-7.0-CE5Anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.10% | 0.16% | 101% | 100%
Class A2 | 0.06% | -0.12% | -0.92% | 99% | 98%
Class B | 0.02% | -0.36% | 0.17% | 101% | 101%
Class C | -0.06% | 0.22% | 0.02% | 100% | 102%
Class E | -0.09% | 0.64% | -0.58% | 100% | 99%
Overall | -0.01% | 0.05% | -0.17% | 100% | 100%
Class D | -0.01% | -0.15% | -0.65% | 98% | 100%
Class F | -0.02% | 0.01% | 0.09% | 100% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0-CE5Anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | -0.03% | -0.02% | -0.38% | 100% | 101%
Class E | -0.08% | 0.23% | -0.92% | 100% | 100%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | -0.01% | -0.49% | -1.07% | 100% | 100%
Class F | 0.07% | -0.09% | 0.79% | 100% | 100%
 | Low delay P Main10 |  |  |  | 
 | Over VTM-7.0-CE5Anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.02% | 0.03% | 0.07% | 100% | 99%
Class C | -0.01% | -0.19% | -0.26% | 100% | 100%
Class E | 0.14% | -0.25% | -1.38% | 100% | 101%
Overall | 0.04% | -0.12% | -0.40% | 100% | 100%
Class D | -0.02% | -1.43% | -1.85% | 99% | 100%
Class F | -0.07% | -0.27% | -0.08% | 101% | 101%
 | Random access Main10 |  |  |  | 
 | Over VTM-7.0-CE5Anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.16% | 0.30% | 101% | 99%
Class A2 | 0.08% | -0.30% | -0.70% | 100% | 97%
Class B | 0.02% | -0.05% | 0.05% | 100% | 100%
Class C | -0.03% | 0.00% | 0.00% | 100% | 102%
Class E |  |  |  |  | 
Overall | 0.02% | -0.04% | -0.06% | 100% | 100%
Class D | -0.03% | -0.29% | -0.30% | 102% | 100%
Class F | -0.02% | 0.09% | -0.10% | 99% | 101%