## Slide 1: Non-CE5: Adaptive precision for CCALF coefficients
Fujitsu
17th JVET Meeting: Brussels, BE, 7–17 January 2020

## Slide 2: Proposed method (1/2)
The CCALF filtering process
  Where = 7 in current CCALF.
Change into a variable
  ranges [5, 12] and ( - 5) will be saved in 3 bits value for each CCALF.

## Slide 3: Proposed method (2/2)
The is derived by Encoder:
  is the coefficient with maximum absolute value in each CCALF filter before fixed point process.
if ( alf_cross_component_cb_filter_signal_flag ) { | 
alf_cross_component_cb_filters_signalled_minus1 | ue(v)
for( k = 0; k < (alf_cross_component_cb_filters_signalled_minus1+1); k++ ) { | 
for ( j = 0; j < 8; j++ ) | 
alf_cross_component_cb_coeff_plus32[ k ][ j ] | u(6)
alf_cross_component_cb_coeff_shift_minus5[k] | u(3)
} | 
} | 

## Slide 4: Experiment results
 |  |  | All Intra Main10 |  | 
 |  |  | Over CE5 anchor |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.51% | -0.14% | 98% | 100%
Class A2 | 0.01% | -0.75% | -0.44% | 93% | 100%
Class B | 0.01% | -0.12% | -0.19% | 105% | 100%
Class C | 0.01% | -0.10% | -0.16% | 108% | 100%
Class E | 0.02% | -0.14% | -0.31% | 100% | 100%
Overall | 0.01% | -0.29% | -0.24% | 102% | 100%
Class D | 0.01% | -0.10% | -0.15% | 88% | #NUM!
Class F | 0.03% | -0.29% | -0.34% | 105% | #NUM!
 |  |  | Random access Main10 |  | 
 |  |  | Over CE5 anchor |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.03% | -1.02% | -0.50% | 102% | 100%
Class A2 | 0.02% | -0.40% | -0.24% | 102% | 100%
Class B | 0.01% | -0.22% | -0.65% | 101% | 100%
Class C | -0.02% | -0.15% | -0.16% | 103% | 100%
Class E |  |  |  |  | 
Overall | 0.01% | -0.40% | -0.41% | 102% | 100%
Class D | -0.02% | -0.02% | -0.05% | 101% | 100%
Class F | 0.00% | -0.48% | -0.48% | 99% | 100%

## Slide 5: Conclusions
With proposed method
  The 6 bits for each CCALF coefficient will be fully utilized to improve the precision.
  It could cooperate with many contributions of CCALF to improve coding gain with no computational complexity increment.
It is proposed to adopt this method if adopt CCALF.
Thank Sharp for cross-checking