## Slide 1: JVET-Q0303 LFNST signaling simplification
Fujitsu
17th Meeting: Brussels, BE, 7–17 January 2020

## Slide 2: Motivation
LfnstDcOnly constraint for LFNST signaling depends on ISP condition
  1. ISP == false. LFNST is applicable if LfnstDcOnly == 0, ie one or more scan positions of the last significant coefficient (lastScanPos) within the CU are no less than 1
  2. ISP == true. The constraint 1 is ignored. LFNST is always applicable

## Slide 3: Proposal
Remove ISP condition check for LFNST signaling
  1. ISP == false. LFNST is applicable if LfnstDcOnly == 0, ie one or more scan positions of the last significant coefficient (lastScanPos) within the CU are no less than 1
  2. ISP == true. The constraint 1 is ignored. LFNST is always applicable

## Slide 4: Results
  Negligible different on coding efficiency and complexity
 | All Intra Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.19% | 0.08% | 99% | 100%
Class A2 | 0.00% | -0.01% | -0.07% | 100% | 100%
Class B | 0.00% | 0.03% | -0.06% | 102% | 101%
Class C | -0.01% | 0.03% | 0.10% | 101% | 99%
Class E | 0.00% | -0.05% | 0.01% | 99% | 99%
Overall | 0.00% | -0.03% | 0.01% | 100% | 100%
Class D | 0.02% | -0.05% | -0.12% | 102% | 102%
Class F | 0.01% | 0.04% | 0.12% | 101% | 101%
 | Random access Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | 0.02% | -0.01% | 99% | 100%
Class A2 | -0.05% | -0.05% | -0.07% | 104% | 100%
Class B | 0.03% | 0.04% | 0.11% | 99% | 100%
Class C | 0.00% | -0.03% | 0.00% | 98% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | 0.00% | 0.02% | 100% | 100%
Class D | -0.03% | 0.06% | -0.16% | 75% | 100%
Class F | 0.04% | 0.06% | 0.07% | 98% | 100%

## Slide 5: Conclusion
Remove ISP condition check for LFNST signaling
  Simpler and consistent LFNST signaling design
  No impact on coding efficiency and complexity
Suggest adopt this contribution
Thanks for HHI’s cross-checking
  JVET-Q0578