## Slide 1: JVET-Q0332 AhG12: On the slice number signaling dependent on subpictures
​Yao-Jen Chang, Vadim Seregin, Muhammed Coban, Marta Karczewicz
​
​Brussels, Belgium
​Jan. 2020

## Slide 2: Summary
Current VVC:
  num_slices_in_pic_minus1 plus 1 specifies the number of rectangular slices in each picture referring to the PPS.
Proposed:
  num_slices_in_pic_minus_num_subpics plus NumSubpic specifies the number of rectangular slices in each picture referring to the PPS.

## Slide 3: Signaling Comparison
PPS signaling in VVC 7
  pps_num_subpics_minus1
    Condition on pps_subpics_id_signalling_present_flag
    The range of the values: 0 ~ 255, inclusive
    15 bits in worst case
  num_slices_in_pic_minus1
    >=15 bits
Suggested change (combined with Q0333/334/335)
  pps_num_subpics_minus1
    Condition on pps_subpics_id_signalling_present_flag
    The range of the values: 0 ~ 255, inclusive
    15 bits in worst case
  num_slices_in_pic_minus_num_subpics
    >= 1 bit
>= 30 bits
>= 16 bits