## Slide 1: JVET-Q0338 CE4-related: Harmonized conditions for CIIP and GEO
N. Park, J. Nam, H. Jang, J. Lim, S. Kim

## Slide 2: Introduction
In GEO mode, theses constraints are applied.
  GEO mode is disabled when block width or height is less than 8.
  GEO mode is disabled when block width or height is larger than 64 by CE4-2.1.
These constraints contributes to the number of the parsing conditions for CIIP and GEO becomes larger.

## Slide 3: Introduction
merge_data( x0, y0, cbWidth, cbHeight, chType ) { | Descriptor
…… | 
if( ( cbWidth * cbHeight ) >= 64 && cbWidth < 128 && cbHeight < 128 && ( (sps_ciip_enabled_flag && cu_skip_flag[ x0 ][ y0 ] = = 0) ¦ ¦ ( sps_geo_enabled_flag && MaxNumGeoMergeCand > 1 && cbWidth>=8 && cbHeight >=8 && slice_type = = B ) ) ) | 
regular_merge_flag[ x0 ][ y0 ] | ae(v)
if( regular_merge_flag[ x0 ][ y0 ] = = 1 ) { | 
if( sps_mmvd_enabled_flag ) | 
mmvd_merge_flag[ x0 ][ y0 ] | ae(v)
…… | 
} else if( MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} else { | 
if( sps_ciip_enabled_flag && sps_geo_enabled_flag && MaxNumGeoMergeCand > 1 && slice_type = = B && cu_skip_flag[ x0 ][ y0 ] = = 0 && cbWidth >= 8 && cbHeight >= 8 && cbWidth < 128 && cbHeight < 128 ) | 
ciip_flag[ x0 ][ y0 ] | ae(v)
…… | 
In the spec text, to parse the regular merge, CIIP and GEO, 1 multiplication, 8 “AND” and 9 “COMPARISION” are required.

## Slide 4: Proposed methods
Different constrained block size for CIIP and GEO makes the parsing condition complicated.
In this proposal, the block size constraint for CIIP and GEO on parsing conditions are unified.
 | Current | Proposed Method
CIIP | ( cbWidth * cbHeight ) >= 64 cbWidth < 128 && cbHeight < 128 | cbWidth >= 8 && cbHeight >= 8 cbWidth < 128 && cbHeight < 128
GEO | cbWidth >= 8 && cbHeight >= 8 | cbWidth >= 8 && cbHeight >= 8 cbWidth < 128 && cbHeight < 128
by CE4-2.1
by proposed method

## Slide 5: Proposed methods
1 multiplication, 8 “AND” and 9 “COMPARISION” operations are reduced to 3 “AND” and 4 “COMPARISION”.
The parsing condition of the “regular_merge_flag” | if( ( cbWidth * cbHeight ) >= 64 ( cbWidth >= 8 && cbHeight >= 8) && cbWidth < 128 && cbHeight < 128 && ( (sps_ciip_enabled_flag && cu_skip_flag[ x0 ][ y0 ] = = 0 ) ¦ ¦ (sps_geo_enabled_flag && MaxNumGeoMergeCand > 1 && cbWidth>=8 && cbHeight>=8 && slice_type = = B ) ) ) regular_merge_flag[ x0 ][ y0 ]
The parsing condition of the “ciip_flag” | if( regular_merge_flag[ x0 ][ y0 ] = = 1 ) { …… } else { if( sps_ciip_enabled_flag && sps_geo_enabled_flag && MaxNumGeoMergeCand > 1 && slice_type = = B && cu_skip_flag[ x0 ][ y0 ] = = 0 && cbWidth >= 8 && cbHeight >= 8 && cbWidth < 128 && cbHeight < 128 ) ciip_flag[ x0 ][ y0 ] }

## Slide 6: Simulation results
Simulation results
CIIP performance on top of the VTM7.0
 | Over VTM7.0 with CE4-2.1 |  |  |  |  |  |  |  |  | 
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.04% | 0.00% | 100% | 99% |  |  |  |  | 
Class A2 | 0.03% | 0.04% | 0.02% | 100% | 99% |  |  |  |  | 
Class B | 0.00% | -0.04% | 0.04% | 100% | 98% | 0.04% | -0.19% | 0.02% | 99% | 99%
Class C | 0.07% | 0.02% | 0.00% | 100% | 99% | 0.08% | -0.09% | 0.00% | 99% | 99%
Class E |  |  |  |  |  | 0.08% | 0.40% | 0.21% | 100% | 102%
Overall | 0.02% | -0.01% | 0.02% | 100% | 99% | 0.06% | -0.01% | 0.06% | 100% | 100%
Class D | 0.03% | -0.01% | 0.14% | 99% | 99% | 0.03% | 0.71% | 0.06% | 99% | 96%
Class F | 0.02% | 0.00% | -0.02% | 100% | 99% | 0.03% | -0.60% | -0.54% | 100% | 98%
RA |  |  |  |  | LDB |  |  |  | 
BDR-Y | BDR-U | BDR-V | EncTime | DecTime | BDR-Y | BDR-U | BDR-V | EncTime | DecTime
0.28% | 0.01% | 0.01% | 99% | 100% | 0.39% | 0.46% | 0.48% | 99% | 100%

## Slide 7: Conclusion
In this contribution, harmonized conditions for CIIP and GEO mode are proposed.
The simulation results reportedly show 0.02% loss in RA and 0.06% loss in LB on top of the CE4-2.1.
It is recommended to consider this method in the next VTM.
Thanks to Bytedance (JVET-Q0575) for crosscheck