## Slide 1
JVET-Q0366
Simplification of interpolation filtering
G. Rath, F. Galpin, F. Urban

## Slide 2: Proposal summary
Remove a filter from the intra prediction process
Reduced intra prediction process complexity for smoothing case (reduce number of multiplications by a factor 4)
Simplify spec (11 lines removed)
No significant changes in BD-rate ( +0.02% in both AI and RA)

## Slide 3
condition A?
integer slope?
integer slope?
copy
yes
no
no
no
yes
yes
cubic 4-tap
copy
Filter ref.
Condition B?
Smooth 4-tap
yes
no
  Cond. A: Luma && refIdx = 0 && ISPmode = 0 && non-MIP && W*H > 32
  Cond. B: mode angularity > Th(W,H)
VTM-7

## Slide 4
condition A&B?
integer slope?
integer slope?
Filter ref.
yes
no
no
no
yes
yes
copy
cubic 4-tap
copy
linear interp
  Cond. A: Luma && refIdx = 0 && ISPmode = 0 && non-MIP && W*H > 32
  Cond. B: mode angularity > Th(W,H)
Proposal

## Slide 5
Complexity analysis
 | VTM 7.0 |  |  |  | Proposal |  |  | 
 | formula | 8*8 | 16*16 | 32*32 | formula | 8*8 | 16*16 | 32*32
mult | 4*h*w | 256 | 1024 | 4096 | h*w | 64 | 256 | 1024
add | 4*h*w+3*x | 280 | 1072 | 4192 | 6*(h+w)+3*h*w | 288 | 960 | 3456
shift | h*w+4*x | 96 | 320 | 1152 | 4*(h+w)+h*w | 128 | 384 | 1280
(*) x is either h or w

## Slide 6
Simulation Results
Thank you!
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-7.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.07% | -0.06% | 0.23% | 100% | 99%
Class A2 | 0.02% | 0.00% | 0.00% | 101% | 98%
Class B | 0.02% | 0.08% | -0.01% | 100% | 97%
Class C | -0.01% | 0.10% | 0.03% | 100% | 93%
Class E | 0.01% | -0.06% | 0.18% | 100% | 95%
Overall | 0.02% | 0.03% | 0.07% | 100% | 96%
Class D | 0.00% | -0.03% | 0.01% | 99% | 94%
Class F | 0.01% | 0.03% | 0.07% | 100% | 93%
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-7.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.04% | -0.05% | -0.01% | 99% | 99%
Class A2 | -0.03% | -0.02% | 0.16% | 100% | 98%
Class B | 0.03% | 0.12% | 0.24% | 99% | 101%
Class C | 0.03% | -0.11% | -0.02% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.02% | 0.00% | 0.10% | 100% | 100%
Class D | 0.02% | -0.05% | -0.18% | 100% | 99%
Class F | 0.03% | 0.06% | 0.08% | 99% | 105%

## Slide 7
Filtering of reference samples in VTM7
Angles with integer slopes (abs(predIntraAngle) is 32, 64, …):
Reference filtered if :
  Luma
  refIdx = 0
  ISPmode = 0
  non-MIP
  W * H > 32
Angles with non-integer slopes:
refMain[x] = (ref[x-1] + 2 * ref[x] + ref[x+1] + 2 ) >> 2;
Reference is never filtered

## Slide 8: Prediction in VTM7
Angles with integer slopes (abs(predIntraAngle) is 32, 64, …)
Direct reference sample copy:
Angles with non-integer slopes: interpolation
)
Luma:
Chroma:
Notes: Background: intra prediction

## Slide 9
Two interpolation filters
(a) 4-tap smoothing filter if:
  Luma
  refIdx = 0
  ISPmode = 0
  non-MIP
  W*H > 32
  mode angularity > Th(W,H)
Else
(b) 4-tap cubic filter
Luma, Angles with non-integer slopes:
4-tap Smoothing filter
f[0] = (16 - (deltaFract >> 1)),
f[1] = (32 - (deltaFract >> 1)),
f[2] = (16 + (deltaFract >> 1)),
f[3] = (deltaFract >> 1);
≡ filtering with [1 2 1]/4 followed by linear interpolation
at deltaFract
Same as reference filtering conditions
for angles with integer slopes
Interpolation filter f in VTM7

## Slide 10
Proposed simplification
Prediction:
Angles with integer slopes (abs(predIntraAngle) is 32, 64, …) (no change)
Direct reference sample copy:
Angles with non-integer slopes: interpolation
If Luma and reference not filtered:
where f = always 4-tap cubic filter (no smooting filter)
Else (i.e., chroma or luma with filtered reference) linear interpolation:
)
Filtering of reference samples:
Reference filtered if:
  Luma
  refIdx = 0
  ISPmode = 0
  non-MIP
  W*H > 32
  mode angularity > Th(W,H)
  (irrespective of if the angle has
  Integer slope or not)