## Slide 1
JVET-Q0417: AHG8/AHG9: On SPS level virtual boundary
J. Chen, Y. Ye, R.-L. Liao, J. Luo (Alibaba)
2020/1/12

## Slide 2
Virtual boundary may be signaled in SPS or PH. When signaled in SPS, it has constraint based on picture width or height which are signaled in PPS. Constraint on high level things based on low level is undesirable.
Problem statement
sps_virtual_boundaries_pos_x[ i ] specifies the location of the i-th vertical virtual boundary in units of luma samples divided by 8. The value of sps_virtual_boundaries_pos_x[ i ] shall be in the range of 1 to Ceil( pic_width_in_luma_samples ÷ 8 ) − 1, inclusive. [Ed. (VD): pic_width_in_luma_samples is in the PPS, not in the SPS.]
sps_virtual_boundaries_pos_y[ i ] specifies the location of the i-th horizontal virtual boundary in units of luma samples divided by 8. The value of sps_virtual_boundaries_pos_y[ i ] shall be in the range of 1 to Ceil( pic_height_in_luma_samples ÷ 8 ) − 1, inclusive. [Ed. (VD): pic_height_in_luma_samples is in the PPS, not in the SPS.]
seq_parameter_set_rbsp( ) { | Descriptor
…. | 
sps_virtual_boundaries_present_flag | u(1)
if( sps_virtual_boundaries_present_flag ) { | 
sps_num_ver_virtual_boundaries | u(2)
for( i = 0; i < sps_num_ver_virtual_boundaries; i++ ) | 
sps_virtual_boundaries_pos_x[ i ] | u(13)
sps_num_hor_virtual_boundaries | u(2)
for( i = 0; i < sps_num_hor_virtual_boundaries; i++ ) | 
sps_virtual_boundaries_pos_y[ i ] | u(13)
} | 

## Slide 3
Constraint the virtual boundary positons signaled in SPS based on maximum picture width/height.
For each picture, only apply the virtual boundary within the current picture (ignore those beyond picture boundary)
Proposed method 1
pic_width_in_luma_samples
pic_width_max_in_luma_samples

## Slide 4
The parameter VirtualBoundariesNumVer and the location of the vertical virtual boundary VirtualBoundariesPosX[ i ] in units of luma samples are derived as follows:
for(i=0,j=0;i< sps_num_ver_virtual_boundaries;i++){
if(sps_virtual_boundaries_pos_x[ i ]<= Ceil( pic_width_in_luma_samples ÷ 8 ) – 1){
VirtualBoundariesPosX[j++]= sps_virtual_boundaries_pos_x[ i ]
}
}
VirtualBoundariesNumVer=j
The parameter VirtualBoundariesNumHor and the location of the horizontal virtual boundary VirtualBoundariesPosY[ i ] in units of luma samples is derived as follows:
for(i=0,j=0;i< sps_num_hor_virtual_boundaries;i++){
if(sps_virtual_boundaries_pos_y [ i ] <= Ceil( pic_height_in_luma_samples ÷ 8 ) – 1){
VirtualBoundariesPosY[j++]= sps_virtual_boundaries_pos_y [ i ]
}
}
VirtualBoundariesNumHor=j
Proposed method 1 – spec change

## Slide 5
Constraint the virtual boundary positons signaled in SPS based on maximum picture width/height.
For each picture, scale the virtual boundary positon signaled in SPS according to the current picture width/height
Proposed method 2
pic_width_in_luma_samples
pic_width_max_in_luma_samples

## Slide 6
The scaling factor VBScaleX and VBScaleY are derived as follows:
    VBScaleX = ( (pic_width_max_in_luma_samples << 14 ) + (pic_width_in_luma_samples >> 1 ) ) / pic_width_in_luma_samples
    VBScaleY = ( (pic_height_max_in_luma_samples << 14 ) + (pic_height_in_luma_samples >> 1 ) ) / pic_height_in_luma_samples
The parameters SPSVirtualBoundariesPosX[i] and SPSVirtualBoundariesPosY[i] are derived as follows:
    SPSVirtualBoundariesPosX[i]= (sps_virtual_boundaries_pos_x[ i ]* VBScaleX + ( 1 << 13 )) >> 14
    SPSVirtualBoundariesPosX[i]=(( SPSVirtualBoundariesPosX[i] + 4 ) >> 3) << 3
    SPSVirtualBoundariesPosY[i]= (sps_virtual_boundaries_pos_y[ i ]* VBScaleX + ( 1 << 13 )) >> 14
    SPSVirtualBoundariesPosY[i]=(( SPSVirtualBoundariesPosY[i] + 4 ) >> 3) << 3
Proposed method 2 – spec change

## Slide 7
Disallow the combination of “virtual boundary signaling in SPS” and “picture size change”
The constraint of ps_virtual_boundaries_pos_x[i]/ps_virtual_boundaries_pos_y[i] in SPS may also changed to be based on maximum picture width/height.
Proposed method 3
Way 1:
  When subpics_present_flag is equal to 1 or ref_pic_resampling_enabled_flag equal to 0 or sps_num_ver_virtual_boundaries is not equal to 0, the value of pic_width_in_luma_samples shall be equal to pic_width_max_in_luma_samples.
  When subpics_present_flag is equal to 1 or ref_pic_resampling_enabled_flag equal to 0 or sps_num_hor_virtual_boundaries is not equal to 0, the value of pic_height_in_luma_samples shall be equal to pic_height_max_in_luma_samples.
Way 2:
  when ref_pic_resampling_enabled_flag is 1, sps_virtual_boundaries_present_flag shall be 0.