## Slide 1: JVET-Q0456: Non-CE4: simplified LUT for GEO blending weights generation
Yanzhuo Ma, Qihong Ran, Ruipeng Qiu, Menglin Zhang,
Junyan Huo, Shuai Wan, Fuzheng Yang,
Yuanfang Yu, Yang Liu,
January. 2020

## Slide 2: Derivation of GEO pre-defined masks in VVC7.0_common base
the information of current block is derived from two sets of pre-defined masks, the calculation of two masks need to looking-up the weight LUT and the angle LUT as follows.
Idx | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
WedgeFilter [idx] | 4 | 4 | 4 | 4 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 6 | 6 | 6
Idx | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 
WedgeFilter [idx] | 6 | 6 | 6 | 6 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 8 | 
idx | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Dis[idx] | 8 | 8 | 8 | 4 | 4 | 2 | 0 | -2 | -4 | -4 | -8 | -8
idx | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
Dis[idx] | -8 | -8 | -8 | -4 | -4 | -2 | -0 | 2 | 4 | 4 | 8 | 8
The look-up table for angle
The look-up table for weight

## Slide 3: Proposed method
In this contribution, it is proposed to reduce or remove the weight LUT without performance loss.
the modification is to reduce the length of weight LUT from 27 to 14
Reduce the length of the weight LUT (GeoFilter [])
Idx | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
GeoFilter [idx] | 4 | 4 | 4 | 4 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 6 | 6 | 6
Idx | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 
GeoFilter [idx] | 6 | 6 | 6 | 6 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 8 | 
The look-up table for weight in CE4 common base
Idx | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
GeoFilter[idx] | 4 | 4 | 5 | 5 | 5 | 5 | 6 | 6 | 6 | 7 | 7 | 7 | 7 | 8
Modified look-up table GeoFilter[]
the calculation of and need to modefiy as follow:

## Slide 4: Proposed method
To apply the reduced weight LUT, all the values in the angle LUT Dis[] need to be reduced respectively.
The look-up table for angle in CE4 common base
The Modified look-up table for angle
idx | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Dis[idx] | 8 | 8 | 8 | 4 | 4 | 2 | 0 | -2 | -4 | -4 | -8 | -8
idx | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
Dis[idx] | -8 | -8 | -8 | -4 | -4 | -2 | -0 | 2 | 4 | 4 | 8 | 8
idx | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Dis[idx] | 4 | 4 | 4 | 2 | 2 | 1 | 0 | -1 | -2 | -2 | -4 | -4
idx | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
Dis[idx] | -4 | -4 | -4 | -2 | -2 | -1 | -0 | 1 | 2 | 2 | 4 | 4
Reduce the length of the weight LUT (GeoFilter [])

## Slide 5: Proposed method
Remove the weights LUT (GeoFilter [])
Another mathematically identical implementation of this contribution is to replace the reduced weight LUT
Idx | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
GeoFilter[idx] | 4 | 4 | 5 | 5 | 5 | 5 | 6 | 6 | 6 | 7 | 7 | 7 | 7 | 8
Modified look-up table GeoFilter[]
the calculations of pre-defined masks are modified as follows:
Remove

## Slide 6: Experimental results
 | Random Access |  |  |  | 
 | Over VTM7.0(CE4)_common base |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 100%
Class A2 | 0.00% | 0.00% | 0.00% | 100% | 100%
Class B | 0.00% | 0.00% | 0.00% | 100% | 100%
Class C | 0.00% | 0.00% | 0.00% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | 0.00% | 0.00% | 100% | 100%
Class D | 0.00% | 0.00% | 0.00% | 100% | 100%
Class F (optional) | 0.00% | 0.00% | 0.00% | 99% | 99%

## Slide 7: Conclusion
Advantages:
  Reduced or Removed the memory to store weight LUT
  the calculation can be implemented in a parallel way when LUT is removed
Recommend to adopt into VVC along the GEO method
Thanks crosschecking by Alibaba

## Slide 8
Thank you