## Slide 1
AHG14: BDPCM for Inter/IBC-predicted residuals (JVET-R0354)
T. Tsukuba, Y. Yagasaki, M. Ikeda, T. Suzuki

## Slide 2: Summary of JVET-R0354
Introduction
  In HEVC, RDPCM can be applied to Intra/Inter/IBC-predicted residuals
  In VVC, BDPCM can be applied to only Intra-predicted residuals
Proposal
  Apply BDPCM to Inter/IBC-predicted residuals
Experimental results
Thanks to Qualcomm for the crosscheck
LowQP | RGB 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT
AI | -0.27% | -0.27% | -0.27% | 103% | 100%
RA | -0.60% | -0.60% | -0.64% | 108% | 100%
LB | -0.44% | -0.45% | -0.44% | 113% | 99%
CTC | RGB 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT
AI | -0.09% | -0.11% | -0.10% | 102% | 98%
RA | -0.15% | -0.16% | -0.14% | 107% | 99%
LB | -0.19% | -0.20% | -0.21% | 109% | 98%
Lossless DualTreeOn | RGB 4:4:4 |  | 
 | Bit-rate savings | EncT | DecT
AI | -0.72% | 102% | 97%
RA | -1.40% | 108% | 98%
LB | -1.93% | 108% | 96%
LowQP | YUV 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT
AI | -0.17% | -0.13% | -0.18% | 106% | 100%
RA | -0.59% | -0.57% | -0.57% | 114% | 100%
LB | -0.33% | -0.32% | -0.33% | 120% | 100%
CTC | YUV 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT
AI | -0.07% | 0.12% | -0.01% | 105% | 99%
RA | -0.03% | 0.14% | 0.12% | 110% | 100%
LB | 0.04% | 0.14% | 0.19% | 111% | 97%
Lossless DualTreeOn | YUV 4:4:4 |  | 
 | Bit-rate savings | EncT | DecT
AI | -0.53% | 105% | 102%
RA | -1.14% | 111% | 98%
LB | -1.32% | 113% | 98%

## Slide 3: Introduction
In HEVC, RDPCM can be applied to Intra/Inter/IBC-predicted residuals.
In VVC, BDPCM can be applied to only Intra-predicted residuals.
At the last meeting, Inter BDPCM was proposed in JVET-Q0460.
  Additional gains were observed, but no support for BDPCM for IBC-predicted residuals
To make the design of BDPCM consistent with HEVC, would like to propose BDPCM for not only Intra but also Inter/IBC-predicted residuals
Method | Supported RDPCM/BDPCM |  | 
 | Intra-predicted block | Inter-predicted block | IBC-predicted block
HEVC | Implicit RDPCM | Explicit RDPCM | Explicit RDPCM
VVC | Intra BDPCM | N/A | N/A
JVET-Q0460 | Intra BDPCM | Inter BDPCM | N/A
JVET-R0354 | Intra BDPCM | Inter BDPCM | IBC BDPCM
Notes: BBCの提案が採用されなかったのは？ゲインが小さかったから？

## Slide 4: Proposal
Apply BDPCM to Inter/IBC-predicted residuals in addition to Intra residuals
Summary of proposed changes
  No change for syntax of Intra BDPCM
  Signal bdpcm_{luma, chroma}_flag for Inter/IBC-predicted residuals after signaling cu_act_enabled_flag for Inter:
  Signal bdcpm_dir_{luma, chroma}_flag to specify the residual prediction direction if bdpcm_{luma, chroma}_flag is equal to 1
  Add one additional context for each bdpcm_{luma, chroma}_flag and bdcpm_dir_{luma, chroma}_flag
  Reuse entire BDPCM modules (Inverse BDPCM, Forward BPDCM) for Inter/IBC BDPCM
  To reduce the encoder runtimes, following fast search is applied:
    Search Chroma BDPCM for Inter/IBC if either of coded_flag for Cb or Cr is equal to 1
    Reuse Chroma BDPCM for non-JCCR case for JCCR case

## Slide 5: Highlighted Spec Changes

## Slide 6: Highlighted Spec Changes
bdpcm_luma_flag equal to 1 specifies that BDPCM is applied to the current luma coding block at the location ( x0, y0 ), i.e. the transform is skipped, the intra luma prediction mode is specified by bdpcm_luma_dir_flag. bdpcm_luma_flag equal to 0 specifies that BDPCM is not applied to the current luma coding block at the location ( x0, y0 ).
When bdpcm_luma_flag is not present it is inferred to be equal to 0.
The variable BdpcmFlag[ x ][ y ][ cIdx ] is set equal to bdpcm_luma_flag for x = x0..x0 + cbWidth − 1, y = y0..y0 + cbHeight − 1 and cIdx = 0.
bdpcm_luma_dir_flag equal to 0 specifies that the BDPCM prediction direction is horizontal. bdpcm_luma_dir_flag equal to 1 specifies that the BDPCM prediction direction is vertical.
The variable BdpcmDir[ x ][ y ][ cIdx ] is set equal to bdpcm_luma_dir_flag for x = x0..x0 + cbWidth − 1, y = y0..y0 + cbHeight − 1 and cIdx = 0.
bdpcm_chroma_flag equal to 1 specifies that BDPCM is applied to the current chroma coding blocks at the location ( x0, y0 ), i.e. the transform is skipped, the chroma prediction mode is specified by bdpcm_chroma_dir_flag. bdpcm_chroma_flag equal to 0 specifies that BDPCM is not applied to the current chroma coding blocks at the location ( x0, y0 ).
When bdpcm_chroma_flag is not present it is inferred to be equal to 0.
The variable BdpcmFlag[ x ][ y ][ cIdx ] is set equal to bdpcm_chroma_flag for x = x0..x0 + cbWidth − 1, y = y0..y0 + cbHeight − 1 and cIdx = 1..2.
bdpcm_chroma_dir_flag equal to 0 specifies that the BDPCM prediction direction is horizontal. bdpcm_chroma_dir_flag equal to 1 specifies that the BDPCM prediction direction is vertical.
The variable BdpcmDir[ x ][ y ][ cIdx ] is set equal to bdpcm_chroma_dir_flag for x = x0..x0 + cbWidth − 1, y = y0..y0 + cbHeight − 1 and cIdx = 1..2.

## Slide 7: Simulation
Proposal was implemented on top of VTM-8.0
Simulation were conducted under following condition
  444/lossless condition
  444/SCC/common QP condition
  444/SCC/low QP condition (QP=2,7,12,17) with first 100 frames

## Slide 8: Coding performance under 444/lossless coding (DualTreeOn)
RGB | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM-8.0 | Tested |  | VTM-8.0 | Tested |  | VTM-8.0 | Tested | 
TGM 1080p | 10.9 | 10.9 | -0.59% | 173.2 | 174.9 | -1.15% | 251.2 | 254.2 | -1.47%
TGM 720p | 5.0 | 5.1 | -0.27% | 51.5 | 51.9 | -1.62% | 90.1 | 90.9 | -1.92%
A | 3.0 | 3.1 | -2.29% | 8.6 | 8.9 | -1.87% | 7.1 | 7.7 | -3.45%
M | 3.0 | 3.0 | -0.37% | 19.1 | 19.5 | -1.74% | 21.0 | 21.5 | -2.12%
CC | 0.9 | 0.9 | -0.04% | 0.9 | 0.9 | -0.21% | 0.9 | 0.9 | -0.32%
Overall | 5.2 | 5.3 | -0.72% | 61.5 | 62.1 | -1.40% | 90.7 | 91.8 | -1.93%
Enc Time[%] | 102% |  |  | 108% |  |  | 108% |  | 
Dec Time[%] | 97% |  |  | 98% |  |  | 96% |  | 
YUV | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM-8.0 | Tested |  | VTM-8.0 | Tested |  | VTM-8.0 | Tested | 
TGM 1080p | 10.7 | 10.7 | -0.62% | 174.7 | 176.5 | -1.28% | 252.9 | 256.1 | -1.60%
TGM 720p | 6.4 | 6.4 | -0.35% | 64.5 | 65.0 | -1.50% | 115.8 | 116.6 | -1.75%
A | 3.5 | 3.6 | -0.96% | 7.9 | 8.0 | -0.94% | 7.9 | 7.9 | -0.68%
M | 3.9 | 3.9 | -0.52% | 26.3 | 26.7 | -1.28% | 28.9 | 29.4 | -1.64%
CC | 1.0 | 1.0 | -0.06% | 1.1 | 1.1 | -0.22% | 1.1 | 1.1 | -0.35%
Overall | 5.8 | 5.8 | -0.53% | 66.3 | 67.0 | -1.14% | 99.2 | 100.3 | -1.32%
Enc Time[%] | 105% |  |  | 111% |  |  | 113% |  | 
Dec Time[%] | 102% |  |  | 98% |  |  | 98% |  | 

## Slide 9: Coding performance under 444/SCC/low QP condition (QP=2,7,12,17, DualTreeOff)
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
TGM 1080p | -0.32% | -0.29% | -0.29% | 108% | 101% | -0.50% | -0.49% | -0.51% | 105% | 101%
TGM 720p | -0.16% | -0.07% | -0.16% | 107% | 101% | -0.20% | -0.24% | -0.20% | 103% | 100%
Animation | 0.08% | 0.07% | -0.03% | 103% | 98% | -0.06% | -0.01% | -0.05% | 102% | 101%
Mixed content | -0.21% | -0.18% | -0.20% | 106% | 101% | -0.26% | -0.29% | -0.28% | 102% | 99%
Overall | -0.17% | -0.13% | -0.18% | 106% | 100% | -0.27% | -0.27% | -0.27% | 103% | 100%
 | Random access Main10 |  |  |  |  |  |  |  |  | 
 | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
TGM 1080p | -0.70% | -0.69% | -0.71% | 115% | 100% | -0.72% | -0.76% | -0.79% | 111% | 101%
TGM 720p | -0.86% | -0.57% | -0.46% | 113% | 100% | -0.75% | -0.84% | -0.86% | 107% | 100%
Animation | -0.04% | 0.12% | -0.04% | 115% | 101% | -0.24% | -0.19% | -0.18% | 107% | 100%
Mixed content | -0.64% | -1.10% | -1.04% | 115% | 101% | -0.58% | -0.50% | -0.60% | 107% | 98%
Overall | -0.59% | -0.57% | -0.57% | 114% | 100% | -0.60% | -0.60% | -0.64% | 108% | 100%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
TGM 1080p | -0.64% | -0.56% | -0.63% | 120% | 100% | -0.81% | -0.84% | -0.80% | 114% | 100%
TGM 720p | -0.33% | -0.30% | -0.25% | 119% | 99% | -0.42% | -0.46% | -0.39% | 112% | 100%
Animation | 0.01% | 0.04% | -0.02% | 122% | 101% | -0.12% | -0.13% | -0.15% | 114% | 96%
Mixed content | -0.23% | -0.36% | -0.34% | 119% | 100% | -0.28% | -0.24% | -0.31% | 110% | 100%
Overall | -0.33% | -0.32% | -0.33% | 120% | 100% | -0.44% | -0.45% | -0.44% | 113% | 99%

## Slide 10: Coding performance under 444/SCC/common QP condition (DualTreeOff)
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
TGM 1080p | -0.10% | 0.00% | 0.01% | 105% | 97% | -0.15% | -0.22% | -0.21% | 104% | 99%
TGM 720p | -0.08% | 0.26% | -0.08% | 105% | 98% | -0.10% | -0.10% | -0.08% | 100% | 96%
Animation | -0.02% | 0.04% | -0.03% | 106% | 101% | 0.04% | 0.05% | 0.05% | 103% | 100%
Mixed content | -0.07% | 0.16% | 0.08% | 104% | 99% | -0.11% | -0.14% | -0.11% | 101% | 98%
Overall | -0.07% | 0.12% | -0.01% | 105% | 99% | -0.09% | -0.11% | -0.10% | 102% | 98%
 | Random access Main10 |  |  |  |  |  |  |  |  | 
 | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
TGM 1080p | -0.13% | 0.06% | 0.01% | 112% | 99% | -0.26% | -0.27% | -0.31% | 108% | 100%
TGM 720p | -0.04% | 0.21% | 0.18% | 109% | 99% | -0.13% | -0.15% | -0.12% | 106% | 99%
Animation | 0.05% | 0.10% | 0.04% | 112% | 101% | 0.05% | 0.00% | 0.07% | 109% | 98%
Mixed content | 0.03% | 0.22% | 0.25% | 108% | 100% | -0.23% | -0.18% | -0.14% | 107% | 101%
Overall | -0.03% | 0.14% | 0.12% | 110% | 100% | -0.15% | -0.16% | -0.14% | 107% | 99%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
TGM 1080p | -0.18% | -0.08% | -0.01% | 112% | 97% | -0.36% | -0.36% | -0.37% | 112% | 99%
TGM 720p | 0.06% | 0.26% | 0.28% | 112% | 98% | -0.13% | -0.03% | -0.16% | 112% | 101%
Animation | 0.12% | 0.20% | 0.13% | 112% | 98% | -0.06% | 0.06% | 0.03% | 105% | 95%
Mixed content | 0.25% | 0.23% | 0.39% | 107% | 97% | -0.17% | -0.47% | -0.30% | 107% | 98%
Overall | 0.04% | 0.14% | 0.19% | 111% | 97% | -0.19% | -0.20% | -0.21% | 109% | 98%

## Slide 11: Conclusion
Apply BDPCM to Inter/IBC-predicted residuals to make design of BDPCM consistent with HEVC
Improved coding performance under 444/lossless, 444/SCC/low QP condition, 444/SCC/common QP condition
Recommend: Adopt JVET-R0354 into the next VTM/VVC WD or further study it toward future extension of VVC