## Slide 1: JVET-P0375: AHG2/AHG16: CCLM bug fix in luma reference down-sampling
L. Pham Van, G. Van der Auwera, J. Chen, V. Seregin, M. Karczewicz
@qualcomm
04/2020
AV

## Slide 2: Content
Problem
Solution
Experimental results
Conclusion

## Slide 3: Problem: avaiTL check is not always in CCLM
Current spec and VTM: avaiTL = avaiT && avaiL
However, in raster slice scan mode, avaiT and avaiL are true but avaiTL may be false
Slice border
CTU border
The top and left of the current point are available, but the top-left point is unavailable

## Slide 4: Proposed fix: Not use the top-left samples in down-sampling
The variables availL and, availT and availTL are derived as follows: The derivation process for neighbouring block availability as specified in clause 6.4.4 is invoked with the current luma location ( xCurr, yCurr ) set equal to ( xTbY, yTbY ), the neighbouring luma location ( xTbY − 1, yTbY ), checkPredModeY set equal to FALSE, and cIdx as inputs, and the output is assigned to availL. The derivation process for neighbouring block availability as specified in clause 6.4.4 is invoked with the current luma location ( xCurr, yCurr ) set equal to ( xTbY, yTbY ), the neighbouring luma location ( xTbY, yTbY − 1 ), checkPredModeY set equal to FALSE, and cIdx as inputs, and the output is assigned to availT. The variable availTL is derived as follows: availTL = availL && availT … When availTL is equal to TRUE, tThe neighbouring top-left luma samples pY[ x ][ y ] with x = −SubWidthC.. −1, y = −1, −2, are set equal to the luma samples pY[ x ][0] reconstructed luma samples prior to the deblocking filter process at the locations ( xTbY+ x, yTbY + y ). … 5. When numSampT is greater than 0, the selected neighbouring top chroma samples pSelC[ idx ] are set equal to p[ pickPosT[ idx − cntL ] ][ -1 ] with idx = cntL..cntL + cntT − 1, and the down-sampled neighbouring top luma samples pSelDsY[ idx ] with idx = 0..cntL + cntT − 1 are specified as follows: The neighbouring top-left luma samples pY[ x ][ y ] with x = −SubWidthC..−1, y = −1, −2, are set equal to the luma samples pY[ 0 ][ y ]. The variable x is set equal to pickPosT[ idx − cntL ].

## Slide 5: Experimental results
Thanks HHI for cross-check
Anchor: VTM8.0
Test: Proposed bug fix
 | All Intra Main10 |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.02% | -0.02% | 101% | 100%
Class A2 | 0.00% | 0.04% | 0.03% | 100% | 100%
Class B | 0.00% | 0.01% | 0.08% | 101% | 101%
Class C | 0.01% | -0.06% | 0.00% | 100% | 99%
Class E | 0.00% | 0.01% | -0.04% | 100% | 100%
Overall | 0.00% | 0.00% | 0.02% | 100% | 100%
Class D | 0.00% | -0.05% | -0.11% | 100% | 98%
Class F | 0.02% | 0.02% | 0.02% | 100% | 99%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.08% | 0.00% | 102% | 101%
Class A2 | -0.02% | -0.06% | 0.14% | 100% | 100%
Class B | 0.00% | -0.11% | -0.06% | 100% | 101%
Class C | -0.02% | -0.11% | -0.14% | 100% | 99%
Class E |  |  |  |  | 
Overall | -0.01% | -0.09% | -0.03% | 100% | 100%
Class D | 0.02% | 0.07% | 0.05% | 100% | 99%
Class F | 0.04% | -0.01% | -0.02% | 99% | 98%

## Slide 6: Conclusions
Simple fix for avaiTL check bug in CCLM mode
Fix bug and editorial change suggestion in ticket# 796 are presented
It is recommended to adopt the above simple and clean fix into VVC

## Slide 7
Thank you!