## Slide 1: JVET-S0089 AHG8: On TMVP derivation using inter-layer reference picture
N. Park, J. Nam, H. Jang, J. Lim, S. Kim

## Slide 2: Introduction
In HEVC
  POC-based MV scaling process for TMVP was disabled when a picture refers a long-term reference picture.
  TMVP was disabled when reference picture type is different.
  Above two rules were applied for ILRP, also. (Since ILRP was marked as LTRP, it was performed as LTRP.)
In VVC,
  The logic of HEVC was inherited.
 | RefPic | ColRefPic | TMVP behavior
For Non-ILRP | STRP | STRP | “available”
 | STRP | LTRP | “unavailable”
 | LTRP | STRP | “unavailable”
 | LTRP | LTRP | “available” but not scaled
For ILRP | STRP | ILRP (LTRP) | “unavailable”
 | ILRP (LTRP) | STRP | “unavailable”
 | LTRP | ILRP (LTRP) | “available” but not scaled
 | ILRP (LTRP) | LTRP | “available” but not scaled
 | ILRP (LTRP) | ILRP (LTRP) | “available” but not scaled
RefPic : reference picture of a current CU
ColRefPic : reference picture of a collocated CU

## Slide 3: Introduction
An example including ILRP:
  A CU refers a picture in the same layer with current picture.
  A collocated CU refers a picture in the same layer with collocated picture.
“available”
“available”
but not scaled

## Slide 4: Introduction
Another example including ILRP:
  A CU refers a picture in the same layer with current picture.
  A collocated CU refers a picture in the different layer with collocated picture.
  A CU refers a picture in the different layer with current picture.
  A collocated CU refers a picture in the same layer with collocated picture.
“unavailable”
“available”
but not scaled
“unavailable”
“available”
but not scaled

## Slide 5: Introduction
Another example including ILRP:
  A CU refers a picture in the same layer with current picture.
  A collocated CU refers a picture in the different layer with collocated picture.
  A CU refers a picture in the different layer with current picture.
  A collocated CU refers a picture in the same layer with collocated picture.
“unavailable”
“available”
but not scaled
“unavailable”
“available”
but not scaled
Undesirable behavior relevant to ILRP is observed
Only LTRP-ILRP case is considered for the TMVP operation, even though ILRP was marked as LTRP to distinct the reference picture type and LTRP-ILRP pair occurs very rarely.
STRP-ILRP case is not considered, even though STRP has higher correlation with current picture than LTRP and ILRP may not mean to have long distance.

## Slide 6: Proposed method
To address TMVP behavior more clearly, three solutions are proposed.
  Solution 1: Disabling TMVP when either RefPic or ColRefPic is ILRP, but not both.
  Solution 2: Enabling TMVP with combination of STRP and ILRP on RefPic or ColRefPic, and disabling TMVP with combination of LTRP and ILRP.
  Solution 3: Enabling TMVP when either RefPic or ColRefPic is ILRP.
RefPic | ColRefPic | Current | Solution 1 | Solution 2 | Solution 3
STRP | ILRP | X | X | O | O
ILRP | STRP | X | X | O | O
LTRP | ILRP | O | X | X | O
ILRP | LTRP | O | X | X | O
X : “unavailable”
O : “available” but not scaled
“unavailable” (X)
“available” but not scaled (O)

## Slide 7: Proposed method
The proposed draft changes
  Solution 1: Disabling TMVP when either RefPic or ColRefPic is ILRP, but not both.
The function LongTermRefPic( aPic, aPb, refIdx, LX ), with X being 0 or 1, is defined as follows:
  If nuh_layer_id of the picture with index refIdx from reference picture list LX of the slice containing prediction block aPb in the picture aPic was not equal to nuh_layer_id of the picture aPic at the time when aPic was the current picture, LongTermRefPic(aPic, aPb, refIdx, LX) is equal to 2.
  Otherwise, if the picture with index refIdx from reference picture list LX of the slice containing prediction block aPb in the picture aPic was marked as "used for long-term reference" at the time when aPic was the current picture, LongTermRefPic( aPic, aPb, refIdx, LX ) is equal to 1.
  Otherwise, LongTermRefPic( aPic, aPb, refIdx, LX ) is equal to 0.
…
– When availableFlagLXCol is equal to TRUE, mvLXCol and availableFlagLXCol are derived as follows:
  If LongTermRefPic( currPic, currCb, refIdxLX, LX ) is not equal to LongTermRefPic( ColPic, colCb, refIdxCol, listCol ), both components of mvLXCol are set equal to 0 and availableFlagLXCol is set equal to 0.
  Otherwise, the variable availableFlagLXCol is set equal to 1, refPicList[ listCol ][ refIdxCol ] is set to be the picture with reference index refIdxCol in the reference picture list listCol of the slice containing coding block colCb in the collocated picture specified by ColPic, and the following applies:
…

## Slide 8: Proposed method
The proposed draft changes
  Solution 2: Enabling TMVP with combination of STRP and ILRP on RefPic or ColRefPic, and disabling TMVP with combination of LTRP and ILRP.
The function LongTermRefPic( aPic, aPb, refIdx, LX ), with X being 0 or 1, is defined as follows:
  If the picture with index refIdx from reference picture list LX of the slice containing prediction block aPb in the picture aPic was marked as "used for long-term reference" and had the nuh_layer_id same with nuh_layer_id of the picture aPic at the time when aPic was the current picture, LongTermRefPic( aPic, aPb, refIdx, LX ) is equal to 1.
  Otherwise, LongTermRefPic( aPic, aPb, refIdx, LX ) is equal to 0.
…
– When availableFlagLXCol is equal to TRUE, mvLXCol and availableFlagLXCol are derived as follows:
  If LongTermRefPic( currPic, currCb, refIdxLX, LX ) is not equal to LongTermRefPic( ColPic, colCb, refIdxCol, listCol ), both components of mvLXCol are set equal to 0 and availableFlagLXCol is set equal to 0.
  Otherwise, the variable availableFlagLXCol is set equal to 1, refPicList[ listCol ][ refIdxCol ] is set to be the picture with reference index refIdxCol in the reference picture list listCol of the slice containing coding block colCb in the collocated picture specified by ColPic, and the following applies:
    colPocDiff = DiffPicOrderCnt( ColPic, refPicList[ listCol ][ refIdxCol ] ) (607)
    currPocDiff = DiffPicOrderCnt( currPic, RefPicList[ X ][ refIdxLX ] ) (608)
    The temporal motion buffer compression process for collocated motion vectors as specified in clause 8.5.2.15 is invoked with mvCol as input, and the modified mvCol as output.
    If RefPicList[ X ][ refIdxLX ] is an LTRP, colPocDiff is equal to 0, or colPocDiff is equal to currPocDiff, mvLXCol is derived as follows:
      mvLXCol = Clip3( −131072, 131071, mvCol ) (609)

## Slide 9: Proposed method
The proposed draft changes
  Solution 3: Enabling TMVP when either RefPic or ColRefPic is ILRP.
The function LongTermRefPic( aPic, aPb, refIdx, LX ), with X being 0 or 1, is defined as follows:
  If the picture with index refIdx from reference picture list LX of the slice containing prediction block aPb in the picture aPic was marked as "used for long-term reference" at the time when aPic was the current picture, LongTermRefPic( aPic, aPb, refIdx, LX ) is equal to 1.
  Otherwise, LongTermRefPic( aPic, aPb, refIdx, LX ) is equal to 0.
…
– When availableFlagLXCol is equal to TRUE, mvLXCol and availableFlagLXCol are derived as follows:
  If LongTermRefPic( currPic, currCb, refIdxLX, LX ) is not equal to LongTermRefPic( ColPic, colCb, refIdxCol, listCol ) and nuh_layer_id of the picture currPic and ColPic is equal to nuh_layer_id of the reference picture of its, both components of mvLXCol are set equal to 0 and availableFlagLXCol is set equal to 0.
  Otherwise, the variable availableFlagLXCol is set equal to 1, refPicList[ listCol ][ refIdxCol ] is set to be the picture with reference index refIdxCol in the reference picture list listCol of the slice containing coding block colCb in the collocated picture specified by ColPic, and the following applies:
    colPocDiff = DiffPicOrderCnt( ColPic, refPicList[ listCol ][ refIdxCol ] ) (607)
    currPocDiff = DiffPicOrderCnt( currPic, RefPicList[ X ][ refIdxLX ] ) (608)
    The temporal motion buffer compression process for collocated motion vectors as specified in clause 8.5.2.15 is invoked with mvCol as input, and the modified mvCol as output.
    If RefPicList[ X ][ refIdxLX ] is an LTRP, colPocDiff is equal to 0, or colPocDiff is equal to currPocDiff, mvLXCol is derived as follows:
      mvLXCol = Clip3( −131072, 131071, mvCol ) (609)

## Slide 10: Conclusion
In the current VVC, undesirable behavior relevant to ILRP is observed.
  Only LTRP-ILRP case is considered for the TMVP operation, even though ILRP was marked as LTRP to distinct the reference picture type and LTRP-ILRP pair occurs very rarely.
  STRP-ILRP case is not considered, even though STRP has more higher correlation with current picture than LTRP and ILRP may not mean to have long distance.
To address TMVP behavior more clearly, three solutions are proposed.
It is recommended to consider one of proposed methods in the next VTM
RefPic | ColRefPic | Current | Solution 1 | Solution 2 | Solution 3
STRP | ILRP | X | X | O | O
ILRP | STRP | X | X | O | O
LTRP | ILRP | O | X | X | O
ILRP | LTRP | O | X | X | O