## Slide 1
JVET-S0215
AHG2: On residual coding syntax
2020/6/22

## Slide 2
Problem statement
Specification bug-fixes
  Aspect 1: Condition of bypass/context coding coeff_sign_flag (#855)
  Aspect 2: Semantic of sig_coeff_flag
  Aspect 3: Semantic of sb_coded_flag

## Slide 3
  Aspect 1: Condition of bypass/context coding coeff_sign_flag (#855)
  In current spec, conditions for by-pass/context of coeff_sign_flag are not aligned with the VTM software
Example:
sh_ts_residual_coding_disabled_flag == 0, and
transform_skip_flag == 1, and
the value of the variable RemCcbs at the beginning of a CG is equal to 3.
In VTM, in the above mentioned conditions, coeff_sign_flag is by-pass coded.
According to spec, coeff_sign_flag is context coded

## Slide 4
  Aspect 1: Proposed fix
/* First scan pass */ | 
inferSbSigCoeffFlag = 1 | 
lastScanPosPass1 = −1 | 
for( n = 0; n <= numSbCoeff − 1 && RemCcbs >= 4; n++ ) { | 
xC = ( xS << log2SbW ) + DiagScanOrder[ log2SbW ][ log2SbH ][ n ][ 0 ] | 
yC = ( yS << log2SbH ) + DiagScanOrder[ log2SbW ][ log2SbH ][ n ][ 1 ] | 
lastScanPosPass1 = n | 
if( sb_coded_flag[ xS ][ yS ] && ( n != numSbCoeff − 1 ¦ ¦ !inferSbSigCoeffFlag ) ) { | 
sig_coeff_flag[ xC ][ yC ] | ae(v)
RemCcbs− − | 
if( sig_coeff_flag[ xC ][ yC ] ) | 
inferSbSigCoeffFlag = 0 | 
} | 
CoeffSignLevel[ xC ][ yC ] = 0 | 
if( sig_coeff_flag[ xC ][ yC ] { | 
coeff_sign_flag[ n ] | ae(v)
RemCcbs− − | 
CoeffSignLevel[ xC ][ yC ] = ( coeff_sign_flag[ n ] > 0 ? −1 : 1 ) | 
abs_level_gtx_flag[ n ][ 0 ] | ae(v)
RemCcbs− − | 
if( abs_level_gtx_flag[ n ][ 0 ] ) { | 
par_level_flag[ n ] | ae(v)
RemCcbs− − | 
} | 
} | 
AbsLevelPass1[ xC ][ yC ] = sig_coeff_flag[ xC ][ yC ] + par_level_flag[ n ] + abs_level_gtx_flag[ n ][ 0 ] | 
lastScanPosPass1 = n | 
} | 
Residual coding syntax table:

## Slide 5
  Aspect 2: Semantic of sig_coeff_flag
sig_coeff_flag[ xC ][ yC ] specifies for the transform coefficient location ( xC, yC ) within the current transform block whether the corresponding transform coefficient level at the location ( xC, yC ) is non-zero as follows:
If sig_coeff_flag[ xC ][ yC ] is equal to 0, the transform coefficient level at the location ( xC, yC ) is set equal to 0.
Otherwise (sig_coeff_flag[ xC ][ yC ] is equal to 1), the transform coefficient level at the location ( xC, yC ) has a non‑zero value.
When sig_coeff_flag[ xC ][ yC ] is not present, it is inferred as follows:
If ( xC, yC ) is the last significant location ( LastSignificantCoeffX, LastSignificantCoeffY ) in scan order or all of the following conditions are true, sig_coeff_flag[ xC ][ yC ] is inferred to be equal to 1:
  ( xC & ( (1 << log2SbW ) − 1 ), yC & ( (1 << log2SbH ) − 1 ) ) is equal to ( 0, 0 ).
  inferSbDcSigCoeffFlag is equal to 1.
  sb_coded_flag[ xS ][ yS ] is equal to 1.
Otherwise, sig_coeff_flag[ xC ][ yC ] is inferred to be equal to 0.
In case of TSRC, the above inference rule does not reflect the design intention and does not match with VTM software.

## Slide 6
  Aspect 2: Semantic of sig_coeff_flag: Proposed fix

## Slide 7
  Aspect 3: Semantic of sb_coded_flag
The above definition is only valid for regular residual coding and if the number of remaining context coded bins is greater than 0 (i.e. context coded bins are still available) to code the CG.
sb_coded_flag[ xS ][ yS ] specifies the following for the subblock at location ( xS, yS ) within the current transform block, where a subblock is an array of transform coefficient levels:
If sb_coded_flag[ xS ][ yS ] is equal to 0, the 16 transform coefficient levels of the subblock at location ( xS, yS ) are inferred to be equal to 0.
Otherwise (sb_coded_flag[ xS ][ yS ] is equal to 1), the following applies:
  If ( xS, yS ) is equal to ( 0, 0 ) and ( LastSignificantCoeffX, LastSignificantCoeffY ) is not equal to ( 0, 0 ), at least one of the 16 sig_coeff_flag syntax elements is present for the subblock at location ( xS, yS ).
  Otherwise, at least one of the 16 transform coefficient levels of the subblock at location ( xS, yS ) has a non-zero value.
When sb_coded_flag[ xS ][ yS ] is not present, it is inferred to be equal to 1.

## Slide 8
  Aspect 3: Semantic of sb_coded_flag: Proposed fix