## Slide 1: JVET-S0217 On deblocking filter for ACT
Shunsuke Iwamura (NHK)

## Slide 2: Introduction
In the current spec, deblocking filter and chroma scaling operation of LMCS is controlled by the existence of transform coefficients for the current TU.
8.8.3.5 Derivation process of boundary filtering strength
8.7.5.3Picture reconstruction with luma dependent chroma residual scaling process for chroma samples

## Slide 3: Problem statement
In VTM-9.0, when ACT is enabled for the current CU, at least one of tu_{y, cb, cr}_coded_flag is 1[1].
During inverse ACT process, the energy of residual signal may be spread to all three components in most case.
When ACT is enabled for the current block, the following issues happen:
  Chroma residual scaling is not applied to Cb/Cr components, and residual signal is not added to the prediction for the component, when the corresponding tu_coded_flag is 0 [2].
  Deblocking filtering process is not applied to the component whose tu_coded_flag is 0, when the flag of the adjacent block is also 0.
[1]: There is a mismatch between VTM and spec and JVET-S0231, JVET-S0233 propose to align spec with VTM.
[2]: JVET-S0234 software solves this problem by removing tu_coded_flag check in chroma scaling
cu_act_enabled=1,
tu_y_coded_flag=1,
tu_cb_coded_flag=0,
tu_cr_coded_flag=0
skipped block (cu_act_enabled=0)
cu_act_enabled=1
tu_y_coded_flag=1,
tu_cb_coded_flag=0,
tu_cr_coded_flag=0
only G component deblocked

## Slide 4: Solution 1: Check whether ACT is enabled
8.7.5.3 Picture reconstruction with luma dependent chroma residual scaling process for chroma samples
…
The reconstructed chroma picture sample recSamples is derived as follows for i = 0..nCurrSw − 1, j = 0..nCurrSh − 1:
If one or more of the following conditions are true, recSamples[ xCurr + i ][ yCurr + j ] is set equal to Clip1( predSamples[ i ][ j ] + resSamples[ i ][ j ] ):
  ph_chroma_residual_scale_flag is equal to 0.
  sh_lmcs_used_flag is equal to 0.
  nCurrSw * nCurrSh is less than or euqal to 4.
  tu_cb_coded_flag [ xCurr ][ yCurr ] is equal to 0 and tu_cr_coded_flag [ xCurr ][ yCurr ] is equal to 0 and cu_act_enabled_flag[ xCurr * SubWidthC ][ yCurr * SubHeightC ] is equal to 0.
Otherwise, the following applies:
…
The reconstructed chroma picture sample array recSamples is derived as follows:
If tuCbfChroma is equal to 1 or cu_act_enabled_flag[ xCurr * SubWidthC ][ yCurr * SubHeightC ] is equal to 1, the following applies:
resSamples[ i ][ j ] = Clip3( −( 1 << BitDepth ), ( 1 << BitDepth ) − 1, resSamples[ i ][ j ] ) (1226)
recSamples[ xCurr + i ][ yCurr + j ] = Clip1( predSamples[ i ][ j ] + (1227) Sign( resSamples[ i ][ j ] ) * ( ( Abs( resSamples[ i ][ j ] ) * varScale + ( 1 << 10 ) ) >> 11 ) )
Otherwise (tuCbfChroma is equal to 0 and cu_act_enabled_flag[ xCurr * SubWidthC ][ yCurr * SubHeightC ] is equal to 0), the following applies:
recSamples[ xCurr + i ][ yCurr + j ] = predSamples[ i ][ j ] (1228)

## Slide 5: Solution 1: Check whether ACT is enabled
ACT=0
cbf_y=1
cbf_cb=0
cbf_cr=0
ACT=1
cbf_y=1
cbf_cb=0
cbf_cr=0
ACT=1
no-resi
SBT-coded
deblock for G, B, R is applied
deblock for G is applied
ACT=0
cbf_y=1
cbf_cb=0
cbf_cr=0
ACT=1
cbf_y=1
cbf_cb=0
cbf_cr=0
ACT=1
no-resi
SBT-coded
deblock for G is applied
Current VTM
Proposal
8.8.3.5 Derivation process of boundary filtering strength
…
Otherwise, if the sample p0 or q0 is in a coding block coded with cu_act_enabled_flag equal to 1 and the sample p0 or q0 is in a transform block coded with either tu_y_coded_flag, tu_cb_coded_flag, or tu_cr_coded_flag equal to 1, bS[ xDi ][ yDj ] is set equal to 1.
…

## Slide 6: Solution 2: Modify coded_flag when ACT is applied
Solution 1 needs additional check in deblocking filter process, which affect not only 4:4:4 but also 4:2:0 and 4:2:2.
In order not to affect non-4:4:4 operation, it is proposed to mofidy tu_coded_flag in inverse ACT process.
8.4.1 General decoding process for coding units coded in intra prediction mode
3. When cu_act_enabled_flag[ xCb ][ yCb ] is equal to 1, the following applies:
- The residual modification process for residual blocks using colour space conversion as specified in clause 8.7.4.6 is invoked with the variable nTbW set equal to cbWidth, the variable nTbH set equal to cbHeight, the array rY set equal to resSamplesL, the array rCb set equal to resSamplesCb, and the array rCr set equal to resSamplesCr as inputs, and the output are modified versions of the arrays resSamplesL, resSamplesCb and resSamplesCr.
- When at least one of tu_y_coded_flag[ xCb ][ yCb ], tu_cb_coded_flag[ xCb ][ yCb ], or tu_cr_coded_flag[ xCb ][ yCb ] is equal to 1, tu_y_coded_flag[ xCb ][ yCb ], tu_cb_coded_flag[ xCb ][ yCb ], and tu_cr_coded_flag[ xCb ][ yCb ] are set equal to 1.
…
8.5.1 General decoding process for coding units coded in inter prediction mode
…
- When cu_act_enabled_flag[ xCb ][ yCb ] is equal to 1, following steps applies:
…
- The residual modification process for residual blocks using colour space conversion as specified in clause 8.7.4.6 is invoked with the variable nTbW set equal to cbWidth, the variable nTbH set equal to cbHeight, the array rY set equal to resSamplesL, the array rCb set equal to resSamplesCb, and the array rCr set equal to resSamplesCr as inputs, and the output are modified versions of the arrays resSamplesL, resSamplesCb and resSamplesCr.
- When at least one of tu_y_coded_flag[ xCb ][ yCb ], tu_cb_coded_flag[ xCb ][ yCb ], or tu_cr_coded_flag[ xCb ][ yCb ] is equal to 1, tu_y_coded_flag[ xCb ][ yCb ], tu_cb_coded_flag[ xCb ][ yCb ], and tu_cr_coded_flag[ xCb ][ yCb ] are set equal to 1.
…

## Slide 7: Solution 2: Modify coded_flag when ACT is applied
8.8.3.5 Derivation process of boundary filtering strength
Otherwise, if the block edge is also a transform block edge, following applies:
  If cIdx is equal to 0 and the sample p0 or q0 is in a transform block which contains one or more non-zero transform coefficient levels coded with tu_y_coded_flag equal to 1, bS[ xDi ][ yDj ] is set equal to 1.
  Otherwise, if cIdx is equal to 1 and the sample p0 or q0 is in a transform block coded with tu_cb_coded_flag equal to 1, bS[ xDi ][ yDj ] is set equal to 1.
  Otherwise, if cIdx is equal to 2 and the sample p0 or q0 is in a transform block coded with tu_cr_coded_flag equal to 1, bS[ xDi ][ yDj ] is set equal to 1.

## Slide 8
Results (VTM-9.0, RA, QP37)

## Slide 9
Results (Prop, RA, QP37)

## Slide 10
Results (VTM-9.0, RA, QP37)

## Slide 11
Results (Prop, RA, QP37)