## Slide 1: Rice parameter selection for high bit depths
JVET-T0072
Advanced Technology Team
European Professional Engineering
Sony Europe BV
Adrian Browne
Sony Corp.

## Slide 2: Extending the range of Rice parameters in VVC
In VVC v1 the range of rice parameters that may be selected is restricted:
  0 -> 3 for regular residual coding (RRC)
  1 for transform skip residual coding (TSRC)
This restriction limits the range of residuals that can be encoded efficiently
For 8 / 10 bit at standard QPs this range is sufficient
  Not optimal for some 10 bit content at low QPs and lossless
For high bit depths the coding becomes more inefficient
  Dependent on magnitude of residuals
    Different types of content e.g. HDR and SDR may have different average residuals
      Due to tone curves
    Content may not be full range (e.g. medical)
      All zeros in MSBs

## Slide 3: Extending the range of Rice parameters in VVC
Outline of modification
  Derive initial Rice parameter by estimating coefficient size
  Compute scaled sum of local coefficient values
    Scaling based on derived Rice parameter
  Select a final Rice parameter using combination of scaled sum and the initial Rice parameter
Attributes of new algorithm
  Adaptive
    Global - uses previously coded residual coefficients in slice
    Local – uses adjacent coefficient values
  No reliance on bit depth
    No assumptions made on expected coefficient sizes
  Allows wider range of Rice parameter
  An extension of VVC v1 technique
    8 / 10 bit coding efficiency maintained

## Slide 4: Estimating coefficient size
Based on method from HEVC for computing rice value using array of counters
  Each counter can be mapped to a Rice parameter which represents latest estimate
  For each non-zero coefficient coded one counter is updated as follows:
    if (abs(value) > 0) {
    idx = calcIndex(isTS, scanPos); // index into the counters based on coefficient position and type
    count = riceCount[component][idx]; // riceCount is the counter array, reset to 0 for each slice
    rice = count >> 4;
    if (abs(value) >= (3 << rice)) { // value larger than expected range so increase count
    count += 4;
    } else if ((abs(value) << 1) < (1 << rice)) { // value smaller than expected range so decrease count
    count = Max(0, count - 1);
    }
    }

## Slide 5: Deriving the Rice parameter
Initial rice value is computed for every coded coefficient
rice = riceCount[component][idx] >> 4;
scaIing (a shift) is computed from this initial Rice value
  If rice is less than 3, scaling is 0 and coding will be same as VVC v1
    scaling = Max( 0, rice – 2 )
Compute the scaled and clipped sum of 5 previously coded local coefficients
  Identical to VVC v1 but with added scaling
    locSumAbs = Clip3( 0, 31, ( locSumAbs − baseLevel * 5 ) >> scaling )
  Note for TSRC, 5 previously coded local coefficients to the top left are used
Select the Rice parameter
  VVC v1 with addition of scaling to normalize result
    rice = g_auiGoRiceParsCoeff[idx] + scaling

## Slide 6: Simplification
The modification as described might introduce a latency
  The coding of a coefficient depends on the state of a counter which may be updated by the previously coded coefficient
  Prevents parallelization of coefficients coding
Suggested fix is to copy the state of riceCount at the beginning of a sub-block
  Use this copy when evaluating the value of rice
  Still increment / decrement riceCount when required
An alternative formulation of the simplification could be considered which uses the copied value for coding but not in the estimation phase.
Results for the simplification are included in the contribution

## Slide 7: Results – 12 and 16 bit vs VTM-10.0
 |  |  | AI-12 |  | 
 |  |  | Over VTM-10.0 |  | 
 | Y | U | V | EncT | DecT
SVT | -3.90% | -3.60% | -3.59% | 99% | 116%
PQ444 | -0.51% | -0.48% | -0.50% | 109% | 105%
PQ422 | -0.60% | -0.58% | -0.61% | 109% | 105%
Overall | -1.67% | -1.55% | -1.57% | 105% | 108%
 |  |  | AI-16 |  | 
 |  |  | Over VTM-10.0 |  | 
 | Y | U | V | EncT | DecT
SVT | -26.56% | -22.09% | -20.73% | 67% | 70%
Overall | -26.56% | -22.09% | -20.73% | 67% | 70%
Under test conditions defined in JVET-T0047 with extended precision disabled
Timings for SVT unreliable due to background operations on cluster
Gains over VTM-10.0
12-bit (where VTM-10.0 typically outperforms HM-16.22)
16 bit (where HM-16.22 typically outperforms VTM-10.0)

## Slide 8: Results – 10 bit CTC and low QP
 |  |  | AI - low QP |  | 
 | Over VTM10.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.05% | -0.04% | -0.03% | 105% | 107%
Class A2 | -0.07% | -0.12% | -0.12% | 106% | 108%
Class B | -0.12% | -0.16% | -0.20% | 105% | 102%
Class C | -0.24% | -0.20% | -0.24% | 107% | 100%
Class E | -0.19% | -0.46% | -0.52% | 104% | 105%
Overall | -0.14% | -0.19% | -0.22% | 105% | 104%
Class D | -0.30% | -0.36% | -0.38% | 107% | 103%
Class F | -1.55% | -1.29% | -1.35% | 104% | 101%
 |  |  | AI - CTC |  |  | 
 | Over VTM10.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.02% | -0.06% | 0.03% | 0.02% | 100% | 100%
Class A2 | 0.02% | 0.00% | -0.02% | 0.01% | 98% | 99%
Class B | 0.02% | 0.03% | 0.01% | 0.02% | 100% | 100%
Class C | -0.01% | 0.00% | -0.06% | -0.02% | 100% | 100%
Class E | 0.05% | -0.08% | 0.11% | 0.04% | 100% | 99%
Overall | 0.02% | -0.02% | 0.01% | 0.01% | 100% | 100%
Class D | 0.00% | -0.04% | 0.13% | 0.01% | 101% | 100%
Class F | -0.04% | -0.07% | -0.09% | -0.04% | 99% | 99%
For CTC the effect of the modification is minimal
For low QP there are gains for screen content

## Slide 9: Results – 8 / 10 bit lossless
YUV420 | All Intra |  | 
 | ratio |  | bit-rate savings
 | VTM-10.0 | T0072 | 
Class A1 | 2.4 | 2.4 | -0.61%
Class A2 | 1.8 | 1.8 | -1.47%
Class B | 2.3 | 2.3 | -0.22%
Class C | 2.1 | 2.1 | -0.13%
Class D | 2.1 | 2.1 | -0.22%
Class E | 3.1 | 3.1 | 0.06%
Class F | 5.8 | 5.8 | -0.57%
TGM | 12.4 | 13.0 | -4.65%
Overall | 2.3 | 2.3 | -0.43%
Enc Time[%] | 105% |  | 
Dec Time[%] | 112% |  | 
RGB | All Intra |  | 
 | ratio |  | bit-rate savings
 | VTM-10.0 | T0072 | 
TGM 1080p | 21.7 | 22.4 | -2.47%
TGM 720p | 10.1 | 10.1 | -0.26%
A | 6.0 | 6.0 | 0.05%
M | 6.0 | 6.0 | -0.57%
CC | 1.7 | 1.8 | -1.59%
Overall | 10.4 | 10.6 | -0.98%
Enc Time[%] | 104% |  | 
Dec Time[%] | 110% |  | 
YUV | All Intra |  | 
 | ratio |  | bit-rate savings
 | VTM-10.0 | T0072 | 
TGM 1080p | 21.3 | 21.6 | -1.32%
TGM 720p | 12.7 | 12.8 | -0.31%
A | 7.1 | 7.1 | -0.03%
M | 7.8 | 7.8 | -0.77%
CC | 2.0 | 2.0 | -0.85%
Overall | 11.6 | 11.6 | -0.66%
Enc Time[%] | 105% |  | 
Dec Time[%] | 108% |  | 
For lossless gains are present for 10 bit sources and screen content

## Slide 10: Conclusions
The proposed modification removes a restriction on Rice parameters in VTM-10
The modification extends the range of the existing VVC v1 technique
  Uses a coefficient estimation technique rather than relying on bit depth
  When coefficients are small, the coding is the same as the VVC v1
  Could further be constrained by a flag at the SPS or PPS level
Offers bd-rate gains when coefficients are larger
  12 and 16 bit SDR and HDR
  10 bit below CTC QPs
  10 bit lossless
Has no significant effect on bd-rate when coefficients are small
  10 bit CTC