## Slide 1: JVET-T0082 New HLG sequences for high bit-depth video coding
K. Kondo, M. Ikeda, A. Browne (Sony)
Notes: 1

## Slide 2: Summary of JVET-T0082
Introduce new HLG 12-bit test sequences
  5 test sequences
  Specifications of camera
Experiment
  Experimental encoding results
    VTM-10.0 compared to HM-16.22-Rext
    Tested as following a test condition in JVET-T0047.

## Slide 3: Camera specifications and contents creation
Spec. | 
Model/Manufacturer | CineAlta F65RS / Sony
Pickup device | Super 35mm equivalent Single-chip CMOS
Frame rate | 59.94fps, progressive
Bit depth | 16bit
Signal format | RGB RAW
RGB RAW
16-bit
Converter
(Sony internal tool)
Converter
(HDR-tools)
files
YUV 4:4:4
HLG
12-bit
files
files
YUV 4:2:2
HLG
12-bit
Alexis kindly helped us to use HDR-tools. Thanks to Alexis.
Config. file
444 to 422 Type 2

## Slide 4: Proposed HLG test sequences
Thumbnail | File name | Brief description
 | DayStreet_3840x2160_60p_12bit_444_hlg DayStreet_3840x2160_60p_12bit_422_hlg | Reflection on the glass of the cars and heat haze (fixed)
 | PeopleInShoppingCenter_3840x2160_60p_12bit_444_hlg PeopleInShoppingCenter_3840x2160_60p_12bit_422_hlg | People walking in shopping center (fixed)
 | NightStreet_3840x2160_60p_12bit_444_hlg NightStreet_3840x2160_60p_12bit_422_hlg | Reflection on the glass and the body of the cars (fixed)
 | SeaSurface_3840x2160_60p_12bit_444_hlg SeaSurface_3840x2160_60p_12bit_422_hlg | Birds flying around on the sea (fixed)
 | StainedGlass_3840x2160_60p_12bit_444_hlg StainedGlass_3840x2160_60p_12bit_422_hlg | Stained glass (tilting)

## Slide 5: DayStreet

## Slide 6: NightStreet

## Slide 7: PeopleInShoppingCenter

## Slide 8: SeaSurface

## Slide 9: StainedGlass

## Slide 10: Experimental results
Test condition: JVET-T0047.
  LMCS is OFF.
JVET-T0047
HLG
 |  |  | AI-12 Low-QP |  | 
 |  |  | Over HM-16.22-Rext |  | 
 | Y | U | V | EncT | DecT
HLG444 | -7.33% | -9.46% | -10.45% | 5649% | 190%
HLG422 | -7.51% | -12.66% | -12.77% | 4865% | 172%
Overall | -7.42% | -11.06% | -11.61% | 5243% | 181%
 |  |  | LDB-12 Low-QP |  | 
 |  |  | Over HM-16.22-Rext |  | 
 | Y | U | V | EncT | DecT
HLG444 | -5.02% | -7.68% | -8.06% | 1084% | 181%
HLG422 | -6.74% | -13.28% | -12.79% | 1499% | 171%
Overall | -5.88% | -10.48% | -10.42% | 1275% | 176%
 |  |  | RA-12 Low-QP |  | 
 |  |  | Over HM-16.22-Rext |  | 
 | Y | U | V | EncT | DecT
HLG444 | -5.96% | -9.61% | -9.98% | 1683% | 180%
HLG422 | -7.45% | -14.20% | -13.56% | 2138% | 178%
Overall | -6.70% | -11.91% | -11.77% | 1683% | 180%
The encoding runtime is not reliable.

## Slide 11: Conclusions
Introduced new HLG 12-bit test sequences
  5 test sequences for each 444 and 422.
    12-bit
    HLG
Proposal
  It is recommended to add new test sequences for HLG 12-bit into next common test condition.

## Slide 12
Notes: 12

## Slide 13: Experimental results
Test condition: QP range 22, 27, 32 and 37.
  LMCS is OFF.
 |  |  | AI-12 High-QP |  | 
 |  |  | Over HM-16.22-Rext |  | 
 | Y | U | V | EncT | DecT
HLG444 | -23.04% | -30.63% | -36.50% | 1999% | 215%
HLG422 | -23.10% | -53.03% | -53.55% | 2139% | 227%
Overall | -23.07% | -41.83% | -45.02% | 2162% | 216%
 |  |  | LDB-12 High-QP |  | 
 |  |  | Over HM-16.22-Rext |  | 
 | Y | U | V | EncT | DecT
HLG444 | -26.61% | -41.21% | -43.64% | 486% | 179%
HLG422 | -25.08% | -52.16% | -50.23% | 448% | 194%
Overall | -26.55% | -50.77% | -51.63% | 464% | 188%
 |  |  | RA-12 High-QP |  | 
 |  |  | Over HM-16.22-Rext |  | 
 | Y | U | V | EncT | DecT
HLG444 | -26.89% | -37.48% | -39.43% | 564% | 231%
HLG422 | -27.68% | -57.52% | -53.82% | 496% | 234%
Overall | -28.78% | -51.79% | -52.13% | 538% | 226%