## Slide 1
JVET-T0089
AHG12: Slice based Rice parameter selection for transform skip residual coding
Hong-Jheng Jhu, Xiaoyu Xiu, Yi-Wen Chen, Tsung-Chuan Ma, Che-Wei Kuo, Xianglin Wang

## Slide 2: Introduction & Proposed Modification
In residual coding of a transform skip block, the remainder of the absolute levels are binarized using fixed Rice parameter “1”
Significant performance degradation is reported in VVC high bit depth configuration
It is proposed to explicitly signal the rice parameter for each slice to indicate the rice parameter for the binary codewords of abs_remainder in transform skip residual coding
Rice parameter | Bit depth
4 | 12
6 | 14
8 | 16

## Slide 3: Simulation Results
Anchor: VTM-10.0 + ExtendedPrecision = 1 on SVT sequences
 |  |  | Intra 16-bit (internal bit depth) |  |  |  |  |  |  |  | 
 |  |  | Average BD-rate Change (%) - Medium Tier() |  |  | Average BD-rate Change (%) - High Tier |  |  | Average BD-rate Change (%) - All Tiers |  | 
 |  |  | Y/G | Cb/B | Cr/R | Y/G | Cb/B | Cr/R | Y/G | Cb/B | Cr/R
SVT |  |  | -14.8% | -14.9% | -14.9% | -37.9% | -38.1% | -38.0% | -27.3% | -27.2% | -27.4%
Encoding Time % |  |  | 96% |  |  | 80% |  |  | 88% |  | 
Decoding Time % |  |  | 98% |  |  | 100% |  |  | 99% |  | 
 |  |  | Intra 14-bit (internal bit depth) |  |  |  |  |  |  |  | 
 |  |  | Average BD-rate Change (%) - Medium Tier |  |  | Average BD-rate Change (%) - High Tier |  |  | Average BD-rate Change (%) - All Tiers |  | 
 |  |  | Y/G | Cb/B | Cr/R | Y/G | Cb/B | Cr/R | Y/G | Cb/B | Cr/R
SVT |  |  | -1.7% | -1.8% | -1.7% | -16.0% | -16.4% | -16.3% | -7.4% | -8.9% | -8.8%
Encoding Time % |  |  | 99% |  |  | 82% |  |  | 90% |  | 
Decoding Time % |  |  | 97% |  |  | 98% |  |  | 98% |  | 
 |  |  | Intra 12-bit (internal bit depth) |  |  |  |  |  |  |  | 
 |  |  | Average BD-rate Change (%) - Medium Tier |  |  | Average BD-rate Change (%) - High Tier |  |  | Average BD-rate Change (%) - All Tiers |  | 
 |  |  | Y/G | Cb/B | Cr/R | Y/G | Cb/B | Cr/R | Y/G | Cb/B | Cr/R
SVT |  |  | -0.1% | -0.1% | -0.1% | -2.4% | -2.6% | -2.5% | -1.1% | -1.2% | -1.2%
Encoding Time % |  |  | 94% |  |  | 82% |  |  | 88% |  | 
Decoding Time % |  |  | 94% |  |  | 100% |  |  | 97% |  | 
BD | Tier | QP values
16 | HT | -28, -31, -34, -37
16 | MT | -16, -19, -22, -25
14 | HT | -16, -19, -22, -25
14 | MT | -4, -7, -10, -13
12 | HT | -4, -7, -10, -13
12 | MT | 8, 5, 2, -1

## Slide 4: Summary
Recommend to establish one CE for studying rice parameter selection for transform skip mode at high bit-depth
Thanks Sony for cross-checking

## Slide 5: Thank you