## Slide 1
JVET-T0091
AHG12: Fix on encoder overflow issue of the LMCS at high bit-depth coding
Xiaoyu Xiu, Hong-Jheng Jhu, Yi-Wen Chen, Tsung-chuan Ma,Xianglin Wang

## Slide 2: Proposal
LMCS parameter calculation for SDR in VTM-10.0
  The variance in the neighborhood of each luma sample is used to calculate the LMCS piece-wise linear function
  When the macro RExt_HIGH_BIT_DEPTH_SUPPORT is enabled, the data type used for the intermediate variables during the LMCS derivation is 32-bit
  Such precision is not sufficient when the internal bit-depth is 16-bit
Solution
  Extend the dynamic range of some intermediate parameters from 32-bit to 64-bit
  Merge request will be submitted if requested.

## Slide 3: Simulations
Tested on top of VTM-10.0, 16-bit coding
The macro JVET_R0351_HIGH_BIT_DEPTH_ENABLED is ENABLED
--ExtendedPrecision=1

## Slide 4: Simulations
VTM-10.0 Anchor
Proposed fixes

## Slide 5: Thank you