## Slide 1
JVET-T0094
AHG11: In-loop filtering based on neutral network
T.-C. Ma, W. Chen, X. Xiu, Y.-W. Chen, H.-J. Jhu, C.-W. Kuo, X. Wang

## Slide 2: Introduction
Neural network (NN) based in-loop filter
Proposed NN filter placed
between de-blocking and SAO
Entropy Decode
Inv. Quant.
Inv.
Trans.
Memory
Intra/Inter
Mode Sel.
Intra Prediction
Motion
Comp.
DB
NN Filter
SAO
ALF/CCALF
Pic.
Buffer
Bitstream
Video
Out

## Slide 3: Proposed NN in-loop filter
One NN filter for both luma and chroma samples
N and K is set equal to 20 and 64, respectively

## Slide 4: Training Process
Data set : DIV2k training set, 800 images are converted to YUV420
QP : 22, 27, 32, 37
VTM9.0 reconstructed images are split into 128x128 sub-images
Batch size : 8
Epoch : 20
Machine learning library: pytorch

## Slide 5: Simulation Result
Anchor: VTM9.0
Only the frame in first 2 intra period are used for each sequence
Both anchor and test are generated in CPU
 |  |  | All Intra |  | 
 |  |  | Over VTM9.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -3.61% | -10.86% | -13.64% | 1901% | 996565%
Class A2 | -4.14% | -15.29% | -16.62% | 850% | 743219%
Class B | -4.49% | -17.88% | -18.15% | 850% | 785819%
Class C | -5.76% | -19.18% | -20.71% | 478% | 563704%
Class E | -7.03% | -16.81% | -15.94% | 976% | 939230%
Overall | -4.99% | -16.39% | -17.34% | 875% | 775056%
Class D | -6.64% | -18.22% | -21.60% | 500% | 644479%
Class F | -3.29% | -15.75% | -15.50% | 430% | 700323%
 |  |  | Random Access |  | 
 |  |  | Over VTM9.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -3.90% | -9.57% | -13.03% | 207% | 866536%
Class A2 | -4.48% | -18.40% | -18.85% | 191% | 506881%
Class B | -3.82% | -22.21% | -18.07% | 205% | 702260%
Class C | -3.65% | -19.09% | -16.99% | 171% | 1000062%
Class E |  |  |  |  | 
Overall | -3.92% | -18.09% | -16.93% | 193% | 754013%
Class D | -3.80% | -19.34% | -18.37% | 187% | 641745%
Class F | -1.91% | -11.57% | -11.72% | 278% | 596299%

## Slide 6
Network Information in Training Stage |  | 
Mandatory | HW environment: | CPU: Intel(R) Xeon(R) Gold 5120 CPU @ 2.20GHz, 40GB memory GPU: NVIDIA GeForce RTX 2080
 | SW environment: | Ubuntu 16.04.6 CUDA Version:10.2, Driver Version: 430.14
 | Framework: | Pytorch 1.4
 | Epoch: | 20
 | Batch size: | 8
 | Training time: | 30h
 | Training data information: | DIV2K
 | Configurations for generating compressed training data (if different to VTM CTC): | QP values: 22, 27, 32, 37

## Slide 7
Network Information in Inference Stage |  | 
Mandatory | HW environment: | Intel(R) Xeon(R) CPU E5-2680 v4 @ 2.40GHz No GPU
 | SW environment: | CentOS Linux 7
 | Framework: | Libtorch 1.5
 | Total Conv. Layers | 46
 | Total FC Layers | 0
 | Total Parameter Number | 1,554,579
 | Parameter Precision | 32(F)
 | Memory Parameter (MB) | 5.93 MB
 | Memory Temp (MB) | 4 (input size 128x128)
 | MAC (Giga) | 23 (input size 128x128)

## Slide 8: Thank you