## Slide 1: T0128: Preliminary results of Neural Network Loop Filter
Zhao Wang, Ru-Ling Liao, Changyue Ma, Yan Ye (Alibaba)
Shanshe Wang, Siwei Ma (Peking Univ.)

## Slide 2: Network Architecture
ResNet
  64 layers
  64 channels for internal convolutional layers
  3x3 kernel (~2.4 million parameters)
  ReLU is used as the activation funtion

## Slide 3: Input/Output
Input:
  YUV444
  Up-sampled from YUV420 for chroma components
  Up-sample: copy from neighbouring sample
Output:
  YUV444
  Down-sampled from YUV444 to YUV420
  Down-sample: save the left-top sample for each 2x2 chroma block

## Slide 4: Training
Model number
  4 models
  Training data collected according to input QP
  {20-27, 28-32, 33-37, 38-45}
Training
  Vimeo90K [1]
  Adam
  Learning rate (0.0001)
  ~0.4 million iterations (40h on TelsaV100-32G)
[1] Xue T, Chen B, Wu J, et al. Video enhancement with task-oriented flow[J]. International Journal of Computer Vision, 2019, 127(8): 1106-1125.

## Slide 5: Inference
on VTM9.3
  Between SAO and ALF
  CTU flag
  The model is selected based on the frame-level QP
  Whole frame is filtered and only the signaled CTU is changged
  Pytorch/Libtorch

## Slide 6: Results/Future Work
Experimental results
  Random Access, QPs (27, 32, 37, 42), Class B
Future Work
  Expanding the test seq and AI configuration
  Reduce the complexity
 | Y | U | V
MarketPlace | -4.65% | -13.59% | -19.15%
RitualDance | -7.45% | -14.42% | -14.14%
Cactus | -5.47% | -14.47% | -12.50%
BasketballDrive | -5.96% | -12.30% | -13.11%
BQTerrace | -4.31% | -7.97% | -9.20%
Overall | -5.57% | -12.55% | -13.62%