## Slide 1: GOP-Based Temporal Filter Improvements
JVET-V0056: [AHG10] GOP-based temporal filter improvements
Per Wennersten
Ericsson

## Slide 2: Agenda
Recap
Update since last meeting

## Slide 3: Existing temporal filter
Motivation: if a coded pixel value is re-used in several frames, its optimal value is the average of the original in those frames
Filters frames 0, 8, 16, …
When possible, uses two frames before and after
  Motion compensation on these frames to match frame to be filtered
Filter using five collocated pixels based on intensity difference, QP and POC
Creates new original pictures for encoder, but final PSNR still measured against unfiltered original

## Slide 4: Block error weighting
Modify filter weights based on absolute and relative different of blocks

## Slide 5: Block frequency weighting
Modify filter weight based on frequency metric. Higher frequencies -> stronger filter

## Slide 6: Reference frame weighting
Higher weights on reference frames with better match during motion estimation
Double number of neighboring frames used for filtering

## Slide 7: Misc. changes
Tweaked motion estimation to be less complex and give slightly improved compression performance
Re-optimized various parameters

## Slide 8: Results
 | Over VTM-12.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.83% | -1.86% | -2.55% | 93% | 95%
Class A2 | -1.07% | -0.78% | -0.79% | 97% | 104%
Class B | -1.40% | -0.95% | -0.98% | 95% | 93%
Class C | -1.19% | -0.57% | -0.30% | 98% | 109%
Class E |  |  |  |  | 
Overall | -1.36% | -1.00% | -1.08% | 96% | 100%
Class D | -1.48% | -0.09% | -0.15% | 99% | 106%
Class F | 0.00% | 0.00% | 0.00% | 96% | 119%
 | Over VTM-12.0 with MCTF = 0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -4.54% | -8.89% | -8.66% | -4.54% | -8.89%
Class A2 | -6.21% | -10.83% | -10.59% | -6.21% | -10.83%
Class B | -7.66% | -9.17% | -9.39% | -7.66% | -9.17%
Class C | -2.82% | -4.37% | -3.86% | -2.82% | -4.37%
Class E |  |  |  |  | 
Overall | -5.45% | -8.17% | -8.01% | -5.45% | -8.17%
Class D | -0.81% | -3.53% | -3.47% | -0.81% | -3.53%
Class F | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Note: enc/dec times are unreliable

## Slide 9: Updates
Code was uploaded for review
Bug fix regarding motion compensation of blocks along the edge of a picture
Subjective viewing showed equal or better quality than old filter
JVET-V0057 built on top
HM version implemented:
 | Random Access Main 10 |  | 
 | Y | U | V
Class A1 | -1.4% | -1.5% | -1.8%
Class A2 | -1.1% | -1.1% | -1.2%
Class B | -1.6% | -1.8% | -1.7%
Class C | -1.0% | -0.9% | -1.0%
Class D | -1.0% | -0.8% | -0.6%
Class E |  |  | 
Class F | 0.0% | 0.0% | 0.0%
Overall | -1.0% | -1.0% | -1.0%
 | -1.0% | -1.0% | -1.0%
Enc Time[%] | 107% |  | 
Dec Time[%] | 100% |  |