## Slide 1
JVET-V0067
A constraint of max transform size for high bit depth and high bit rate coding
Kenji Kondo, Masaru Ikeda (Sony)

## Slide 2: Summary
Introduce an issue
  A large transformation increases a cost of hardware.
  JVET-U0063
    Further study after re-defining a new CTC.
Proposed solution
  A constraint to restrict max transform size to 32.
Experiment
  Log2MaxTbSize : 5
Conclusion
  Small impact BD-rate
  Propose the above constraint

## Slide 3: Issue: Storage cost for large transform and high bit depth
Need buffers corresponding to max size of transform.
  For high bit depth, the memory size more increases.
Related topics
  Low QPs for high bit depth coding
    To keep high quality for HBD content, low QPs are used as a HBD CTC.
    At low QPs range, small coding loss is expected even without large transform.
  64-point transform
    Max size of transform in VVC
    A technique, zero-out is used.
Dequantization
Vertical Transform
Horizontal Transform
CABAC
Mem.
3
Mem.
2
Reconstruct
1
32x64
64x64
32x32

## Slide 4: Complexity analysis (memory 2)
Cases
  VVC v1
    10-bit input
      32 x 64 x 16 bit (+0%)
  VVC v2
    16-bit input
      32 x 64 x 23 bit (+43%) Additional cost to use 64-point transform and HBD.
    12-bit input
      32 x 64 x 16 bit (+0%)
  VVC v2 + constraint (sps_max_luma_transform_size_64_flag = 0)
    16-bit input
      32 x 32 x 23 bit (-28%)
    12-bit input
      32 x 32 x 16 bit (-50%)
HEVC spec:
extended_precision_processing_flag equal to 1 specifies that an extended dynamic range is used for transform coefficients and transform processing. extended_precision_processing_flag equal to 0 specifies that the extended dynamic range is not used. When not present, the value of extended_precision_processing_flag is inferred to be equal to 0.
The variables CoeffMinY, CoeffMinC, CoeffMaxY and CoeffMaxC are derived as follows:
CoeffMinY = −( 1 << ( extended_precision_processing_flag ? Max( 15, BitDepthY + 6 ) : 15 ) ) (7-27)
CoeffMinC = −( 1 << ( extended_precision_processing_flag ? Max( 15, BitDepthC + 6 ) : 15 ) ) (7-28)
CoeffMaxY = ( 1 << ( extended_precision_processing_flag ? Max( 15, BitDepthY + 6 ) : 15 ) ) − 1 (7-29)
CoeffMaxC = ( 1 << ( extended_precision_processing_flag ? Max( 15, BitDepthC + 6 ) : 15 ) ) − 1 (7-30)
Note: If the chip supports both v1 and v2, the storage size becomes the same as v1.

## Slide 5: Complexity analysis (memory 3)
Cases
  VVC v1
    10-bit input
      64 x 64 x 11 bit (+0%)
  VVC v2
    16-bit input
      64 x 64 x 17 bit (+54%) Additional cost to use 64-point transform and HBD.
    12-bit input
      64 x 64 x 13 bit (+18%) Additional cost to use 64-point transform and HBD.
  VVC v2 + constraint (sps_max_luma_transform_size_64_flag = 0)
    16-bit input
      32 x 32 x 17 bit (-61%)
    12-bit input
      32 x 32 x 13 bit (-70%)
Note: If the chip supports both v1 and v2, the storage size becomes the same as v1.

## Slide 6: Proposed solution
Propose a constraint
  For high bit depth and high bit rate coding,
    To save hardware cost, restrict max transform size to 32.
    sps_max_luma_transform_size_64_flag sets equal to 0.
Experiment
  Anchor
    Follow HBD CTC
  Test
    Log2MaxTbSize : 5
Cross checking
  JVET-V0159
  Thank Sharp for the cross checking.

## Slide 7: Experimental results – Low QP
HDR PQ |  |  | AI |  |  |  |  | 
 |  |  | Over VTM12.0 |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 0.01% | 0.03% | 0.03% | 0.01% | 0.03% | 0.03% | 101% | 101%
PQ422 | 0.01% | 0.08% | 0.04% | 0.01% | 0.08% | 0.04% | 101% | 100%
Overall | 0.01% | 0.06% | 0.03% | 0.01% | 0.05% | 0.04% | 101% | 100%
 |  |  | LDB |  |  |  |  | 
 |  |  | Over VTM12.0 |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 100% | 100%
PQ422 | 0.01% | 0.01% | 0.00% | 0.00% | 0.00% | 0.00% | 103% | 99%
Overall | 0.00% | 0.01% | 0.00% | 0.00% | 0.00% | 0.00% | 102% | 100%
 |  |  | RA |  |  |  |  | 
 |  |  | Over VTM12.0 |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 0.00% | 0.01% | -0.01% | 0.00% | 0.01% | -0.01% | 100% | 100%
PQ422 | 0.01% | 0.01% | 0.01% | 0.00% | 0.00% | 0.01% | 102% | 100%
Overall | 0.01% | 0.01% | 0.00% | 0.00% | 0.01% | 0.00% | 101% | 100%
Overall PQ | 0.01% | 0.02% | 0.01% | 0.00% | 0.02% | 0.01% | 101% | 100%
HDR HLG |  |  | AI |  | 
 |  |  | Over VTM12.0 |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | 0.00% | 0.00% | 0.00% | 103% | 100%
HLG422 | 0.01% | 0.00% | 0.00% | 102% | 100%
Overall | 0.00% | 0.00% | 0.00% | 102% | 100%
 |  |  | LDB |  | 
 |  |  | Over VTM12.0 |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | -0.01% | 0.00% | 0.00% | 101% | 100%
HLG422 | 0.00% | 0.02% | 0.00% | 102% | 99%
Overall | 0.00% | 0.01% | 0.00% | 102% | 100%
 |  |  | RA |  | 
 |  |  | Over VTM12.0 |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | -0.01% | 0.01% | 0.01% | 104% | 100%
HLG422 | 0.00% | 0.00% | -0.02% | 102% | 100%
Overall | 0.00% | 0.01% | -0.01% | 103% | 100%
Overall HLG | 0.00% | 0.01% | 0.00% | 102% | 100%
For low QP, the coding efficiency loss is negligible.
The transform size 64 is not necessary at low QP range.

## Slide 8: Experimental results – Normal QP
 | Random Access |  |  |  |  |  |  |  |  | 
 | Over VTM-12.0 |  |  |  |  |  |  |  |  | 
 |  |  | wPSNR |  |  | PSNR |  |  |  | 
 | DE100 | PSNR-L100 | Y | U | V | Y | U | V | EncT | DecT
Class H1 | 8.16% | 0.63% | 0.26% | 5.87% | 5.90% | 0.22% | 5.39% | 5.40% | 102% | 102%
Class H2 |  |  |  |  |  | 0.47% | 3.51% | 3.89% | 96% | 103%
Overall | 8.16% | 0.63% | 0.26% | 5.87% | 5.90% | 0.35% | 4.45% | 4.64% | 99% | 102%
 | All Intra |  |  |  |  |  |  |  |  | 
 | Over VTM-12.0 |  |  |  |  |  |  |  |  | 
 |  |  | wPSNR |  |  | PSNR |  |  |  | 
 | DE100 | PSNR-L100 | Y | U | V | Y | U | V | EncT | DecT
Class H1 | 9.68% | 0.58% | 0.13% | 9.22% | 9.44% | 0.11% | 8.47% | 8.44% | 102% | 102%
Class H2 |  |  |  |  |  | 0.15% | 3.69% | 4.42% | 103% | 101%
Overall | 9.68% | 0.58% | 0.13% | 9.22% | 9.44% | 0.13% | 6.08% | 6.43% | 103% | 101%
For normal QP, loss was confirmed.

## Slide 9: Conclusion
Introduced an issue of this contribution
  A large transform Increases memory size and cost.
Proposed a constraint for high bit depth
  For high bit depth and high bit rate coding
  sps_max_luma_transform_size_64_flag sets equal to 0.
Showed experimental results
  Tested “Log2MaxTbSize : 5”
  Negligible loss for low QP tests
  Loss was confirmed for normal QP tests

## Slide 11: Experimental results
For RGB contents, an anchor sets “Log2MaxTbSize : 5”.
Test results become the same as anchor.
SVT RGB |  |  | AI |  | 
 |  |  | Over VTM12.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.00% | 0.00% | 0.00% | 100% | 100%
SVT12 | 0.00% | 0.00% | 0.00% | 97% | 100%
Overall | 0.00% | 0.00% | 0.00% | 99% | 100%
 |  |  | LDB |  | 
 |  |  | Over VTM12.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.00% | 0.00% | 0.00% | 106% | 100%
SVT12 | 0.00% | 0.00% | 0.00% | 105% | 100%
Overall | 0.00% | 0.00% | 0.00% | 105% | 100%
 |  |  | RA |  | 
 |  |  | Over VTM12.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.00% | 0.00% | 0.00% | 104% | 100%
SVT12 | 0.00% | 0.00% | 0.00% | 103% | 100%
Overall | 0.00% | 0.00% | 0.00% | 104% | 100%
Overall RGB | 0.00% | 0.00% | 0.00% | 103% | 100%