## Slide 1: AHG12: Extensions to CCALF
JVET-V0080
Advanced Technology Team
European Professional Engineering
Sony Europe BV.
Steve Keating
Sony Group Corp.

## Slide 2: Introduction
  JVET-U0100 included extensions to ALF but not to CCALF
  CCALF could also be extended

## Slide 3: CCALF Extension
  VVC currently has a choice of 4 filters per colour component
    This could be increased to 8:
 | 8sets Over U0100 |  | 
 | Y | U | V
Class A1 | 0.04% | -0.43% | -0.55%
Class A2 | 0.05% | -0.65% | -1.76%
Class B | 0.06% | -1.54% | -0.91%
Class C | 0.05% | -0.18% | -0.17%
Class E | 0.03% | -0.26% | 0.42%
Overall | 0.05% | -0.69% | -0.61%
Class D | 0.01% | -0.14% | -0.08%
Class F | 0.04% | -0.34% | -0.30%
Class TGM | 0.02% | -0.15% | -0.18%

## Slide 4: CCALF Extension
  The filter size could also be increased from 7 to, e.g., 11 taps:
 | 11tapType0 8sets Over U0100 |  | 
 | Y | U | V
Class A1 | 0.07% | -0.65% | -1.98%
Class A2 | 0.06% | -1.73% | -2.89%
Class B | 0.09% | -2.77% | -2.38%
Class C | 0.11% | -0.75% | -0.66%
Class E | 0.13% | -1.90% | -0.78%
Overall | 0.09% | -1.65% | -1.75%
Class D | 0.02% | -0.76% | -0.31%
Class F | 0.10% | -1.20% | -0.96%
Class TGM | 0.06% | -0.97% | -0.61%

## Slide 5: CCALF Filter Shape
  The filter shape is suited to Type 0 chroma
 |  | T0 |  | 
 | T1 | C | T2 | 
 | T3 | T4 | T5 | 
 |  | T6 |  | 
 |  | T0 |  | 
T7 | T1 | C | T2 | T8
T9 | T3 | T4 | T5 | T10
 |  | T6 |  | 

## Slide 6: CCALF Filter Shape
  Some improvement is achieved by changing the filter shape:
 | T9 | T0 | T10 | 
T7 | T1 | C | T2 | T8
 | T3 | T4 | T5 | 
 |  | T6 |  | 
 |  | T0 |  | 
T7 | T1 | C | T2 | T8
T9 | T3 | T4 | T5 | T10
 |  | T6 |  | 
Type 0
Type 2

## Slide 7: CCALF Filter Shape
  For Type 0 content (JVET-M1010)
 | 11tap Type0 8sets Over U0100 |  | 
 | Y | U | V
Class A1 | 0.07% | -0.65% | -1.98%
Class A2 | 0.06% | -1.73% | -2.89%
Class B | 0.09% | -2.77% | -2.38%
Class C | 0.11% | -0.75% | -0.66%
Class E | 0.13% | -1.90% | -0.78%
Overall | 0.09% | -1.65% | -1.75%
Class D | 0.02% | -0.76% | -0.31%
Class F | 0.10% | -1.20% | -0.96%
Class TGM | 0.06% | -0.97% | -0.61%
 | 11tap Type2 8sets Over U0100 |  | 
 | Y | U | V
Class A1 | 0.07% | -0.62% | -2.05%
Class A2 | 0.06% | -1.75% | -3.02%
Class B | 0.09% | -2.70% | -2.26%
Class C | 0.11% | -0.70% | -0.60%
Class E | 0.13% | -1.50% | -0.74%
Overall | 0.09% | -1.55% | -1.73%
Class D | 0.02% | -0.69% | -0.20%
Class F | 0.11% | -1.26% | -1.00%
Class TGM | 0.06% | -1.13% | -0.82%

## Slide 8: CCALF Filter Shape
  For Type 2 content (JVET-U2018-STDQP)
 | 11tap Type0 8sets over U0100 |  |  |  |  | 
 | wPSNR |  |  | PSNR |  | 
 | Y | U | V | Y | U | V
Class H1 | 0.10% | -1.24% | -3.19% | 0.10% | -1.34% | -3.06%
Class H2 |  |  |  | 0.06% | -1.79% | -0.94%
Overall | 0.10% | -1.24% | -3.19% | 0.08% | -1.57% | -2.00%
 | 11tap Type2 8sets over U0100 |  |  |  |  | 
 | wPSNR |  |  | PSNR |  | 
 | Y | U | V | Y | U | V
Class H1 | 0.10% | -1.42% | -3.67% | 0.10% | -1.51% | -3.55%
Class H2 |  |  |  | 0.06% | -1.82% | -0.89%
Overall | 0.10% | -1.42% | -3.67% | 0.08% | -1.66% | -2.22%

## Slide 9: Conclusion
  We should consider extending CCALF
    Choice of more filters
    Use more filter taps
    Use a different filter shape for Type0 and Type2 chroma