## Slide 1: JVET-V0093 AHG9:Film grain estimation and film grain synthesis for VVC Film grain characteristics SEI message, film grain estimation and film grain synthesis modules
Miloš Radosavljević, Edouard François (Interdigital)
Wassim Hamidouche, Thomas Amestoy, Guillaume Gautier (INSA)
April 2021

## Slide 2: Proposal
Proposal is related with
  Film grain characteristics SEI message
  Film grain synthesis module
  Film grain analysis (parameter estimation) module
Film grain is sometimes referred as desirable noise
Film grain is a desirable feature in video production
Film grain can be used as a tool to mask compression artifacts
  Which leads to increased subjective video quality

## Slide 3: General framework
General framework of the proposed contribution
Analysis and synthesis are not mandatory
Complete framework is in conformance with standardized syntax
The model we use is bit-exact, and complete framework is bit-exact
To model film grain, this contribution uses
  SMPTE RDD 5 specification (directly defines synthesis part)
  Specification is based on frequency filtering model
  Additive blending mode

## Slide 4: SMPTE RDD 5 Specification
FGC-SEI Params
Decoded samples
Video stream
VVC video decoder
Decoded frame
Video Output
Select Film grain params
8x8 grain block selection
Film grain Database
Uniform pseudo-Random Number generator
De-blocking
Compute 8x8 block average
Previous 8x8 block
RDD 5 defines film grain synthesis part
Database of film grain patterns
Uniform pseudo-random number generator
And complete and precise sequence of operations

## Slide 5: SMPTE RDD 5 Specification
Film grain is content dependent
Hence RDD 5 model supports different intensity intervals for FG
  Different film grain parameters for different intensity
  Parameters are accessed based on block average
  Parameters are used to access film grain database (if database is created off-line) or to create film grain patterns (on-fly)
FGC-SEI Params
Decoded samples
Video stream
VVC video decoder
Decoded frame
Video Output
Select Film grain params
8x8 grain block selection
Film grain Database
Uniform pseudo-Random Number generator
De-blocking
Compute 8x8 block average
Previous 8x8 block

## Slide 6: SMPTE RDD 5 Specification
To create film grain pattern (film grain database), start from predefined transformed block of Gaussian random numbers
  Predefined in RDD 5
  Already in transformed domain
  RDD 5 uses internal DCT transform
  Block size 64x64
FGC-SEI Params
Decoded samples
Video stream
VVC video decoder
Decoded frame
Video Output
Select Film grain params
8x8 grain block selection
Film grain Database
Uniform pseudo-Random Number generator
De-blocking
Compute 8x8 block average
Previous 8x8 block

## Slide 7: SMPTE RDD 5 Specification
Based on model parameters – Vertical and horizontal cut-off frequency
VVC’s DCT-2 64x64 can be used instead of RDD 5 internal transform
Vertical cut-off frequency
Horizontal cut-off frequency
INVERSE DCT

## Slide 8: SMPTE RDD 5 Specification
From 64x64 pseudo-randomly select 8x8 block (blending is done on 8x8 block)
Scale it based on parameter from FGC SEI
Blend it to frame
  Additive blending
SMPTE RDD 5 defines more precisely all steps

## Slide 9: Film Grain Analysis
PRE-PROCESSING
FG PARAMETER ESTIMATION
To create map that indicates flat regions of an input frame
  We use Canny edge detector on two scales, in combination with morphological operations
For filtering we use MCTF
  We created additional instance of EncTemporalFilter class
  Encoding process is unchanged – we use internal picture buffer for FG filtering
  For LD only on first frame
  AI on all frames
  RA per I period
  Strength of filter is set to 1.5
Filtered frame is used to find
film grain image (film grain estimate)

## Slide 10: Film Grain Analysis
PRE-PROCESSING
FG PARAMETER ESTIMATION
Variance is used as scaling factor for film grain block before blending
Found over all available 64x64 blocks
  Blocks that belong to the flat regions of an input frame

## Slide 11: Film Grain Analysis
For cut-off frequencies, we need to go in transform domain
We use VVC’s DCT-2 64x64
  Which replaces RDD 5 transform
FORWARD DCT
Average vectors

## Slide 12: Film Grain Analysis
Index of the intersection point is estimated cut-off frequency
For the current RDD 5 spec
  cut-off frequency is scaled down to fit range of the parameter defined in the spec

## Slide 13: Software
For both synthesis and analysis part
Code is initial version and there is space for improvement
  We would appreciate comments from the community
Code will be provided

## Slide 14: Results
Original

## Slide 15: Results
Reconstructed+FG, Qp=37

## Slide 16: Results
Reconstructed, Qp=37

## Slide 17
Original
Decoded+FG
Decoded

## Slide 18: Results
Original Reconstructed+FG, Qp 37 Reconstructed, Qp 37

## Slide 19: Conclusions
Film grain is good candidate to be considered for future use in VVC and VTM reference software.
  It is reported that the visual quality benefits from the synthesized film grain
    tool for subjective quality enhancement of compressed video
  It may be relevant to make the FG synthesis and blending process more precisely specified, in order to guaranty reproducibility of the process
  It may be relevant to make the FG synthesis and blending process mandatory, when the FG SEI is inserted in the bitstream
    Mandatory post-processing
  We propose to incorporate the software update in the VTM fork for future study

## Slide 20: Acknowledgment
Thanks to Dolby for cross-checking (JVET-V0151)
We note that part of the code is based on previous Dolby’s contribution
This work has been achieved in the context of the 3EMS project funded by the “Region Bretagne”