## Slide 1
AHG8: Signaling TSRC rice parameter in slice header extension
(JVET-W0055)
T. Tsukuba, M. Ikeda, T. Suzuki

## Slide 2: Motivation
VVC ver.1 has an extension field, called slice header extension, in slice header.
  It is useful to add new syntax elements to the slice header which can be ignored by a version 1 decoder but used by a future version decoder.
In WD for VVC ver.2, TSRC rice parameter can be signaled in slice header but not in slice header extension
  It may lose backward compatibility between VVC ver.1 and VVC ver.2
    Ex. Stream merger or parcat for ver.1 may not parse the current slice header in VVC ver.2.
… | 
if( sps_transform_skip_enabled_flag && !sh_dep_quant_used_flag && !sh_sign_data_hiding_used_flag ) | 
sh_ts_residual_coding_disabled_flag | u(1)
if( !sh_ts_residual_coding_disabled_flag && sps_ts_residual_coding_rice_present_in_sh_flag ) | 
sh_ts_residual_coding_rice_idx_minus1 | u(3)
if( pps_slice_header_extension_present_flag ) { | 
sh_slice_header_extension_length | ue(v)
for( i = 0; i < sh_slice_header_extension_length; i++) | 
sh_slice_header_extension_data_byte[ i ] | u(8)
} | 
… | 
yellow: syntaxes related to TSRC rice parameter
green: syntax related to slice header extension
Syntax table of slice header

## Slide 3: Proposal
Considering the motivation of slice header extension, it is natural to signal TSRC rice parameter in slice header extension.
Changes
  Move sh_ts_residual_coding_rice_idx_minus1 to slice header extension
  Add a syntax slice_header_exntension_data_bit and a function more_data_in_slice_header_extension() to represent the remining bits of slice header extension
    Inherit from HEVC
… | 
if( sps_transform_skip_enabled_flag && !sh_dep_quant_used_flag && !sh_sign_data_hiding_used_flag ) | 
sh_ts_residual_coding_disabled_flag | u(1)
if( !sh_ts_residual_coding_disabled_flag && sps_ts_residual_coding_rice_present_in_sh_flag ) | 
sh_ts_residual_coding_rice_idx_minus1 | u(3)
if( pps_slice_header_extension_present_flag ) { | 
sh_slice_header_extension_length | ue(v)
for( i = 0; i < sh_slice_header_extension_length; i++) | 
sh_slice_header_extension_data_byte[ i ] | u(8)
if( !sh_ts_residual_coding_disabled_flag && sps_ts_residual_coding_rice_present_in_sh_flag ) | 
sh_ts_residual_coding_rice_idx_minus1 | u(3)
while ( more_data_in_slice_header_extension() ) | 
slice_header_extension_data_bit | u(1)
} | 
… | 
slice_header_extension_data_bit could have any value. Its presence and value do not affect the decoding process specified in this version of this Specification. Decoders conforming to this version of this Specification shall ignore the values of all the slice_header_extension_data_bit syntax elements. Its value does not affect the decoding process specified in this version of specification.
more_data_in_slice_header_extension( ) is specified as follows:
– If ( the current position in the slice_header( ) syntax structure ) − ( the position immediately following slice_header_extension_length ) is less than ( slice_header_extension_length * 8 ), the return value of more_data_in_slice_header_extension( ) is equal to TRUE.
– Otherwise, the return value of more_data_in_slice_header_extension( ) is equal to FALSE

## Slide 4: Conclusion
This contribution proposes to signal sh_ts_residual_coding_rice_idx_minus1 in slice header extension.
  It is useful to make the slice header backward-compatible between VVC ver.1 and VVC ver.2.
A patch for this changes is attached.
It is recommended to adopt this cleanup to the next version of WD and VTM.