## Slide 1
JVET-W0060
AHG8: A constraint of max CTU size and tile on WPP for high bit rate coding
Kenji Kondo, Masaru Ikeda (Sony)

## Slide 2: Outline
Introduce an issue
  Throughput case analysis for 4K HLG contents
  When WPP is used, a large CTU may make a CABAC throughput worse.
Proposed solution
  restrict max CTU size to 64 or CTU row split.
Experiment
  WPP: 1 (sps_entropy_coding_sync_enabled_flag = 1)
    CTU size: 64
    Tile: 2x1
Conclusion
  Propose to have the constraint

## Slide 3: Bins statistics and estimated parsing time
QP | EP bins | Context bins | ctxbins+epbins/2 | ctxbins+epbins/4
-13 | 98649680 | 52236665 | 101554671 | 76892251
-8 | 75615675 | 50843571 | 88642450 | 69743010.5
-3 | 54646068 | 47561968 | 74882491.5 | 61222229.75
2 | 40957725 | 41768709 | 62237056.5 | 52002882.75
7 | 27320531 | 35501232 | 49161497.5 | 42331364.75
12 | 16103422 | 30186968 | 38222286.5 | 34204627.25
 | Parse time [ms] | 
QP | ctxbins+epbins/2 | ctxbins+epbins/4
-13 | 203.1 | 153.8
-8 | 177.3 | 139.5
-3 | 149.8 | 122.4
2 | 124.5 | 104.0
7 | 98.3 | 84.7
12 | 76.4 | 68.4
Encode HLG 4K contents using AI config
Find the max # of bins in one frame
Illustrated the number of bins
Estimate the time to finish parsing
  Clock frequency: 500 MHz
  1 context bin + 2 or 4 EP bins / clock
60 fps

## Slide 4: The issue of parallel parsing with WPP
For VVC, max CTU size was extended to 128 from HEVC.
One entropy slice becomes bigger because of large CTU size.
  It’s illustrated below.
The time for parsing becomes longer.
  It would make a real time playback difficult.
CTU rows
…
Many bits may be concentrated into specific CTU rows.
…
CTU size: 64
CTU size: 128

## Slide 5: Proposed solution
Propose a constraint
  Restrict max CTU size to 64, which is the same as HEVC.
  Split CTU rows by tiling
Experiment
  Anchor
    CTC for HBD and high bit rate coding
  Test
    (Test-1) WPP: 1
    (Test-2) WPP: 1 and CTU size : 64
    (Test-3) WPP: 1 and Tile: 2x1
  QP range
    Additionally, other QP ranges were tested.
      {-8 to 12}, {-3 to 22} and {2 to 27}
Base QP |  |  |  |  |  |  |  | 
-13 | -8 | -3 | 2 | 7 | 12 | 17 | 22 | 27

## Slide 6: Results for PQ contents
HDR PQ |  |  | AI |  |  |  |  | 
 |  |  | Over VTM13.0 |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 0.03% | 0.04% | 0.02% | 0.03% | 0.04% | 0.02% | 100% | 100%
PQ422 | 0.04% | 0.04% | 0.01% | 0.04% | 0.04% | 0.01% | 103% | 100%
Overall | 0.04% | 0.04% | 0.02% | 0.04% | 0.04% | 0.02% | 102% | 100%
 |  |  | LDB |  |  |  |  | 
 |  |  | Over VTM13.0 |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 0.08% | 0.10% | 0.03% | 0.07% | 0.10% | 0.03% | 103% | 101%
PQ422 | 0.11% | 0.09% | 0.03% | 0.10% | 0.10% | 0.04% | 100% | 99%
Overall | 0.09% | 0.09% | 0.03% | 0.09% | 0.10% | 0.03% | 102% | 100%
 |  |  | RA |  |  |  |  | 
 |  |  | Over VTM13.0 |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 0.10% | 0.08% | 0.02% | 0.09% | 0.08% | 0.03% | 104% | 98%
PQ422 | 0.12% | 0.07% | 0.02% | 0.12% | 0.07% | 0.02% | 101% | 100%
Overall | 0.11% | 0.08% | 0.02% | 0.10% | 0.07% | 0.02% | 103% | 99%
Overall PQ | 0.08% | 0.07% | 0.02% | 0.08% | 0.07% | 0.02% | 102% | 100%
HDR PQ |  |  | AI |  |  |  |  | 
 |  |  | Over VTM13.0 |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 0.11% | 0.00% | -0.07% | 0.10% | 0.01% | -0.05% | 99% | 98%
PQ422 | 0.13% | 0.04% | -0.04% | 0.12% | 0.06% | -0.03% | 102% | 99%
Overall | 0.12% | 0.02% | -0.06% | 0.11% | 0.03% | -0.04% | 101% | 99%
 |  |  | LDB |  |  |  |  | 
 |  |  | Over VTM13.0 |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 0.10% | 0.04% | -0.18% | 0.11% | 0.05% | -0.14% | 96% | 95%
PQ422 | 0.17% | -0.04% | -0.28% | 0.18% | -0.01% | -0.25% | 94% | 97%
Overall | 0.13% | 0.00% | -0.23% | 0.14% | 0.02% | -0.19% | 95% | 96%
 |  |  | RA |  |  |  |  | 
 |  |  | Over VTM13.0 |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 0.15% | 0.04% | -0.19% | 0.16% | 0.05% | -0.15% | 102% | 97%
PQ422 | 0.22% | -0.05% | -0.23% | 0.23% | -0.01% | -0.20% | 99% | 98%
Overall | 0.19% | 0.00% | -0.21% | 0.19% | 0.02% | -0.18% | 101% | 97%
Overall PQ | 0.15% | 0.01% | -0.17% | 0.15% | 0.02% | -0.14% | 99% | 97%
Test-1: WPP=1 (CTU size: 128)
Test-2: WPP=1, CTU size=64

## Slide 7: Results for PQ contents
Test-3: WPP=1 (CTU size: 128), Tile=2x1
HDR PQ |  |  | AI |  |  |  |  | 
 |  |  | Over VTM13.0 |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 0.10% | 0.10% | 0.08% | 0.09% | 0.09% | 0.07% | 97% | 99%
PQ422 | 0.11% | 0.13% | 0.10% | 0.10% | 0.13% | 0.09% | 101% | 99%
Overall | 0.11% | 0.11% | 0.09% | 0.10% | 0.11% | 0.08% | 99% | 99%
 |  |  | LDB |  |  |  |  | 
 |  |  | Over VTM13.0 |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 0.20% | 0.22% | 0.13% | 0.19% | 0.20% | 0.12% | 95% | 100%
PQ422 | 0.24% | 0.21% | 0.11% | 0.23% | 0.20% | 0.11% | 94% | 99%
Overall | 0.22% | 0.21% | 0.12% | 0.21% | 0.20% | 0.11% | 95% | 100%
 |  |  | RA |  |  |  |  | 
 |  |  | Over VTM13.0 |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 0.22% | 0.22% | 0.10% | 0.21% | 0.21% | 0.09% | 98% | 100%
PQ422 | 0.26% | 0.20% | 0.13% | 0.25% | 0.20% | 0.11% | 95% | 99%
Overall | 0.24% | 0.21% | 0.11% | 0.23% | 0.20% | 0.10% | 96% | 100%
Overall PQ | 0.19% | 0.18% | 0.11% | 0.18% | 0.17% | 0.10% | 97% | 99%

## Slide 8: Results for HLG contents
Test-1: WPP=1 (CTU size: 128)
Test-2: WPP=1, CTU size=64
HDR HLG |  |  | AI |  | 
 |  |  | Over VTM13.0 |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | 0.01% | 0.00% | 0.01% | 102% | 100%
HLG422 | 0.01% | 0.00% | 0.01% | 102% | 99%
Overall | 0.01% | 0.00% | 0.01% | 102% | 100%
 |  |  | LDB |  | 
 |  |  | Over VTM13.0 |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | 0.08% | 0.05% | 0.02% | 108% | 100%
HLG422 | 0.09% | 0.04% | -0.01% | 107% | 98%
Overall | 0.08% | 0.04% | 0.00% | 107% | 99%
 |  |  | RA |  | 
 |  |  | Over VTM13.0 |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | 0.07% | 0.05% | 0.01% | 104% | 99%
HLG422 | 0.09% | 0.04% | 0.01% | 105% | 100%
Overall | 0.08% | 0.05% | 0.01% | 105% | 99%
Overall HLG | 0.06% | 0.03% | 0.01% | 105% | 99%
HDR HLG |  |  | AI |  | 
 |  |  | Over VTM13.0 |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | 0.07% | 0.02% | 0.03% | 104% | 98%
HLG422 | 0.08% | 0.03% | 0.02% | 102% | 98%
Overall | 0.07% | 0.02% | 0.02% | 103% | 98%
 |  |  | LDB |  | 
 |  |  | Over VTM13.0 |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | 0.15% | 0.02% | -0.09% | 103% | 97%
HLG422 | 0.19% | 0.02% | -0.16% | 100% | 96%
Overall | 0.17% | 0.02% | -0.12% | 102% | 96%
 |  |  | RA |  | 
 |  |  | Over VTM13.0 |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | 0.17% | 0.04% | -0.12% | 105% | 98%
HLG422 | 0.22% | 0.01% | -0.19% | 103% | 99%
Overall | 0.20% | 0.03% | -0.15% | 104% | 98%
Overall HLG | 0.15% | 0.02% | -0.08% | 103% | 98%
HDR HLG |  |  | AI |  | 
 |  |  | Over VTM13.0 |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | 0.04% | 0.03% | 0.03% | 99% | 100%
HLG422 | 0.04% | 0.04% | 0.03% | 98% | 99%
Overall | 0.04% | 0.03% | 0.03% | 98% | 100%
 |  |  | LDB |  | 
 |  |  | Over VTM13.0 |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | 0.12% | 0.10% | 0.04% | 100% | 101%
HLG422 | 0.12% | 0.11% | -0.01% | 99% | 96%
Overall | 0.12% | 0.10% | 0.01% | 99% | 99%
 |  |  | RA |  | 
 |  |  | Over VTM13.0 |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | 0.11% | 0.11% | 0.02% | 101% | 100%
HLG422 | 0.14% | 0.12% | 0.05% | 100% | 99%
Overall | 0.13% | 0.11% | 0.04% | 100% | 100%
Overall HLG | 0.10% | 0.08% | 0.03% | 99% | 99%
Test-3: WPP=1 (CTU size: 128), Tile=2x1

## Slide 9: Results for SVT contents
Test-1: WPP=1 (CTU size: 128)
Test-2: WPP=1, CTU size=64
SVT RGB |  |  | AI |  | 
 |  |  | Over VTM13.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.01% | 0.02% | 0.01% | 106% | 100%
SVT12 | 0.01% | 0.01% | 0.01% | 104% | 100%
Overall | 0.01% | 0.01% | 0.01% | 105% | 100%
 |  |  | LDB |  | 
 |  |  | Over VTM13.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.01% | 0.02% | 0.02% | 106% | 100%
SVT12 | 0.02% | 0.01% | 0.01% | 108% | 101%
Overall | 0.01% | 0.02% | 0.01% | 107% | 100%
 |  |  | RA |  | 
 |  |  | Over VTM13.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.02% | 0.01% | 0.01% | 98% | 98%
SVT12 | 0.02% | 0.01% | 0.01% | 103% | 99%
Overall | 0.02% | 0.01% | 0.01% | 101% | 99%
Overall RGB | 0.01% | 0.01% | 0.01% | 104% | 100%
SVT RGB |  |  | AI |  | 
 |  |  | Over VTM13.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.03% | 0.03% | 0.02% | 106% | 99%
SVT12 | 0.03% | 0.02% | 0.01% | 105% | 99%
Overall | 0.03% | 0.03% | 0.02% | 105% | 99%
 |  |  | LDB |  | 
 |  |  | Over VTM13.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.04% | 0.04% | 0.04% | 100% | 98%
SVT12 | 0.07% | 0.03% | 0.02% | 100% | 99%
Overall | 0.06% | 0.04% | 0.03% | 100% | 98%
 |  |  | RA |  | 
 |  |  | Over VTM13.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.06% | 0.03% | 0.03% | 100% | 97%
SVT12 | 0.07% | 0.01% | 0.01% | 99% | 98%
Overall | 0.07% | 0.02% | 0.02% | 99% | 98%
Overall RGB | 0.05% | 0.03% | 0.02% | 102% | 98%
SVT RGB |  |  | AI |  | 
 |  |  | Over VTM13.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.03% | 0.03% | 0.02% | 102% | 100%
SVT12 | 0.03% | 0.02% | 0.02% | 100% | 99%
Overall | 0.03% | 0.03% | 0.02% | 101% | 100%
 |  |  | LDB |  | 
 |  |  | Over VTM13.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.03% | 0.03% | 0.03% | 102% | 99%
SVT12 | 0.04% | 0.02% | 0.02% | 101% | 99%
Overall | 0.04% | 0.03% | 0.03% | 102% | 99%
 |  |  | RA |  | 
 |  |  | Over VTM13.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.04% | 0.03% | 0.03% | 101% | 98%
SVT12 | 0.04% | 0.03% | 0.03% | 101% | 99%
Overall | 0.04% | 0.03% | 0.03% | 101% | 99%
Overall RGB | 0.04% | 0.03% | 0.02% | 101% | 99%
Test-3: WPP=1 (CTU size: 128), Tile=2x1

## Slide 10: Results in wide QP range
HDR PQ | Test-1 WPP:1 (CTU size: 128) |  |  |  |  |  |  |  |  | HDR HLG | Test-1 WPP:1 (CTU size: 128) |  |  |  |  |  | SVT RGB | Test-1 WPP:1 (CTU size: 128) |  |  |  | 
 | Over VTM13.0 |  |  |  |  |  |  |  |  |  | Over VTM13.0 |  |  |  |  |  |  | Over VTM13.0 |  |  |  | 
QP range | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT |  | QP range | psnrY | psnrU | psnrV | EncT | DecT |  | QP range | psnrG | psnrB | psnrR | EncT | DecT
QP: -13 … 12 | 0.08% | 0.07% | 0.02% | 0.08% | 0.07% | 0.02% | 102% | 100% |  | QP: -13 … 12 | 0.06% | 0.03% | 0.01% | 105% | 99% |  | QP: -13 … 12, QP:-33 … -8 | 0.01% | 0.01% | 0.01% | 104% | 100%
QP: -8 … 17 | 0.10% | 0.11% | 0.02% | 0.10% | 0.11% | 0.03% | 102% | 100% |  | QP: -8 … 17 | 0.08% | 0.05% | -0.02% | 104% | 100% |  | QP: -8 … 17, QP: -28 … -3 | 0.02% | 0.01% | 0.01% | 104% | 100%
QP: -3 … 22 | 0.14% | 0.15% | 0.06% | 0.14% | 0.15% | 0.05% | 101% | 100% |  | QP: -3 … 22 | 0.11% | 0.05% | -0.05% | 103% | 100% |  | QP: -3 … 22, QP: -23 … 2 | 0.02% | 0.01% | 0.01% | 103% | 100%
QP: 2 … 27 | 0.23% | 0.21% | 0.12% | 0.22% | 0.20% | 0.10% | 101% | 100% |  | QP: 2 … 27 | 0.16% | 0.04% | -0.10% | 102% | 100% |  | QP: 2 … 27, QP: -18 … 7 | 0.03% | 0.01% | 0.01% | 102% | 100%
HDR PQ | Test-2 WPP:1, CTU size: 64 |  |  |  |  |  |  |  |  | HDR HLG | Test-2 WPP:1, CTU size: 64 |  |  |  |  |  | SVT RGB | Test-2 WPP:1, CTU size: 64 |  |  |  | 
 | Over VTM13.0 |  |  |  |  |  |  |  |  |  | Over VTM13.0 |  |  |  |  |  |  | Over VTM13.0 |  |  |  | 
QP range | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT |  | QP range | psnrY | psnrU | psnrV | EncT | DecT |  | QP range | psnrG | psnrB | psnrR | EncT | DecT
QP: -13 … 12 | 0.15% | 0.01% | -0.17% | 0.15% | 0.02% | -0.14% | 99% | 97% |  | QP: -13 … 12 | 0.15% | 0.02% | -0.08% | 103% | 98% |  | QP: -13 … 12, QP:-33 … -8 | 0.05% | 0.03% | 0.02% | 102% | 98%
QP: -8 … 17 | 0.21% | 0.02% | -0.27% | 0.22% | 0.05% | -0.23% | 99% | 100% |  | QP: -8 … 17 | 0.19% | -0.03% | -0.25% | 102% | 101% |  | QP: -8 … 17, QP: -28 … -3 | 0.06% | 0.03% | 0.02% | 101% | 100%
QP: -3 … 22 | 0.33% | 0.05% | -0.29% | 0.34% | 0.08% | -0.25% | 100% | 100% |  | QP: -3 … 22 | 0.27% | -0.07% | -0.37% | 102% | 100% |  | QP: -3 … 22, QP: -23 … 2 | 0.07% | 0.02% | 0.02% | 100% | 100%
QP: 2 … 27 | 0.56% | 0.19% | -0.15% | 0.55% | 0.18% | -0.14% | 101% | 100% |  | QP: 2 … 27 | 0.41% | -0.09% | -0.48% | 101% | 101% |  | QP: 2 … 27, QP: -18 … 7 | 0.12% | 0.03% | 0.03% | 100% | 100%
HDR PQ | Test-3 WPP:1, CTU size: 128, Tile: 2x1 |  |  |  |  |  |  |  |  | HDR HLG | Test-3 WPP:1, CTU size: 128, Tile: 2x1 |  |  |  |  |  | SVT RGB | Test-3 WPP:1, CTU size: 128, Tile: 2x1 |  |  |  | 
 | Over VTM13.0 |  |  |  |  |  |  |  |  |  | Over VTM13.0 |  |  |  |  |  |  | Over VTM13.0 |  |  |  | 
QP range | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT |  | QP range | psnrY | psnrU | psnrV | EncT | DecT |  | QP range | psnrG | psnrB | psnrR | EncT | DecT
QP: -13 … 12 | 0.19% | 0.18% | 0.11% | 0.18% | 0.17% | 0.10% | 97% | 99% |  | QP: -13 … 12 | 0.10% | 0.08% | 0.03% | 99% | 99% |  | QP: -13 … 12, QP:-33 … -8 | 0.04% | 0.03% | 0.02% | 101% | 99%
QP: -8 … 17 | 0.24% | 0.25% | 0.12% | 0.23% | 0.25% | 0.12% | 98% | 100% |  | QP: -8 … 17 | 0.13% | 0.13% | 0.01% | 99% | 100% |  | QP: -8 … 17, QP: -28 … -3 | 0.04% | 0.02% | 0.02% | 101% | 100%
QP: -3 … 22 | 0.32% | 0.32% | 0.19% | 0.31% | 0.32% | 0.18% | 99% | 99% |  | QP: -3 … 22 | 0.19% | 0.17% | 0.01% | 100% | 100% |  | QP: -3 … 22, QP: -23 … 2 | 0.05% | 0.03% | 0.03% | 101% | 100%
QP: 2 … 27 | 0.50% | 0.43% | 0.36% | 0.48% | 0.42% | 0.34% | 99% | 99% |  | QP: 2 … 27 | 0.30% | 0.24% | -0.03% | 100% | 100% |  | QP: 2 … 27, QP: -18 … 7 | 0.07% | 0.04% | 0.04% | 100% | 100%
PQ contents
HLG contents
SVT contents

## Slide 11: Conclusion
Introduced an issue of this contribution
  The CABAC throughput might be worse when large CTU and WPP are used.
Proposed a constraint for high bit rate coding
  Max CTU size 64 or Tile split
Showed experimental results
  (Test-1) WPP: 1
  (Test-2) WPP: 1 and CTU size : 64
  (Test-3) WPP: 1 and Tile: 2x1
Thank Sharp for cross checking.