## Slide 1: JVET-W0071 AHG9: Green Metadata SEI message for VVC
C. Herglotz, M. Kränzler, A. Kaup, E. Francois, M. Radosavljevic, E. Reinhard, X. Ducloux, D. Menard, Y. He, M. Coban, D. Rusanovskyy, M. Karczewicz
FAU, InterDigital, Harmonic, INSA, Qualcomm

## Slide 2: Outline
Overview on the current GREEN-MPEG standard
Complexity assessment of VVC decoding
SEI Messaging for Decoder Complexity
SEI Messaging for objective quality

## Slide 3: Overview on GREEN-MPEG
Main components:
Chapter 5: Decoder power reduction
Chapter 6: Display power reduction using display adaptation
Chapter 7: Energy-efficient media selection
Chapter 8: Metrics for quality recovery after low-power encoding

## Slide 4: Overview on GREEN-MPEG
Main components:
Chapter 5: Decoder power reduction
Chapter 6: Display power reduction using display adaptation
Chapter 7: Energy-efficient media selection
Chapter 8: Metrics for quality recovery after low-power encoding

## Slide 5: Outline
Overview on the current GREEN-MPEG standard
Complexity assessment of VVC decoding
SEI Messaging for Decoder Complexity
SEI Messaging for objective quality

## Slide 6: Complexity Assessment of VVC Decoding
Analysis of
VTM-13.0 (single thread)
VVdeC v1.0.0 (multithreading)
using
Time measurements
Energy measurements
Quality evaluation

## Slide 7: Complexity Assessment of VVC Decoding
Dataset: Tool on/off tests
Encoder: VTM11.0
Configuration: VTM11.0 CTCs [4], random-access (RA) configuration (cfg file encoder_randomaccess_vtm.cfg), with GOP size 32.
4 QPs: 22, 27, 32, 37
12 HD (1920x1080) clips, with length 100 frames, frame rates of 30, 50 or 60 fps, generated from native UHD content downscaled to HD.
12 UHD (3840x2160) clips, with length 100 frames, frame rates of 30, 50 or 60 fps.
Tested tools
  Intra: MIP, MRL, LMchroma, ISP, Planar, DC, Directional Horiz/Vertic
  Transform: MTS, SBT, LFNST, JCCR, DepQuant, TU32 (instead of 64 max)
  Loop Filter: DBF, SAO, ALF+CCALF, CCALF, LMCS
  Inter:
    Motion-coding related: AFFINE, TMVP, SbTMVP, AMVR, MMVD, SMVD
    Inter Blending: BCW, GPM, CIIP
    Inter prediction refinement: DMVR, BDOF, PROF
  Others
    CTU64 (instead of 128)
All tools off (still with CTU 128 and TU 64)

## Slide 8: Complexity Assessment of VVC Decoding
Results for VTM-13.0 (part 1)
 | BDR | BDDE | BDDT | BDRY | BDRU | BDRV | BDRVMAF | BDDEVMAF | RelDecEnergy | RelDecTime
ALLOFF | 37,38 | -37,90 | -37,31 | 29,79 | 75,23 | 139,36 | 28,46 | -40,79 | 58,84 | 59,53
NODBF | 0,73 | -10,33 | -9,75 | 0,87 | -0,04 | -0,04 | 0,91 | -10,64 | 89,53 | 90,12
NOALF | 5,79 | -5,67 | -5,15 | 2,61 | 19,44 | 39,02 | 5,67 | -5,81 | 92,92 | 93,53
NOAffine | 2,40 | -1,36 | -0,18 | 2,52 | 1,73 | 2,47 | 2,58 | -1,41 | 98,69 | 99,99
ALL | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 100,00 | 100,00
NODMVR | 0,78 | -1,34 | 0,10 | 0,73 | 0,90 | 1,27 | 1,04 | -1,50 | 98,70 | 100,26
NOISP | 0,34 | -0,48 | 0,65 | 0,34 | 0,08 | 0,87 | 0,45 | -0,68 | 99,45 | 100,56
NOTMVP | 1,18 | -0,71 | 1,22 | 1,24 | 0,84 | 0,97 | 1,38 | -0,90 | 99,03 | 101,03
MTS2 | 0,49 | 0,67 | 0,97 | 0,28 | 1,73 | 0,03 | 0,32 | 0,32 | 100,54 | 101,04
NOBIO | 0,79 | -0,17 | 1,26 | 0,87 | 0,44 | 0,34 | 1,20 | -0,60 | 99,64 | 101,09
NOLMCS | 0,22 | 0,11 | 1,80 | -0,04 | 1,71 | 1,76 | -1,20 | -0,22 | 99,54 | 101,18
NOSAO | 0,19 | -0,40 | 1,05 | 0,11 | 0,29 | 2,80 | 0,16 | -0,17 | 99,51 | 101,18
NOLFNST | 0,57 | -0,37 | 1,21 | 0,63 | 0,24 | 0,53 | 0,94 | -0,19 | 99,60 | 101,19
MTS3 | -0,16 | 0,37 | 0,95 | -0,16 | -0,22 | -1,13 | -0,02 | 0,26 | 100,53 | 101,20
NOPROF | 0,30 | -0,54 | 1,20 | 0,36 | -0,06 | 0,13 | 0,39 | -0,65 | 99,37 | 101,20
NOJointCbCr | 0,23 | -2,05 | 1,41 | 0,33 | -0,78 | 0,56 | 0,36 | -2,33 | 97,85 | 101,40
NOSBT | 0,46 | -0,31 | 1,59 | 0,54 | -0,06 | 0,46 | 0,44 | -0,38 | 99,57 | 101,50
NOIMV | 1,19 | 0,81 | 1,65 | 0,94 | 2,06 | 4,93 | 1,00 | 0,54 | 100,71 | 101,58
NOGPM | 0,74 | 0,75 | 1,71 | 0,70 | 0,71 | 1,15 | 0,64 | 0,64 | 100,63 | 101,69
NOSbTMVP | 0,38 | 0,17 | 1,85 | 0,41 | 0,16 | 0,11 | 0,58 | 0,20 | 100,10 | 101,90
NOLMChroma | 3,86 | 0,83 | 2,44 | 1,17 | 17,72 | 22,58 | 1,34 | 0,39 | 100,32 | 101,96

## Slide 9: Complexity Assessment of VVC Decoding
Results for VTM-13.0 (part 2)
 | BDR | BDDE | BDDT | BDRY | BDRU | BDRV | BDRVMAF | BDDEVMAF | RelDecEnergy | RelDecTime
ALLLP | 29,01 | 3,92 | 7,94 | 23,82 | 62,51 | 72,52 | 23,65 | 0,70 | 97,99 | 102,00
NOMIP | 0,27 | -0,55 | 1,84 | 0,38 | -0,37 | -1,42 | 0,37 | -0,69 | 99,71 | 102,01
NOMTS | 0,71 | 0,47 | 2,12 | 0,88 | -0,14 | -1,41 | 0,92 | 0,84 | 100,30 | 102,05
NOCCALF | 2,61 | 1,47 | 2,89 | -0,14 | 14,68 | 30,55 | 1,36 | 1,41 | 100,81 | 102,22
ALLLB | 24,13 | 4,80 | 8,22 | 19,57 | 53,73 | 58,57 | 19,43 | 1,71 | 99,08 | 102,49
NOMRL | 0,48 | 0,95 | 2,88 | 0,52 | 0,06 | 0,66 | 0,31 | 0,86 | 100,63 | 102,60
CTU64 | 2,32 | 2,31 | 2,55 | 1,98 | 3,53 | 5,62 | 2,10 | 2,39 | 102,18 | 102,63
NOCIIP | 0,26 | 1,37 | 2,78 | 0,32 | -0,12 | 0,12 | 0,55 | 1,37 | 101,46 | 102,81
NOMMVD | 0,40 | 1,11 | 2,95 | 0,42 | 0,18 | 0,81 | 0,31 | 1,02 | 101,12 | 103,02
NOSMVD | 0,21 | 1,22 | 2,99 | 0,19 | 0,19 | 0,75 | 0,22 | 1,23 | 101,18 | 103,05
noPLANAR | -0,12 | 0,86 | 3,00 | -0,14 | -0,16 | 0,16 | -0,08 | 0,90 | 100,93 | 103,17
noDC | 0,05 | 0,54 | 3,16 | 0,06 | 0,00 | 0,05 | 0,12 | 0,58 | 100,64 | 103,23
noHV | 0,23 | 0,68 | 3,38 | 0,22 | 0,09 | 0,74 | 0,28 | 0,71 | 100,53 | 103,26
NODepQuant | 2,02 | 1,98 | 3,17 | 1,88 | 2,76 | 3,10 | 2,35 | 1,58 | 102,23 | 103,53
NOBCW | 0,96 | 3,43 | 4,60 | 0,80 | 1,78 | 1,93 | 0,33 | 2,76 | 103,03 | 104,26
TU32 | 1,10 | 3,38 | 5,29 | 0,80 | 1,86 | 4,45 | 1,04 | 3,82 | 103,40 | 105,30

## Slide 10: Complexity Assessment of VVC Decoding
Results for VVdeC v1.0.0 (part 1)
 | BDR | BDDE | BDDT | BDRY | BDRU | BDRV | BDRVMAF | BDDEVMAF | RelDecEnergy | RelDecTime
ALLOFF | 37,38 | -32,54 | -25,17 | 29,79 | 75,23 | 139,36 | 28,46 | -34,76 | 64,44 | 71,65
NOALF | 5,79 | -11,52 | -10,84 | 2,61 | 19,44 | 39,02 | 5,67 | -12,33 | 87,15 | 87,73
NODBF | 0,73 | -5,84 | -3,33 | 0,87 | -0,04 | -0,04 | 0,91 | -5,77 | 94,12 | 96,60
ALLLP | 29,01 | 0,84 | 2,82 | 23,82 | 62,51 | 72,52 | 23,65 | -1,83 | 95,47 | 97,76
NODMVR | 0,78 | -1,87 | -0,82 | 0,73 | 0,90 | 1,27 | 1,04 | -2,32 | 98,18 | 99,20
ALLLB | 24,13 | 2,23 | 4,17 | 19,57 | 53,73 | 58,57 | 19,43 | -0,15 | 97,24 | 99,26
MTS2 | 0,49 | -0,50 | -0,26 | 0,28 | 1,73 | 0,03 | 0,32 | -0,61 | 99,53 | 99,65
ALL | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 100,00 | 100,00
TU32 | 1,10 | 0,12 | 0,11 | 0,80 | 1,86 | 4,45 | 1,04 | 0,10 | 100,00 | 100,00
NOSAO | 0,19 | -0,36 | 0,06 | 0,11 | 0,29 | 2,80 | 0,16 | 0,13 | 99,68 | 100,01
NOAffine | 2,40 | -0,93 | 0,12 | 2,52 | 1,73 | 2,47 | 2,58 | -1,04 | 99,07 | 100,07
NOLMCS | 0,22 | 0,44 | 0,87 | -0,04 | 1,71 | 1,76 | -1,20 | 0,22 | 99,70 | 100,28
MTS3 | -0,16 | 0,10 | 0,37 | -0,16 | -0,22 | -1,13 | -0,02 | 0,20 | 100,28 | 100,52
NOPROF | 0,30 | 0,42 | 0,71 | 0,36 | -0,06 | 0,13 | 0,39 | 0,36 | 100,50 | 100,71
NOLMChroma | 3,86 | 0,41 | 1,44 | 1,17 | 17,72 | 22,58 | 1,34 | -0,02 | 99,89 | 100,83
NOMIP | 0,27 | 0,59 | 0,91 | 0,38 | -0,37 | -1,42 | 0,37 | 0,67 | 100,68 | 100,95
NOLFNST | 0,57 | 0,32 | 1,09 | 0,63 | 0,24 | 0,53 | 0,94 | 0,38 | 100,39 | 101,14
NOMTS | 0,71 | 0,93 | 1,27 | 0,88 | -0,14 | -1,41 | 0,92 | 1,03 | 100,89 | 101,24

## Slide 11: Complexity Assessment of VVC Decoding
Results for VVdeC v1.0.0 (part 2)
 | BDR | BDDE | BDDT | BDRY | BDRU | BDRV | BDRVMAF | BDDEVMAF | RelDecEnergy | RelDecTime
NOTMVP | 1,18 | -0,07 | 1,32 | 1,24 | 0,84 | 0,97 | 1,38 | -0,01 | 100,00 | 101,30
NOBIO | 0,79 | -0,49 | 1,37 | 0,87 | 0,44 | 0,34 | 1,20 | -0,81 | 99,41 | 101,32
NOMRL | 0,48 | 1,08 | 1,49 | 0,52 | 0,06 | 0,66 | 0,31 | 1,00 | 100,97 | 101,41
NOSBT | 0,46 | 0,80 | 1,90 | 0,54 | -0,06 | 0,46 | 0,44 | 0,79 | 100,82 | 101,78
NOCIIP | 0,26 | 0,92 | 1,82 | 0,32 | -0,12 | 0,12 | 0,55 | 0,79 | 100,99 | 101,80
NOMMVD | 0,40 | 1,40 | 2,11 | 0,42 | 0,18 | 0,81 | 0,31 | 1,17 | 101,43 | 102,06
NOSbTMVP | 0,38 | 0,37 | 2,07 | 0,41 | 0,16 | 0,11 | 0,58 | 0,60 | 100,55 | 102,08
NOISP | 0,34 | 0,84 | 2,16 | 0,34 | 0,08 | 0,87 | 0,45 | 0,97 | 100,91 | 102,13
NOCCALF | 2,61 | 1,66 | 2,80 | -0,14 | 14,68 | 30,55 | 1,36 | 1,41 | 101,17 | 102,23
NOSMVD | 0,21 | 1,66 | 2,52 | 0,19 | 0,19 | 0,75 | 0,22 | 1,46 | 101,66 | 102,49
NOGPM | 0,74 | 1,94 | 2,72 | 0,70 | 0,71 | 1,15 | 0,64 | 1,79 | 101,90 | 102,73
NOJointCbCr | 0,23 | 1,48 | 2,91 | 0,33 | -0,78 | 0,56 | 0,36 | 1,54 | 101,60 | 102,95
NOBCW | 0,96 | 2,52 | 3,65 | 0,80 | 1,78 | 1,93 | 0,33 | 2,24 | 102,32 | 103,41
noHV | 0,23 | 1,68 | 3,85 | 0,22 | 0,09 | 0,74 | 0,28 | 1,78 | 101,77 | 103,84
noPLANAR | -0,12 | 1,58 | 3,80 | -0,14 | -0,16 | 0,16 | -0,08 | 1,53 | 101,59 | 103,86
NODepQuant | 2,02 | 2,90 | 3,67 | 1,88 | 2,76 | 3,10 | 2,35 | 2,73 | 103,26 | 103,92
noDC | 0,05 | 2,14 | 3,91 | 0,06 | 0,00 | 0,05 | 0,12 | 2,19 | 102,12 | 103,92
NOIMV | 1,19 | 2,92 | 4,11 | 0,94 | 2,06 | 4,93 | 1,00 | 2,76 | 102,83 | 103,98
CTU64 | 2,32 | 7,37 | 9,64 | 1,98 | 3,53 | 5,62 | 2,10 | 8,31 | 107,59 | 109,83

## Slide 12: Complexity Assessment of VVC Decoding
Complexity assessment by decoding time modeling
Decoding time
: Index of a tool
Frequency of occurrence of the -th tool
: Estimated complexity for a single execution of the -th tool

## Slide 13: Complexity Assessment of VVC Decoding
Complexity assessment by decoding time modeling
Decoding time
: Index of a tool
Frequency of occurrence of the -th tool
: Estimated complexity for a single execution of the -th tool
Block size, bi-prediction, DMVR, DF instances etc.

## Slide 14: Complexity Assessment of VVC Decoding
Complexity assessment by decoding time modeling
Decoding time
: Index of a tool
Frequency of occurrence of the -th tool
: Estimated complexity for a single execution of the -th tool
Training data obtained from complexity analysis

## Slide 15: Complexity Assessment of VVC Decoding
Complexity assessment by decoding time modeling
Decoding time
: Index of a tool
Frequency of occurrence of the -th tool
: Estimated complexity for a single execution of the -th tool
Obtained from bit stream analysis
(JVET-P0085) https://gitlab.lms.tf.fau.de/LMS/vtm-analyzer

## Slide 16: Complexity Assessment of VVC Decoding
Complexity assessment by decoding time modeling
Decoding time
: Index of a tool
Frequency of occurrence of the -th tool
: Estimated complexity for a single execution of the -th tool
Trained for optimal estimation of

## Slide 17: Complexity Assessment of VVC Decoding
Proposed set of complexity parameters
Trained on VVdeC v1.0.0
randomaccess configuration
Data set from complexity analysis
Mean estimation error: 4.92%
Offset
portion_non_zero_4_8_16_blocks_area
portion_non_zero_32_64_128_blocks_area
portion_non_zero_256_512_1024_blocks_area
portion_non_zero_2048_4096_blocks_area
portion_non_zero_transform_coefficients_area
portion_intra_predicted_blocks_area
portion_bi_or_gpm_predicted_blocks_area
portion_deblocking_instances
portion_alf_blocks
portion_sao_blocks

## Slide 18: Complexity Assessment of VVC Decoding
Proposed set of complexity parameters
Intra tools
Modeling and complexity analysis for allIntra will be performed for the next meeting cycle.
Granularity options of signalling (syntax element period_type)
Single picture
Number of successive pictures in decoding order
Time interval (in second)
Single picture with slice / tile / subpicture granularity
portion_planar_blocks_in_intra_area
portion_dc_blocks_in_intra_area
portion_angular_hv_blocks_in_intra_area
portion_mip_blocks_in_intra_area

## Slide 19: Outline
Overview on the current GREEN-MPEG standard
Complexity assessment of VVC decoding
SEI Messaging for Decoder Complexity
SEI Messaging for objective quality

## Slide 20: SEI Messaging for Decoder Complexity
Syntax and semantics added in GREEN-MPEG document
.
.
.
.
.
.

## Slide 21: Outline
Overview on the current GREEN-MPEG standard
Complexity assessment of VVC decoding
SEI Messaging for Decoder Complexity
SEI Messaging for objective quality

## Slide 22: SEI Messaging for Objective Quality
Currently: only PSNR
Proposed: Add SSIM, VMAF, wPSNR, WS-PSNR (cf. JVET-W0085)
.
.
.

## Slide 23: Next steps
Complete the decoding complexity analysis with alternate software decoders implementations
Complete the decoding complexity analysis with additional bitstreams corresponding to All Intra and Low Delay configurations
Implement the SEI message in the VTM analyzer
Consolidate the proposed specification

## Slide 24
Questions?
Acknowledgments: this work has been partially achieved in the context of the 3EMS project funded by the “Region Bretagne”.

## Slide 25: BACKUP
Metrics for complexity evaluation
BDR: Average BD-rate increase [3] when the tool is switched off (for YUV-PSNR) in percent.
BDRY: Average BD-rate increase [3] when the tool is switched off (for Y-PSNR) in percent.
BDRU: Average BD-rate increase [3] when the tool is switched off (for U-PSNR) in percent.
BDRV: Average BD-rate increase [3] when the tool is switched off (for V-PSNR) in percent.
BDRVMAF: Average BD-rate increase [3] when the tool is switched off (for VMAF-score) in percent.
BDDE: Average BD-decoding energy increase when the tool is switched off. For the calculation of the BD-energy, the rate is replaced by the measured energy in percent.
BDDT: Average BD-decoding time increase when the tool is switched off. For the calculation of the BD-time, the rate is replaced by the measured decoding time in percent.
RelDecTime: Average decoding time change at the same QP in percent.
RelDecEnergy: Average decoding time change at the same QP in percent.

## Slide 26: BACKUP: Time coefficients after training
Name | Value [t]
‘Offset' | 0.000650155716769603
'coeff' | 1.02777083453380e-08
'nonZeroBlocks4_8_16' | 6.00657696799381e-08
'nonZeroBlocks32_64_128' | 1.34718249956742e-08
'nonZeroBlocks256_512_1024' | 2.60046536604479e-07
'nonZeroBlocks2048_4096' | 5.87187577805715e-07
'intraBlocks' | 9.19631475638654e-10
'gpmNbiBlocks' | 6.49943651841137e-10
'dbfInstances' | 5.98809393012043e-09
'saoInstances' | 2.25769670761765e-06
'alfInstances' | 1.17267989268419e-06