## Slide 1: JVET-W0072 AHG9:Enhancement of film grain parameter estimation for different intensity intervals
Miloš Radosavljević, Edouard François (Interdigital)
Wassim Hamidouche, Thomas Amestoy, Guillaume Gautier (INSA)
July 2021

## Slide 2: Proposal – Film Grain
Film grain module is based on frequency filtering model
  SMPTE-RDD5 specification
Proposal is related with
  Film grain analysis – film grain parameter estimation module
  Film grain synthesis remains the same
An extension of the previous version proposed in JVET-V0093
  Where we used one intensity interval for complete dynamic range
    Hence one film grain scaling factor
In this proposal
  We estimate different film grain scaling factor for different intensity intervals

## Slide 3: Film Grain Analysis
PRE-PROCESSING
FG PARAMETER ESTIMATION
To create map that indicates flat regions of an input frame
  We use Canny edge detector
For filtering we use MCTF
Filtered frame is used to find film grain image
  Difference between input and filtered frame

## Slide 4: Film Grain Analysis
PRE-PROCESSING
FG PARAMETER ESTIMATION
Film grain image and filtered image are scanned block by block at 64x64 granularity
Blocks at the flat part of the image are processed further
Average value calculated on a block within the filtered frame
Variance of the film grain block calculated on a block from the film grain image

## Slide 5: Film Grain Analysis

## Slide 6: Film Grain Analysis
Fit the data points to a parameterized curve
  4-th order polynomial fitting
  Obtain scaling function by curve fitting
Approximate the scaling function by a simplified scaling function, in our case stepwise function
  Using Lloyd-Max non-uniform quantization
  Adapted (trained) for each new set of points
  Using 4 quantization levels

## Slide 7: Film Grain Analysis
BikeSparklers clip

## Slide 8: Film Grain Analysis
By analyzing quantized function, we get parameters used in SEI message and RDD5 model
fg_intensity_interval_lower_bound[ c ][ i ]
fg_intensity_interval_upper_bound[ c ][ i ]
and scaling factor fg_comp_model_value[ c ][ i ][ 0 ]

## Slide 9: Film Grain Analysis
CrowdRun sequence

## Slide 10: Conclusions
It is reported that presented method can model intensity of the film grain for different intensity intervals with more accuracy
  There is space for additional improving
We will provide software update after we merge with other contributions on film grain
  W0095 – our proposals are fully compatible
  Fully compatible with current RDD5 spec
  Provides parameters fully compatible with current SEI message