## Slide 1: AHG8: On significance, GT1, and GT2 flag coding for high bit depths
JVET-W0093
Sony Europe BV.
Adrian Browne, Steve Keating, Karl Sharman
Sony Group Corp.

## Slide 2: Motivation
JVET-V0122 reported results for disabling the context coding of coefficient values using SigMap, GT1, GT2, parity flags
  Losses for PQ and HLG in low QP range
    Expected result
  Gains for SVT-16 in low QP range, and all HBD content for lossless coding
    Unexpected result
Gains for JVET-V0122 indicate
  For lossless and SVT-16 low QP range context coding offers no benefit
  Better to code using only Golomb-Rice than use SigMap, GT1, GT2, parity
  Effectively, context coding is no longer working at these operating points

## Slide 3: Analysis of VTM13.0
Using decoder analyser extracted for CrowdRun (SVT-12 and SVT-16 AI)
  Number of SigMap, GT1, GT2 flags coded and set
QP | Coded Bins (millions) |  |  | Set Bins (millions) |  |  | %Set |  | 
 | Sig Map | GT1 | GT2 | Sig Map | GT1 | GT2 | Sig Map | GT1 | GT2
12 | 49.50 | 43.50 | 22.77 | 42.05 | 22.77 | 5.59 | 85.0% | 52.3% | 24.6%
7 | 42.37 | 40.06 | 28.01 | 38.42 | 28.01 | 12.04 | 90.7% | 69.9% | 43.0%
2 | 38.04 | 37.71 | 31.17 | 35.88 | 31.17 | 19.76 | 94.3% | 82.7% | 63.4%
-3 | 35.88 | 36.50 | 32.54 | 34.47 | 32.54 | 24.85 | 96.1% | 89.1% | 76.4%
-8 | 34.53 | 35.78 | 33.62 | 33.75 | 33.62 | 29.25 | 97.7% | 94.0% | 87.0%
-13 | 33.29 | 35.27 | 34.10 | 32.85 | 34.10 | 31.79 | 98.7% | 96.7% | 93.2%
QP | Coded Bins (millions) |  |  | Set Bins (millions) |  |  | %Set |  | 
 | Sig Map | GT1 | GT2 | Sig Map | GT1 | GT2 | Sig Map | GT1 | GT2
-8 | 34.31 | 35.78 | 33.55 | 33.49 | 33.55 | 29.01 | 97.6% | 93.8% | 86.5%
-13 | 33.76 | 35.43 | 34.18 | 33.27 | 34.18 | 31.68 | 98.6% | 96.5% | 92.7%
-18 | 33.46 | 35.27 | 34.54 | 33.16 | 34.54 | 33.17 | 99.1% | 97.9% | 96.0%
-23 | 32.61 | 34.64 | 34.20 | 32.43 | 34.20 | 33.45 | 99.4% | 98.7% | 97.8%
-28 | 31.83 | 34.37 | 34.08 | 31.71 | 34.08 | 33.67 | 99.6% | 99.2% | 98.8%
-33 | 31.30 | 34.37 | 34.18 | 31.23 | 34.18 | 33.93 | 99.8% | 99.5% | 99.3%
12 bit
16 bit
Number of coefficients coded
reduced by ~33%
Percentage of GT2 flags set
increases from <25% to >99%
Almost all coefficients at least 4
> 98% require Golomb-Rice coding

## Slide 4: Analysis of VTM13.0
As QPs reduce, flags are coded more efficiently
But actual coefficient value coded less efficiently
  Almost all coefficients require additional Golomb-Rice coding

## Slide 5: Proposal
Significance and subsequent flags are in effect shifted left by n bits
  Less predictable, noisier LSBs coded using EP-bins
SigMap, GT1, GT2 and parity used for sub-block coding of MSBs
  No change from VVC
Value reconstructed by shifting left MSBs and adding LSBs
  At end of block coding
In addition a new block significance flag is introduced
  Set when no coefficient in the block meets the significance test
  All sub-block coding can be skipped if not set
Code MSBs using SigMap, GT1, GT2, parity
and/or Golumb-Rice
Code LSBs as EP-bins
Significance test shifted left by n bits

## Slide 6: Selection of shift
Values for luma and chroma shifts signalled in slice header
  Could be determined by algorithm or be application specific
In proposal, values calculated in pre-encode step
  Used for current slice not next slice
    Suitable for still frames or if scene changes
Algorithm (non-normative):
  Compute estimated residual using value above and to the left
    residual = min(abs(value – valueAbove), abs(value – valueLeft))
  Compute histogram bin using residual value and QP adjustment
    qpAdjustment = sliceQP – (4 – (bitDepth - 8) * 6)
    bin = max(0, round(log2(residual) * 6) – qpAdjustment)
  Compute histogram using cumulative frequency

## Slide 7: Selection of shift
QP adjustment shifts the histogram to the left
  Number of entries in bin 0 increases as adjustment increases
Histogram and cumulative frequency for CrowdRun (16 bit AI) with and without QP adjustment

## Slide 8: Selection of shift
Shift is calculated using the centre of the second quartile
  Normalised into bits by dividing by 6
Multiplication / division by 6 increases granularity of cumulative frequency

## Slide 9: Analysis of Proposal
QP | Coded Bins (millions) |  |  | Set Bins (millions) |  |  | %Set |  | 
 | Sig Map | GT1 | GT2 | Sig Map | GT1 | GT2 | Sig Map | GT1 | GT2
12 | 49.50 | 43.50 | 22.77 | 42.05 | 22.77 | 5.59 | 85.0% | 52.3% | 24.6%
7 | 42.37 | 40.06 | 28.01 | 38.42 | 28.01 | 12.04 | 90.7% | 69.9% | 43.0%
2 | 46.78 | 39.24 | 25.23 | 37.48 | 25.23 | 10.33 | 80.1% | 64.3% | 40.9%
-3 | 51.90 | 36.27 | 22.41 | 36.27 | 22.41 | 7.73 | 69.9% | 61.8% | 34.5%
-8 | 51.00 | 37.80 | 23.06 | 35.72 | 23.06 | 8.79 | 70.0% | 61.0% | 38.1%
-13 | 51.44 | 37.28 | 22.10 | 34.68 | 22.10 | 8.10 | 67.4% | 59.3% | 36.7%
QP | Coded Bins (millions) |  |  | Set Bins (millions) |  |  | %Set |  | 
 | Sig Map | GT1 | GT2 | Sig Map | GT1 | GT2 | Sig Map | GT1 | GT2
-8 | 52.03 | 37.73 | 22.83 | 35.87 | 22.83 | 8.89 | 68.9% | 60.5% | 39.0%
-13 | 54.06 | 37.22 | 21.77 | 35.37 | 21.77 | 8.22 | 65.4% | 58.5% | 37.8%
-18 | 47.67 | 37.22 | 25.28 | 35.24 | 25.28 | 11.46 | 73.9% | 67.9% | 45.3%
-23 | 49.18 | 37.12 | 24.18 | 34.98 | 24.18 | 10.19 | 71.1% | 65.2% | 42.1%
-28 | 49.81 | 36.77 | 22.82 | 34.11 | 22.82 | 8.83 | 68.5% | 62.1% | 38.7%
-33 | 50.40 | 36.49 | 21.67 | 33.41 | 21.67 | 7.77 | 66.3% | 59.4% | 35.9%
Number of coefficients coded
remains similar
Percentage of GT2 flags set
remains less than 50%
Small MSB values exist
< 15% require Golomb-Rice

## Slide 10: Analysis of Proposal
As QPs reduce, flags are coded at similar probabilities
Many coefficients coded with flags + LSBs only
Number of coefficients requiring Golomb-Rice coding is reduced

## Slide 11: Results vs VTM 13.0
Lossless | AI | LDB | RA
PQ | -0.36% | -0.41% | -0.41%
HLG | -0.77% | -1.13% | -1.13%
SVT-12 | -1.10% | -1.33% | -1.34%
SVT-16 | -1.12% | -1.45% | -1.46%
Low QP | AI |  |  | LDB |  |  | RA |  |  | Time | 
 | Y/G | U/B | V/R | Y/G | U/B | V/R | Y/G | U/B | V/R | Enc | Dec
PQ | 0.05% | 0.05% | 0.06% | 0.03% | 0.03% | 0.04% | 0.03% | 0.04% | 0.04% | 102% | 99%
HLG | -0.08% | -0.10% | -0.10% | 0.02% | 0.03% | 0.03% | 0.01% | 0.03% | 0.03% | 102% | 101%
SVT-12 | -0.25% | -0.23% | -0.25% | -0.09% | -0.06% | -0.07% | -0.10% | -0.05% | -0.06% | 104% | 103%
SVT-16 | -0.87% | -0.89% | -0.89% | -0.87% | -0.80% | -0.80% | -0.85% | -0.77% | -0.77% |  | 

## Slide 12: Results vs VTM 13.0
Lossless | AI | LDB | RA
PQ | -1.00% | -1.06% | -1.00%
HLG | -2.74% | -2.65% | -2.51%
SVT-12 | -3.16% | -2.91% | -2.90%
SVT-16 | -2.81% | -2.41% | -2.42%
Low QP | AI |  |  | LDB |  |  | RA |  |  | Time | 
 | Y/G | U/B | V/R | Y/G | U/B | V/R | Y/G | U/B | V/R | Enc | Dec
PQ | 0.02% | 0.04% | 0.05% | 0.03% | 0.03% | 0.03% | 0.02% | 0.02% | 0.03% | 101% | 99%
HLG | -0.30% | -0.16% | -0.17% | -0.01% | 0.01% | 0.01% | -0.01% | 0.01% | 0.01% | 103% | 100%
SVT-12 | -0.82% | -0.55% | -0.56% | -0.38% | -0.34% | -0.35% | -0.38% | -0.28% | -0.29% | 114% | 115%
SVT-16 | -2.33% | -2.08% | -2.06% | -1.78% | -1.82% | -1.82% | -1.76% | -1.69% | -1.69% |  | 
GolombRiceParameterAdaptation disabled in proposal and anchor

## Slide 13: Conclusions
Context coding of coefficient values using SigMap, GT1, GT2 can generate BD-rate losses
  For lossless coding and SVT-16 content
At low QPs the percentage of these flags that are set approaches 100%
  Bins are efficiently coded
  Flags provide little information about coefficient value
Proposal introduces a technique to adapt coefficient coding
  Shifts the position of the significance test
    Allows the ratio of SigMap, GT1 and GT2 flags that are set to be maintained for all QP
    Flags are used to code more predictable portion of the coefficient
    Noisy LSBs coded separately
  Works well in combination with rice coding modifications previously adopted in VVC v2
    With or without Golumb-Rice parameter adaptation (history)
  Provides gains for SVT content and lossless coding