## Slide 1: JVET-W0106: EE2-related: Bilateral matching AMVP-merge mode
Zhi Zhang, Han Huang, Chun-Chi Chen, Vadim Seregin, Marta Karczewicz

## Slide 2: Introduction
        Bilateral Matching in ECM-1.0
Applied to a regular merge mode
Bilateral MV refinement
  To the whole coding block
  To each 16 × 16 subblock within the coding block
        Proposed method: Bilateral Matching AMVP-merge mode
Composed of an AMVP predictor and a merge predictor
AMVP part is signaled as a regular uni-directional AMVP
Merge part is implicitly derived by minimizing the bilateral matching cost between the AMVP predictor and a merge predictor
AMVR and BCW parameters set to the default values IMV_OFF and BCW_DEFAULT
Affine and SMVD are not used together with the proposed mode

## Slide 3: MV derivation
        Select a merge candidate base on minimum bilateral matching cost
A valid merge candidate has a predictor at direction (1 ̶ LX)
A valid pair of merge and AMVP reference blocks has one reference picture from the past and one reference picture from the future relatively to the current picture
        Apply bilateral matching MV refinement to the selected MV pair
        Set refined merge-MV to merge direction
        Set refined AMVP-MV + signaled MVD to AMVP direction

## Slide 4: Simulation results
        Results over ECM-1.0
        Results over ECM-1.0 with template matching disabled
 | Random Access |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.07% | -0.02% | -0.19% | 106% | 99%
Class A2 | -0.10% | -0.12% | -0.06% | 106% | 99%
Class B | -0.11% | -0.02% | -0.04% | 106% | 99%
Class C | -0.14% | -0.07% | -0.22% | 106% | 99%
Class E |  |  |  |  | 
Overall | -0.11% | -0.05% | -0.12% | 106% | 99%
Class D | -0.11% | -0.11% | 0.06% | 106% | 99%
Class F | -0.08% | 0.00% | 0.02% | 105% | 100%
 | Random Access |  |  |  | 
 | Over ECM-1.0 TM OFF |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.36% | -0.21% | -0.27% | 110% | 100%
Class A2 | -0.50% | -0.51% | -0.49% | 109% | 99%
Class B | -0.46% | -0.41% | -0.32% | 110% | 100%
Class C | -0.56% | -0.58% | -0.46% | 110% | 100%
Class E |  |  |  |  | 
Overall | -0.48% | -0.44% | -0.38% | 110% | 100%
Class D | -0.65% | -0.69% | -0.91% | 110% | 100%
Class F | -0.26% | -0.31% | -0.25% | 109% | 101%
        Both anchor and test disable template matching