## Slide 1: JVET-W0110 AHG12: GPM with inter and intra prediction
Y. Kidani, H. Kato and K. Kawamura
KDDI Corp. (KDDI Research Inc.)

## Slide 2: Summary
Motivation
  In current GPM, the pred. signal is generated from the sample-wise weighted combination of two uni-pred. signals for non-rectangular split regions.
  The couple of the two MVs are obtained from a merge candidate list.
  However, GPM has room to improve coding performance if the two pred. signals can be generated from not only inter pred. pixels but also intra pred. pixels.
Proposal
  GPM with inter and intra pred. is proposed.
  Pre-defined intra modes against GPM-splitting line can be selected in addition to merge candidates for each GPM-separated region.
  With the proposal, GPM can be applied to the uni-pred. CU where GPM is restricted in VVC.
Simulation results (over VTM-11.0+MCTF)
  RA: BD-rate YUV: -0.18%, -0.51%, -0.36%; EncT: 102%; DecT: 101%
  LB: BD-rate YUV: -0.43%, -1.00%, -1.00%; EncT: 103%; DecT: 106%
  LP: BD-rate YUV: -1.01%, -1.84%, -1.81%; EncT: 111%; DecT: 101%

## Slide 3: Proposal
GPM with intra and inter
  Whether intra or inter pred. mode is determined for each GPM-separated region with a flag.
  Inter pred. signal is generated by MVs from the merge candidate list.
  Intra pred. signal is generated from the neighboring pixels for the intra pred. mode specified by an index from the encoder.
    The variation of the possible intra pred. modes is restricted by the geometric shapes.
  Two uni-pred. signals are blended with the same way of ordinary GPM.
Variation of intra pred. modes
  Test 1: Parallel and perpendicular modes against the GPM-splitting line.
  Test 2: Test 1 plus Planar mode.
Inter
Intra
GPM-splitting line
parallel
perpendicular

## Slide 4: Simulation results over VTM-11.0+MCTF
 |  |  | RA |  |  |  |  | LB |  |  |  |  | LP |  | 
Class | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | _DecT
A1 | -0.07% | -0.37% | -0.28% | 101% | 100% |  |  |  |  |  |  |  |  |  | 
A2 | -0.06% | -0.15% | -0.21% | 102% | 101% |  |  |  |  |  |  |  |  |  | 
B | -0.12% | -0.53% | -0.34% | 101% | 101% | -0.37% | -1.03% | -1.05% | 103% | 104% | -0.74% | -1.83% | -1.42% | 109% | 101%
C | -0.33% | -0.61% | -0.40% | 101% | 102% | -0.57% | -0.86% | -1.31% | 103% | 107% | -1.39% | -2.87% | -2.85% | 110% | 101%
E |  |  |  |  |  | -0.06% | -0.57% | -0.64% | 103% | 107% | -0.54% | -0.47% | -0.87% | 108% | 103%
Overall | -0.15% | -0.45% | -0.32% | 101% | 101% | -0.36% | -0.86% | -1.04% | 103% | 106% | -0.91% | -1.84% | -1.76% | 109% | 101%
D | -0.19% | -0.46% | -0.36% | 102% | 101% | -0.43% | -1.27% | -1.51% | 102% | 104% | -0.80% | -3.40% | -1.55% | 109% | 101%
F | -0.12% | -0.31% | -0.37% | 100% | 101% | -0.42% | -0.42% | -0.74% | 102% | 107% | -0.60% | -0.75% | -1.29% | 106% | 102%
 |  |  | RA |  |  |  |  | LB |  |  |  |  | LP |  | 
Class | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | _DecT
A1 | -0.05% | -0.57% | -0.24% | 102% | 101% |  |  |  |  |  |  |  |  |  | 
A2 | -0.09% | -0.27% | -0.21% | 102% | 101% |  |  |  |  |  |  |  |  |  | 
B | -0.15% | -0.55% | -0.50% | 102% | 101% | -0.41% | -1.27% | -1.11% | 103% | 104% | -0.82% | -1.78% | -1.48% | 110% | 101%
C | -0.38% | -0.58% | -0.41% | 102% | 102% | -0.65% | -0.92% | -1.59% | 104% | 107% | -1.57% | -2.73% | -2.56% | 112% | 101%
E |  |  |  |  |  | -0.19% | -0.65% | -0.02% | 103% | 108% | -0.59% | -0.74% | -1.38% | 110% | 102%
Overall | -0.18% | -0.51% | -0.36% | 102% | 101% | -0.43% | -1.00% | -1.00% | 103% | 106% | -1.01% | -1.84% | -1.81% | 111% | 101%
D | -0.21% | -0.37% | -0.43% | 102% | 101% | -0.35% | -1.40% | -1.13% | 103% | 106% | -0.94% | -2.91% | -1.48% | 109% | 101%
F | -0.15% | -0.40% | -0.36% | 101% | 101% | -0.46% | -0.51% | -0.47% | 103% | 107% | -0.69% | -1.09% | -1.18% | 108% | 102%
Test 2: Test 1 plus Planar mode.
Test1: Parallel and perpendicular modes against the GPM-splitting line.

## Slide 5: Simulation results over ECM-1.0
 |  |  | RA |  |  |  |  | LB |  |  |  |  | LP |  | 
Class | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | _DecT
A1 | -0.04% | -0.39% | -0.10% | 101% | 100% |  |  |  |  |  |  |  |  |  | 
A2 | -0.06% | -0.18% | -0.06% | 101% | 100% |  |  |  |  |  |  |  |  |  | 
B | -0.04% | -0.31% | -0.35% | 101% | 100% | -0.13% | -0.36% | -0.07% | 100% | 100% | -0.29% | -1.01% | -1.05% | 106% | 101%
C | -0.07% | -0.26% | -0.29% | 101% | 100% | -0.19% | -1.01% | -0.82% | 100% | 99% | -0.47% | -1.20% | -1.66% | 106% | 100%
E |  |  |  |  |  | -0.12% | -0.47% | -0.32% | 101% | 101% | -0.05% | 0.58% | 0.34% | 107% | 101%
Overall | -0.05% | -0.29% | -0.23% | 101% | 100% | -0.15% | -0.60% | -0.39% | 101% | 100% | -0.29% | -0.68% | -0.91% | 106% | 101%
D | -0.04% | -0.23% | 0.00% | 101% | 101% | -0.02% | -0.21% | -0.32% | 100% | 101% | -0.38% | -1.00% | -0.71% | 105% | 101%
F | -0.01% | -0.16% | -0.04% | 100% | 101% | 0.00% | -0.19% | 0.33% | 100% | 101% | -0.13% | -0.73% | -0.83% | 103% | 101%
 |  |  | RA |  |  |  |  | LB |  |  |  |  | LP |  | 
Class | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | _DecT
A1 | -0.03% | -0.32% | -0.11% | 102% | 100% |  |  |  |  |  |  |  |  |  | 
A2 | -0.01% | -0.13% | -0.03% | 102% | 100% |  |  |  |  |  |  |  |  |  | 
B | -0.02% | -0.33% | -0.31% | 102% | 101% | -0.15% | -0.85% | -0.41% | 101% | 100% | -0.33% | -1.08% | -0.86% | 107% | 100%
C | -0.10% | -0.33% | -0.18% | 101% | 101% | -0.28% | -1.17% | -0.80% | 101% | 100% | -0.65% | -1.42% | -1.64% | 106% | 100%
E |  |  |  |  |  | -0.19% | -0.50% | -0.16% | 103% | 101% | -0.08% | -0.03% | -0.05% | 107% | 102%
Overall | -0.04% | -0.29% | -0.18% | 101% | 100% | -0.20% | -0.87% | -0.48% | 101% | 100% | -0.38% | -0.93% | -0.92% | 107% | 101%
D | -0.05% | 0.08% | 0.00% | 101% | 100% | -0.08% | -0.23% | -1.00% | 101% | 100% | -0.41% | -0.75% | -0.62% | 104% | 101%
F | 0.01% | 0.00% | 0.05% | 101% | 101% | 0.09% | -0.02% | -0.02% | 101% | 101% | -0.22% | -0.60% | -0.97% | 103% | 100%
Test 2: Test 1 plus Planar mode.
Test1: Parallel and perpendicular modes against the GPM-splitting line.

## Slide 6: Conclusion
Proposal
  GPM with inter and intra prediction is proposed.
  Pre-defined intra modes against GPM line can be selected in addition to merge candidates for each GPM-separated region.
  With the proposal, GPM can be applied to the uni-pred. CU where GPM is restricted in VVC.
Results over VTM-11.0+MCTF
  RA: BD-rate YUV: -0.18%, -0.51%, -0.36%; EncT: 102%; DecT: 101%
  LB: BD-rate YUV: -0.43%, -1.00%, -1.00%; EncT: 103%; DecT: 106%
  LP: BD-rate YUV: -1.01%, -1.84%, -1.81%; EncT: 111%; DecT: 101%
Results over ECM-1.0
  RA: BD-rate YUV: -0.04%, -0.29%, -0.18%; EncT: 101%; DecT: 100%
  LB: BD-rate YUV: -0.20%, -0.87%, -0.48%; EncT: 101%; DecT: 100%
  LP: BD-rate YUV: -0.38%, -0.93%, -0.92%; EncT: 107%; DecT: 101%
Recommend the proposal will be studied in the next EE2.
  This work was supported by Ministry of Internal Affairs and Communications (MIC) of Japan (Grant no. JPJ000595).

## Slide 7: Subjective evaluation and analysis of GPM-applied blocks (BQMall)

## Slide 8: LB, QP=37, VTM-11.0+MCTF, POC=68
Gray: Inter
Green: Intra/Parallel
Blue: Intra/Perpendicular
Red: Intra/Planar

## Slide 9: LB, QP=37, Test 2 over VTM-11.0+MCTF, POC=68
Gray: Inter
Green: Intra/Parallel
Blue: Intra/Perpendicular
Red: Intra/Planar

## Slide 10: LB, QP=37, VTM-11.0+MCTF, POC=68
Gray: Inter
Green: Intra/Parallel
Blue: Intra/Perpendicular
Red: Intra/Planar

## Slide 11: LB, QP=37, Test 2 over VTM-11.0+MCTF, POC=68
Gray: Inter
Green: Intra/Parallel
Blue: Intra/Perpendicular
Red: Intra/Planar

## Slide 12: LB, QP=37, VTM-11.0+MCTF, POC=79
Gray: Inter
Green: Intra/Parallel
Blue: Intra/Perpendicular
Red: Intra/Planar

## Slide 13: LB, QP=37, Test 2 over VTM-11.0+MCTF, POC=79
Gray: Inter
Green: Intra/Parallel
Blue: Intra/Perpendicular
Red: Intra/Planar

## Slide 14: LB, QP=37, VTM-11.0+MCTF, POC=79
Gray: Inter
Green: Intra/Parallel
Blue: Intra/Perpendicular
Red: Intra/Planar

## Slide 15: LB, QP=37, Test 2 over VTM-11.0+MCTF, POC=79
Gray: Inter
Green: Intra/Parallel
Blue: Intra/Perpendicular
Red: Intra/Planar