## Slide 1: AHG11: neural network based cross-component prediction model
Liqiang Wang, Sheng Lin, Renjie Chang, Xiaozhong Xu and Shan Liu
Tencent

## Slide 2: Outline
Introduction
Proposed method
Results
Conclusions

## Slide 3: Introduction
Cross-component linear model prediction (CCLM) is adopted in VVC.
In this contribution, an alternative model is built, but by the neural network.

## Slide 4: Proposed Method
The pre-processing unit in this contribution.
The n is set to 4 in the pre-processing unit.

## Slide 5: Proposed Method
The network structure of the proposed method.
                The number of ResBlock is set to 8.
                As for the internal convolutional layers, the number of feature maps is set as 32.

## Slide 6: Proposed Method
Network information in training and inference stage.
Network Information in Inference Stage |  | 
Mandatory | HW environment: | 
 | GPU Type | CPU only
 | Framework: | PyTorch v1.5
 | Number of GPUs per Task | 0
 | Total Parameter Number | 150.15k
 | Parameter Precision (Bits) | 32
 | Memory Parameter (MB) | 0.600488
 | Multiplay Accumulate (MAC) | 166k/pixel
Optional |  | 
 | Total Conv. Layers | 27
 | Total FC Layers | 0
 | Total Memory (MB) | 
 | Batch size: | 
 | Patch size | 
 | Changes to network configuration or weights required to generate rate points | 
 | Peak Memory Usage (Total) | 
 | Peak Memory Usage (per Model) | 
 | Border handling | 
 | Other information: | 
Network Information in Training Stage |  | 
Mandatory | GPU Type | GPU: V100
 | Framework: | PyTorch v1.5
 | Number of GPUs per Task | 1
 | Epoch: | 500
 | Batch size: | 16
 | Loss function: | L1
 | Training time: | 50h
 | Training data information: | DIV2K
 | Training configurations for generating compressed training data (if different to VTM CTC): | QP = 22, 27, 32, 37, 42
Optional |  | 
 | Number of iterations | 
 | Patch size | 32*32
 | Learning rate: | 1e-4
 | Optimizer: | ADAM
 | Preprocessing: | 
 | Mini-batch selection process: | 
 | Other information: | 

## Slide 7: Results
The anchor is VTM11+V0056, and the 2s results are provided.
      Test 1: NNCCP is only enabled for 8x8, 16x16 and 32x32 chroma blocks.
Test 2: NNCCP is enabled for all chroma blocks, which is same as CCLM.

## Slide 8: Results
Additionally, the CTC result of Test 1 is also provided.
      Test 1: NNCCP is only enabled for 8x8, 16x16 and 32x32 chroma blocks.

## Slide 9: Conclusions
Propose a NN-based cross-component prediction method.
Simulation results show that additional BD rate saving can be achieved.