## Slide 1
CE-related: High throughput mode for high bit-depth coding – harmonization of CE-3.2 and CE-1.1 – (JVET-W0114)
T. Tsukuba, M. Ikeda, T. Suzuki

## Slide 2: Summary
Motivation
  CE-3.2 (JVET-W0045) proposes CABAC high throughput mode.
    Roughly 0.1% loss (G) in BD-bitrate and -37% gain in weighted BD-binrate for SVT 16-bit/AI/low QPs
    There is room to further improve throughput by bypass-coding last coefficient position.
  CE-1.1 (JVET-W0046) proposes modifications to last coefficient coding.
    Useful to reduce the number of bins of last coefficient position: Roughly -0.3% gain (G) in BD-bitrate and -4.2% gain in weighted BD-binrate for SVT 16-bit/AI/low QPs
Proposal
  Harmonize CE-3.2 and CE-1.1 in order to fully bypass-code all syntax in residual coding
    bypass-code last coefficient position in RRC and conduct bypass alignment at the beginning of TB in RRC
    Roughly 0.3% loss (G) in BD-bitrate and -44% gain in weighted BD-binrate for SVT 16-bit/AI/low QPs.
  Apply only to High throughput 16-bit 4:4:4 profile

## Slide 3: Proposed changes relative to CE-3.2 in RRC
CE-3.2
Proposal
Apply CE-1.1 technique
    Bypass-code last coefficient position in RRC
    Conduct bypass alignment at the beginning of TB in RRC
    Apply CE-1.1 technique to last coefficient coding
    Enable only for high throughput 16-bit 4:4:4 profile

## Slide 4: Pseudocode for RRC
CE-3.2
Proposal

## Slide 5: Coding performance over VTM-13.0 for SVT-16 sequences at low QPs
SVT RGB |  |  | AI |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrG | psnrB | psnrR | psnrG | psnrB | psnrR | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
SVT16 | 0.26% | 0.17% | 0.15% | -43.76% | -43.78% | -43.79% | 1.16 | 1.01 | -12.91% | 0.47 | 0.26 | -43.76% | 81% | 71%
 |  |  | LDB |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrG | psnrB | psnrR | psnrG | psnrB | psnrR | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
SVT16 | 0.31% | 0.31% | 0.31% | -44.73% | -44.69% | -44.69% | 1.16 | 1.01 | -12.84% | 0.47 | 0.26 | -43.37% | 90% | 79%
 |  |  | RA |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrG | psnrB | psnrR | psnrG | psnrB | psnrR | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
SVT16 | 0.35% | 0.35% | 0.35% | -45.10% | -45.04% | -45.04% | 1.15 | 1.01 | -12.55% | 0.46 | 0.26 | -42.40% | 92% | 78%
Loss in BD-bitrate is minor but significant gain in BD-binrate (weighted) and Bin-to-bit ratio (weighed)
Note: BD-binrate and Bin-to-bit ratio were measured based on JVET-N0049 and JVET-V0150

## Slide 6: Estimated clock cycle at low QPs
To measure the throughput performance of the proposed method, the clock cycle is estimated for VTM-13.0 and the proposed method based on the method in JVET-W0044.
Assumed that VTM can process 4 bypass-coded bin per cycle while the proposed method can process 12 bypass coded bins.
Clk Cycle in MHz = (((totalCtxBins + totalbypassBin/bypassWeight)* numCodedFrame)/framerate)/1000000
where,
totalCtxBins = Total number of context coded bins in the sequence
totalbypassBin = Total number of bypass coded bins
bypassWeight is the number of bypass coded bins can be parsed per cycle. For anchor, bypassWeight is equal to 4. For proposed method, the bypassWeight is equal to 12.
numCodedFrame is the total number of encoded frames
Estimated saving of clock cycle over VTM-13.0
Estimated max clock cycle
Chart: clk cycle TRF bin MHz
| SVT-AI16-OldTownCross | SVT-AI16-CrowdRun | SVT-AI16-DucksTakeOff | SVT-AI16-InToTree | SVT-AI16-ParkJoy
VTM-13.0 | 1435.4064 | 1423.5228 | 1441.4869 | 1404.7716 | 1420.3856
JVET-W0114 | 287.7131 | 282.8171 | 289.3214 | 277.4634 | 281.5589
 | SVT16 RGB
AI | 18%

## Slide 7: Coding performance over CE-3.2 for SVT-16 sequences at low QPs
SVT RGB |  |  | AI |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrG | psnrB | psnrR | psnrG | psnrB | psnrR | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
SVT16 | 0.19% | 0.08% | 0.07% | -9.85% | -9.95% | -9.95% | 1.04 | 1.01 | -2.61% | 0.29 | 0.26 | -10.08% | 95% | 90%
 |  |  | LDB |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrG | psnrB | psnrR | psnrG | psnrB | psnrR | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
SVT16 | -0.01% | -0.05% | -0.04% | -7.84% | -7.86% | -7.86% | 1.03 | 1.01 | -2.55% | 0.29 | 0.26 | -9.88% | 99% | 94%
 |  |  | RA |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrG | psnrB | psnrR | psnrG | psnrB | psnrR | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
SVT16 | 0.00% | -0.06% | -0.06% | -7.87% | -7.92% | -7.92% | 1.03 | 1.01 | -2.46% | 0.29 | 0.26 | -9.54% | 100% | 94%
Loss in BD-bitrate is negligible but additional gain in BD-binrate (weighted) and Bin-to-bit ratio (weighed)
Note: BD-binrate and Bin-to-bit ratio were measured based on JVET-N0049 and JVET-V0150

## Slide 8: Conclusion
This contribution proposes a harmonization of CE-3.2 and CE-1.1
  Bypass-code last coefficient position in RRC
  Conduct bypass alignment at the beginning of TB in RRC
  Apply it only to High throughput 16-bit 4:4:4 profile
Results for SVT-16 sequences at low QPs: minor loss but large gain in BD-binrate/Bin2Bit
It is recommended to study it in next CE
Thanks to OPPO for cross-checking
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrG | psnrB | psnrR | psnrG | psnrB | psnrR | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
SVT16/AI | 0.26% | 0.17% | 0.15% | -43.76% | -43.78% | -43.79% | 1.16 | 1.01 | -12.91% | 0.47 | 0.26 | -43.76% | 81% | 71%
SVT16/LB | 0.31% | 0.31% | 0.31% | -44.73% | -44.69% | -44.69% | 1.16 | 1.01 | -12.84% | 0.47 | 0.26 | -43.37% | 90% | 79%
SVT16/RA | 0.35% | 0.35% | 0.35% | -45.10% | -45.04% | -45.04% | 1.15 | 1.01 | -12.55% | 0.46 | 0.26 | -42.40% | 92% | 78%

## Slide 10: Estimated clock cycle at low QPs
 | HDR PQ | HDR HLG | SVT12 RGB | SVT16 RGB
AI | 33% | 12% | 15% | 18%
Chart: clk cycle TRF bin MHz
| SVT-AI16-OldTownCross | SVT-AI16-CrowdRun | SVT-AI16-DucksTakeOff | SVT-AI16-InToTree | SVT-AI16-ParkJoy | SVT-AI12-OldTownCross | SVT-AI12-CrowdRun | SVT-AI12-DucksTakeOff | SVT-AI12-InToTree | SVT-AI12-ParkJoy | HLG-AI444-DayStreet | HLG-AI444-PeopleInShoppingCenter | HLG-AI444-NightStreet | HLG-AI444-StainedGlass | HLG-AI422-DayStreet | HLG-AI422-PeopleInShoppingCenter | HLG-AI422-NightStreet | HLG-AI422-StainedGlass | PQ-AI444-BalloonFestival | PQ-AI444-Hurdles | PQ-AI444-Market3 | PQ-AI444-Starting | PQ-AI444-FireEater | PQ-AI422-BalloonFestival | PQ-AI422-Hurdles | PQ-AI422-Market3 | PQ-AI422-Starting | PQ-AI422-FireEater
VTM-13.0 | 1435.4064 | 1423.5228 | 1441.4869 | 1404.7716 | 1420.3856 | 1157.3865 | 1136.5258 | 1163.3941 | 1119.0342 | 1132.484 | 1056.1473 | 1063.6004 | 1155.378 | 1103.6573 | 727.6672 | 729.2597 | 781.649 | 757.6424 | 179.0838 | 681.3877 | 817.9398 | 615.8352 | 299.7177 | 136.498 | 524.0917 | 576.3757 | 474.5208 | 226.7393
JVET-W0114 | 287.7131 | 282.8171 | 289.3214 | 277.4634 | 281.5589 | 201.4699 | 196.3065 | 203.0497 | 191.1616 | 195.1033 | 150.4697 | 153.0538 | 176.7862 | 165.5429 | 106.6831 | 107.7388 | 120.7742 | 115.7062 | 70.7716 | 288.822 | 330.1535 | 265.7281 | 96.574 | 55.326 | 223.5017 | 244.6672 | 202.4934 | 74.329
SVT-AI16
SVT-AI12
HLG-AI
PQ-AI
Estimated saving of clock cycle over VTM-13.0

## Slide 11: Coding performance over VTM-13.0 for SVT 16/12-bit sequences at low QPs
SVT RGB |  |  | AI |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrG | psnrB | psnrR | psnrG | psnrB | psnrR | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
SVT16 | 0.26% | 0.17% | 0.15% | -43.76% | -43.78% | -43.79% | 1.16 | 1.01 | -12.91% | 0.47 | 0.26 | -43.76% | 81% | 71%
SVT12 | 1.76% | 1.76% | 1.75% | -52.25% | -52.24% | -52.24% | 1.17 | 1.01 | -13.40% | 0.58 | 0.27 | -53.20% | 83% | 76%
Overall | 1.01% | 0.96% | 0.95% | -48.00% | -48.01% | -48.02% | 1.16 | 1.01 | -13.16% | 0.52 | 0.27 | -48.96% | 82% | 73%
 |  |  | LDB |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrG | psnrB | psnrR | psnrG | psnrB | psnrR | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
SVT16 | 0.31% | 0.31% | 0.31% | -44.73% | -44.69% | -44.69% | 1.16 | 1.01 | -12.84% | 0.47 | 0.26 | -43.37% | 90% | 79%
SVT12 | 3.08% | 3.36% | 3.35% | -55.29% | -55.24% | -55.23% | 1.17 | 1.01 | -13.41% | 0.57 | 0.27 | -52.59% | 82% | 80%
Overall | 1.70% | 1.84% | 1.83% | -50.01% | -49.96% | -49.96% | 1.16 | 1.01 | -13.13% | 0.52 | 0.27 | -48.44% | 86% | 79%
 |  |  | RA |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrG | psnrB | psnrR | psnrG | psnrB | psnrR | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
SVT16 | 0.35% | 0.35% | 0.35% | -45.10% | -45.04% | -45.04% | 1.15 | 1.01 | -12.55% | 0.46 | 0.26 | -42.40% | 92% | 78%
SVT12 | 3.61% | 3.88% | 3.86% | -56.03% | -55.96% | -55.95% | 1.17 | 1.01 | -13.30% | 0.56 | 0.27 | -51.29% | 80% | 80%
Overall | 1.98% | 2.12% | 2.11% | -50.56% | -50.50% | -50.50% | 1.16 | 1.01 | -12.92% | 0.51 | 0.27 | -47.26% | 86% | 79%
Note: BD-binrate and Bin-to-bit ratio were measured based on JVET-N0049 and JVET-V0150

## Slide 12: Coding performance over VTM-13.0 for HLG 12-bit sequences at low QPs
HDR HLG |  |  | AI |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrY | psnrU | psnrV | psnrY | psnrU | psnrV | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
HLG444 | 7.48% | 8.88% | 9.48% | -60.70% | -60.24% | -59.84% | 1.24 | 1.02 | -17.80% | 0.80 | 0.29 | -63.18% | 89% | 78%
HLG422 | 6.79% | 7.96% | 8.40% | -58.75% | -58.30% | -57.93% | 1.23 | 1.02 | -16.86% | 0.77 | 0.30 | -61.39% | 85% | 79%
Overall | 7.14% | 8.42% | 8.94% | -59.72% | -59.27% | -58.89% | 1.24 | 1.02 | -17.33% | 0.78 | 0.29 | -62.30% | 87% | 78%
 |  |  | LDB |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrY | psnrU | psnrV | psnrY | psnrU | psnrV | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
HLG444 | 17.51% | 18.41% | 19.33% | -66.50% | -66.13% | -65.70% | 1.25 | 1.02 | -17.99% | 0.81 | 0.30 | -63.67% | 72% | 81%
HLG422 | 18.57% | 19.37% | 19.71% | -64.78% | -64.49% | -64.11% | 1.23 | 1.03 | -16.80% | 0.78 | 0.30 | -61.32% | 69% | 80%
Overall | 18.04% | 18.89% | 19.52% | -65.64% | -65.31% | -64.90% | 1.24 | 1.02 | -17.40% | 0.80 | 0.30 | -62.52% | 70% | 81%
 |  |  | RA |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrY | psnrU | psnrV | psnrY | psnrU | psnrV | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
HLG444 | 17.87% | 18.43% | 19.18% | -66.44% | -66.21% | -65.88% | 1.24 | 1.02 | -17.17% | 0.79 | 0.29 | -62.53% | 70% | 81%
HLG422 | 18.82% | 19.01% | 19.35% | -64.78% | -64.72% | -64.36% | 1.22 | 1.03 | -16.14% | 0.75 | 0.30 | -60.20% | 67% | 80%
Overall | 18.35% | 18.72% | 19.26% | -65.61% | -65.46% | -65.12% | 1.23 | 1.02 | -16.66% | 0.77 | 0.30 | -61.39% | 68% | 81%
Note: BD-binrate and Bin-to-bit ratio were measured based on JVET-N0049 and JVET-V0150

## Slide 13: Coding performance over VTM-13.0 for PQ 12-bit sequences at low QPs
HDR PQ |  |  | AI |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrY | psnrU | psnrV | PsnrY | PsnrU | PsnrV | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
PQ444 | 13.37% | 15.63% | 16.23% | -60.28% | -59.76% | -59.44% | 1.27 | 1.04 | -18.55% | 0.90 | 0.32 | -64.36% | 94% | 87%
PQ422 | 11.05% | 12.70% | 12.85% | -59.59% | -58.98% | -58.65% | 1.26 | 1.04 | -18.10% | 0.87 | 0.32 | -63.09% | 92% | 86%
Overall | 12.21% | 14.17% | 14.54% | -59.94% | -59.37% | -59.04% | 1.27 | 1.04 | -18.32% | 0.88 | 0.32 | -63.73% | 93% | 87%
 |  |  | LDB |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrY | psnrU | psnrV | PsnrY | PsnrU | PsnrV | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
PQ444 | 20.21% | 23.85% | 24.55% | -61.65% | -60.67% | -60.53% | 1.26 | 1.04 | -17.57% | 0.89 | 0.32 | -64.09% | 89% | 89%
PQ422 | 19.04% | 21.86% | 22.49% | -61.14% | -60.46% | -60.05% | 1.24 | 1.04 | -16.20% | 0.83 | 0.32 | -61.34% | 84% | 88%
Overall | 19.63% | 22.85% | 23.52% | -61.40% | -60.57% | -60.29% | 1.25 | 1.04 | -16.89% | 0.86 | 0.32 | -62.77% | 86% | 89%
 |  |  | RA |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrY | psnrU | psnrV | PsnrY | PsnrU | PsnrV | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
PQ444 | 19.98% | 23.12% | 24.51% | -61.85% | -61.00% | -60.60% | 1.23 | 1.04 | -15.82% | 0.84 | 0.32 | -61.80% | 88% | 90%
PQ422 | 18.67% | 21.41% | 22.01% | -61.34% | -60.59% | -60.19% | 1.22 | 1.04 | -15.39% | 0.80 | 0.32 | -60.30% | 83% | 88%
Overall | 19.32% | 22.27% | 23.26% | -61.59% | -60.79% | -60.39% | 1.23 | 1.04 | -15.61% | 0.82 | 0.32 | -61.06% | 85% | 89%
Note: BD-binrate and Bin-to-bit ratio were measured based on JVET-N0049 and JVET-V0150

## Slide 14: Coding performance over VTM-13.0 for PQ 12-bit sequences at low QPs
HDR PQ |  |  | AI |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 13.42% | 15.70% | 16.18% | 13.11% | 15.43% | 16.01% | 95% | 87%
PQ422 | 11.07% | 12.95% | 13.06% | 11.00% | 12.82% | 13.01% | 90% | 86%
Overall | 12.24% | 14.32% | 14.62% | 12.06% | 14.13% | 14.51% | 92% | 86%
 |  |  | LDB |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 13.15% | 14.57% | 14.83% | 12.83% | 14.33% | 14.68% | 93% | 86%
PQ422 | 20.80% | 24.35% | 24.72% | 20.21% | 23.85% | 24.55% | 89% | 89%
Overall | 16.97% | 19.46% | 19.77% | 16.52% | 19.09% | 19.61% | 91% | 88%
 |  |  | RA |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 19.58% | 22.34% | 22.63% | 19.04% | 21.86% | 22.49% | 84% | 88%
PQ422 | 20.51% | 23.52% | 24.59% | 19.98% | 23.12% | 24.51% | 88% | 90%
Overall | 20.05% | 22.93% | 23.61% | 19.51% | 22.49% | 23.50% | 86% | 89%

## Slide 15: Coding performance over CE-3.2 for SVT 16/12-bit sequences at low QPs
SVT RGB |  |  | AI |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrG | psnrB | psnrR | psnrG | psnrB | psnrR | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
SVT16 | 0.19% | 0.08% | 0.07% | -9.85% | -9.95% | -9.95% | 1.04 | 1.01 | -2.61% | 0.29 | 0.26 | -10.08% | 95% | 90%
SVT12 | 0.24% | 0.06% | 0.06% | -12.47% | -12.63% | -12.63% | 1.05 | 1.01 | -3.35% | 0.31 | 0.27 | -12.58% | 100% | 91%
Overall | 0.22% | 0.07% | 0.07% | -11.16% | -11.29% | -11.29% | 1.04 | 1.01 | -2.98% | 0.30 | 0.27 | -11.36% | 98% | 91%
 |  |  | LDB |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrG | psnrB | psnrR | psnrG | psnrB | psnrR | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
SVT16 | -0.01% | -0.05% | -0.04% | -7.84% | -7.86% | -7.86% | 1.03 | 1.01 | -2.55% | 0.29 | 0.26 | -9.88% | 99% | 94%
SVT12 | 0.08% | 0.06% | 0.07% | -9.17% | -9.17% | -9.17% | 1.05 | 1.01 | -3.38% | 0.31 | 0.27 | -12.66% | 100% | 95%
Overall | 0.03% | 0.01% | 0.01% | -8.51% | -8.52% | -8.52% | 1.04 | 1.01 | -2.97% | 0.30 | 0.27 | -11.31% | 100% | 94%
 |  |  | RA |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrG | psnrB | psnrR | psnrG | psnrB | psnrR | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
SVT16 | 0.00% | -0.06% | -0.06% | -7.87% | -7.92% | -7.92% | 1.03 | 1.01 | -2.46% | 0.29 | 0.26 | -9.54% | 100% | 94%
SVT12 | 0.20% | 0.18% | 0.18% | -8.96% | -8.98% | -8.98% | 1.05 | 1.01 | -3.39% | 0.31 | 0.27 | -12.66% | 97% | 95%
Overall | 0.10% | 0.06% | 0.06% | -8.42% | -8.45% | -8.45% | 1.04 | 1.01 | -2.93% | 0.30 | 0.27 | -11.14% | 99% | 95%
Note: BD-binrate and Bin-to-bit ratio were measured based on JVET-N0049 and JVET-V0150

## Slide 16: Coding performance over CE-3.2 for HLG 12-bit sequences at low QPs
Note: BD-binrate and Bin-to-bit ratio were measured based on JVET-N0049 and JVET-V0150
HDR HLG |  |  | AI |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrY | psnrU | psnrV | psnrY | psnrU | psnrV | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
HLG444 | 0.80% | 0.32% | 0.33% | -12.51% | -12.78% | -12.72% | 1.05 | 1.02 | -3.15% | 0.34 | 0.29 | -13.33% | 113% | 95%
HLG422 | 0.69% | 0.30% | 0.31% | -13.03% | -13.27% | -13.24% | 1.06 | 1.02 | -3.36% | 0.34 | 0.30 | -13.70% | 107% | 94%
Overall | 0.74% | 0.31% | 0.32% | -12.77% | -13.02% | -12.98% | 1.06 | 1.02 | -3.26% | 0.34 | 0.29 | -13.52% | 110% | 94%
 |  |  | LDB |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrY | psnrU | psnrV | psnrY | psnrU | psnrV | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
HLG444 | 1.00% | 0.59% | 0.61% | -9.61% | -9.37% | -8.95% | 1.06 | 1.02 | -3.43% | 0.35 | 0.30 | -15.26% | 100% | 99%
HLG422 | 0.97% | 0.45% | 0.61% | -10.19% | -10.19% | -9.88% | 1.06 | 1.03 | -3.56% | 0.35 | 0.30 | -14.97% | 103% | 98%
Overall | 0.98% | 0.52% | 0.61% | -9.90% | -9.78% | -9.42% | 1.06 | 1.02 | -3.50% | 0.35 | 0.30 | -15.11% | 101% | 98%
 |  |  | RA |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrY | psnrU | psnrV | psnrY | psnrU | psnrV | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
HLG444 | 0.99% | 0.55% | 0.56% | -9.30% | -9.11% | -8.68% | 1.06 | 1.02 | -3.41% | 0.34 | 0.29 | -14.06% | 100% | 98%
HLG422 | 0.97% | 0.39% | 0.56% | -9.77% | -9.82% | -9.47% | 1.06 | 1.03 | -3.62% | 0.35 | 0.30 | -14.33% | 98% | 99%
Overall | 0.98% | 0.47% | 0.56% | -9.54% | -9.47% | -9.08% | 1.06 | 1.02 | -3.51% | 0.35 | 0.30 | -14.20% | 99% | 98%

## Slide 17: Coding performance over CE-3.2 for PQ 12-bit sequences at low QPs
HDR PQ |  |  | AI |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrY | psnrU | psnrV | PsnrY | PsnrU | PsnrV | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
PQ444 | 2.09% | 1.76% | 1.92% | -13.21% | -13.43% | -13.29% | 1.07 | 1.04 | -2.87% | 0.37 | 0.32 | -14.81% | 105% | 97%
PQ422 | 1.66% | 1.39% | 1.52% | -13.35% | -13.52% | -13.44% | 1.07 | 1.04 | -3.01% | 0.37 | 0.32 | -14.56% | 106% | 97%
Overall | 1.87% | 1.57% | 1.72% | -13.28% | -13.47% | -13.36% | 1.07 | 1.04 | -2.94% | 0.37 | 0.32 | -14.69% | 105% | 97%
 |  |  | LDB |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrY | psnrU | psnrV | PsnrY | PsnrU | PsnrV | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
PQ444 | 2.45% | 2.55% | 2.78% | -14.41% | -14.35% | -14.22% | 1.07 | 1.04 | -3.22% | 0.39 | 0.32 | -17.08% | 110% | 98%
PQ422 | 2.20% | 2.38% | 2.64% | -14.22% | -14.28% | -14.21% | 1.07 | 1.04 | -3.25% | 0.38 | 0.32 | -16.26% | 104% | 97%
Overall | 2.32% | 2.46% | 2.71% | -14.31% | -14.31% | -14.22% | 1.07 | 1.04 | -3.24% | 0.38 | 0.32 | -16.67% | 107% | 98%
 |  |  | RA |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrY | psnrU | psnrV | PsnrY | PsnrU | PsnrV | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
PQ444 | 2.40% | 2.42% | 2.62% | -14.17% | -14.17% | -14.07% | 1.07 | 1.04 | -3.08% | 0.38 | 0.32 | -15.85% | 107% | 99%
PQ422 | 2.14% | 2.23% | 2.47% | -13.88% | -14.00% | -13.95% | 1.07 | 1.04 | -3.35% | 0.38 | 0.32 | -15.97% | 107% | 97%
Overall | 2.27% | 2.33% | 2.55% | -14.03% | -14.08% | -14.01% | 1.07 | 1.04 | -3.21% | 0.38 | 0.32 | -15.91% | 107% | 98%
Note: BD-binrate and Bin-to-bit ratio were measured based on JVET-N0049 and JVET-V0150

## Slide 18: Coding performance over CE-3.2 for PQ 12-bit sequences at low QPs
HDR PQ |  |  | AI |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 2.27% | 1.94% | 2.11% | 2.27% | 1.95% | 2.12% | 105% | 97%
PQ422 | 1.81% | 1.49% | 1.63% | 1.80% | 1.48% | 1.63% | 104% | 97%
Overall | 2.04% | 1.71% | 1.87% | 2.03% | 1.72% | 1.88% | 105% | 97%
 |  |  | LDB |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 1.23% | 1.05% | 1.16% | 1.24% | 0.99% | 1.09% | 108% | 98%
PQ422 | 2.47% | 2.57% | 2.79% | 2.45% | 2.55% | 2.78% | 110% | 98%
Overall | 1.85% | 1.81% | 1.97% | 1.84% | 1.77% | 1.94% | 109% | 98%
 |  |  | RA |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 2.20% | 2.41% | 2.67% | 2.20% | 2.38% | 2.64% | 104% | 97%
PQ422 | 2.42% | 2.43% | 2.64% | 2.40% | 2.42% | 2.62% | 107% | 99%
Overall | 2.31% | 2.42% | 2.65% | 2.30% | 2.40% | 2.63% | 106% | 98%

## Slide 19: Coding performance over VTM-13.0 at lossless condition
PQ | All Intra |  |  | Low delay B |  |  | Random Access |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM13 | Test |  | VTM13 | Test |  | VTM13 | Test | 
PQ444 | 2.6 | 2.5 | 3.34% | 3.1 | 2.9 | 6.41% | 3.1 | 2.9 | 6.38%
PQ422 | 2.4 | 2.3 | 2.86% | 2.9 | 2.7 | 5.92% | 2.9 | 2.7 | 5.86%
Overall | 2.5 | 2.4 | 3.10% | 3.0 | 2.8 | 6.17% | 3.0 | 2.8 | 6.12%
Enc Time[%] | 104% |  |  | 95% |  |  | 91% |  | 
Dec Time[%] | 79% |  |  | 89% |  |  | 88% |  | 
HLG | All Intra |  |  | Low delay B |  |  | Random Access |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM13 | Test |  | VTM13 | Test |  | VTM13 | Test | 
HLG444 | 1.8 | 1.7 | 1.28% | 2.0 | 1.9 | 1.34% | 2.0 | 1.9 | 1.34%
HLG422 | 1.7 | 1.7 | 1.11% | 1.9 | 1.9 | 1.32% | 1.9 | 1.9 | 1.31%
Overall | 1.7 | 1.7 | 1.19% | 1.9 | 1.9 | 1.33% | 1.9 | 1.9 | 1.32%
Enc Time[%] | 107% |  |  | 86% |  |  | 91% |  | 
Dec Time[%] | 76% |  |  | 84% |  |  | 84% |  | 
SVT | All Intra |  |  | Low delay B |  |  | Random Access |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM13 | Test |  | VTM13 | Test |  | VTM13 | Test | 
SVT16 | 1.2 | 1.2 | -0.11% | 1.2 | 1.2 | -0.29% | 1.2 | 1.2 | -0.26%
SVT12 | 1.3 | 1.3 | 0.66% | 1.3 | 1.3 | 0.39% | 1.3 | 1.3 | 0.41%
Overall | 1.2 | 1.2 | 0.28% | 1.3 | 1.3 | 0.05% | 1.3 | 1.3 | 0.07%
Enc Time[%] | 88% |  |  | 92% |  |  | 90% |  | 
Dec Time[%] | 76% |  |  | 85% |  |  | 84% |  | 

## Slide 20: Coding performance over CE-3.2 at lossless condition
PQ | All Intra |  |  | Low delay B |  |  | Random Access |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM13 | Test |  | VTM13 | Test |  | VTM13 | Test | 
PQ444 | 2.5 | 2.5 | 0.18% | 2.9 | 2.9 | 0.03% | 2.9 | 2.9 | 0.00%
PQ422 | 2.3 | 2.3 | 0.19% | 2.7 | 2.7 | 0.08% | 2.7 | 2.7 | 0.04%
Overall | 2.4 | 2.4 | 0.19% | 2.8 | 2.8 | 0.06% | 2.8 | 2.8 | 0.02%
Enc Time[%] | 100% |  |  | 103% |  |  | 99% |  | 
Dec Time[%] | 103% |  |  | 113% |  |  | 112% |  | 
HLG | All Intra |  |  | Low delay B |  |  | Random Access |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM13 | Test |  | VTM13 | Test |  | VTM13 | Test | 
HLG444 | 1.8 | 1.7 | 0.29% | 1.9 | 1.9 | 0.02% | 1.9 | 1.9 | 0.01%
HLG422 | 1.7 | 1.7 | 0.23% | 1.9 | 1.9 | 0.06% | 1.9 | 1.9 | 0.04%
Overall | 1.7 | 1.7 | 0.26% | 1.9 | 1.9 | 0.04% | 1.9 | 1.9 | 0.02%
Enc Time[%] | 104% |  |  | 97% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 112% |  |  | 113% |  | 
SVT | All Intra |  |  | Low delay B |  |  | Random Access |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM13 | Test |  | VTM13 | Test |  | VTM13 | Test | 
SVT16 | 1.2 | 1.2 | 0.18% | 1.2 | 1.2 | -0.01% | 1.2 | 1.2 | 0.00%
SVT12 | 1.3 | 1.3 | 0.24% | 1.3 | 1.3 | -0.01% | 1.3 | 1.3 | -0.01%
Overall | 1.2 | 1.2 | 0.21% | 1.3 | 1.3 | -0.01% | 1.3 | 1.3 | -0.01%
Enc Time[%] | 97% |  |  | 101% |  |  | 101% |  | 
Dec Time[%] | 112% |  |  | 120% |  |  | 115% |  |