## Slide 1: JVET-W0123 EE2-related: Fusion for template-based intra mode derivation
Keming Cao, Nan Hu, Vadim Seregin, Marta Karczewicz (Qualcomm Inc.)
Yang Wang, Kai Zhang, Li Zhang (Bytedance Inc.)

## Slide 2: Fusion of TIMD modes
EE2-2.1: Template-based Intra Mode Derivation (TIMD)
            Compute SATD cost between prediction and reconstruction of templates
            Check each mode in MPM list and adjacent MPM modes
            Select a mode with the smallest SATD as TIMD mode
Proposed fusion of TIMD modes
            Select two TIMD modes with the smallest cost
            Compare the costs of those two modes with a threshold t (t=2 in the test), if true, the fusion will be applied, otherwise, use mode1 without the fusion:
            costMode2 < t*costMode1
            Weights in the fusion are derived based on the cost as follows:
            weight1 = costMode2/(costMode1+costMode2)
            weight2 = 1 – weight1

## Slide 3: Result
            On top of EE2-2.1, additional 0.1% gain in AI with similar runtime
            Test EE2-2.1: TIMD Proposed TIMD Fusion
            Thank Alibaba for cross-checking
 | All Intra Main10 |  | All Intra Main10 |  | 
 | Over ECM1.0 |  | Over ECM1.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.17% | -0.06% | -0.20% | 124% | 103%
Class A2 | -0.28% | -0.25% | -0.28% | 124% | 110%
Class B | -0.38% | -0.27% | -0.37% | 123% | 110%
Class C | -0.38% | -0.25% | -0.26% | 123% | 116%
Class E | -0.61% | -0.54% | -0.47% | 124% | 114%
Overall | -0.37% | -0.27% | -0.32% | 123% | 111%
Class D | -0.33% | -0.36% | -0.20% | 121% | 113%
Class F | -0.19% | 0.01% | -0.09% | 113% | 112%
 | Random access Main10 |  | Random access Main10 |  | 
 | Over ECM1.0 |  | Over ECM1.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.10% | 0.03% | -0.09% | 105% | 101%
Class A2 | -0.18% | -0.08% | -0.17% | 104% | 101%
Class B | -0.19% | -0.01% | -0.13% | 105% | 102%
Class C | -0.15% | 0.00% | -0.31% | 105% | 103%
Class E |  |  |  |  | 
Overall | -0.16% | -0.01% | -0.18% | 105% | 102%
Class D | -0.17% | 0.25% | 0.07% | 105% | 104%
Class F | -0.12% | -0.22% | -0.06% | 106% | 103%
 | All Intra Main10 |  | All Intra Main10 |  | 
 | Over ECM1.0 |  | Over ECM1.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.24% | -0.05% | -0.14% | 125% | 105%
Class A2 | -0.38% | -0.36% | -0.32% | 125% | 112%
Class B | -0.50% | -0.36% | -0.46% | 124% | 110%
Class C | -0.46% | -0.32% | -0.40% | 123% | 116%
Class E | -0.77% | -0.57% | -0.46% | 123% | 111%
Overall | -0.47% | -0.34% | -0.37% | 124% | 111%
Class D | -0.40% | -0.33% | -0.14% | 122% | 117%
Class F | -0.25% | -0.09% | -0.06% | 112% | 107%
 | Random access Main10 |  | Random access Main10 |  | 
 | Over ECM1.0 |  | Over ECM1.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.15% | -0.01% | -0.16% | 105% | 103%
Class A2 | -0.17% | -0.16% | -0.23% | 105% | 102%
Class B | -0.22% | -0.11% | -0.17% | 104% | 101%
Class C | -0.20% | -0.04% | -0.37% | 105% | 103%
Class E |  |  |  |  | 
Overall | -0.19% | -0.08% | -0.23% | 105% | 102%
Class D | -0.18% | -0.23% | -0.12% | 105% | 103%
Class F | -0.12% | -0.41% | -0.14% | 105% | 102%