## Slide 1: EE2-Related: DIMD with implicitly derived multiple blending modes (JVET-W0126)
Jie Zhao, Seethal Paluri, and Seung-Hwan Kim
LG Electronics

## Slide 2: Introduction
This proposal is based on techniques in both EE2-2.1 and 2.2.
  EE2-2.2 -- DIMD with multiple blending modes and
  EE2-2.1 – Template-based decoder mode derivation (TIMD)
Proposes a way to implicitly derive the DIMD blending modes using template-based method.
Performance:
  AI: -0.04% -0.04% -0.08% 101%(Enc) 112%(Dec)
  RA: -0.01% 0.00% -0.12% 100%(Enc) 100%(Dec)

## Slide 3: Background
In ECM1.0, one of the intra tools is Decoder Side Intra Mode Derivation (DIMD).
  Two intra modes are derived from the reconstructed neighboring samples based on Histogram of Gradients (HoG)
  Prediction is done by blending the predictions from planar and the two derived intra modes
  A dimd_flag is signalled
EE2-2.2 extends the DIMD to 3 blending modes.
  The 3 blending modes have different weights for planar and the two derived intra modes
  A DIMD index {0, 1, 2, 3) is signalled.
EE2-2.1 introduces template-based decoder side intra mode derivation using MPM.
  Given the template, mode with minimum SATD is chosen as TIMD mode
  A TIMD flag is signalled
EE2-2.1 and 2.2 both added additional full RDO checks to encoder, therefore they both have large encoding time increase ~20%.
Figure 1. Template and its reference samples used in TIMD

## Slide 4: Proposed Methods
  Proposes a way to implicitly derive the DIMD blending modes using template-based method.
  It shows another way of combining these two technologies in EE2-2.2 and EE2-2.1.
  Has 3 blending modes
  The best blending modes is selected based-on template-based method as in EE2-2.1, template and reference samples used are the same as those in EE2-2.1, as shown in Fig. 1.
  Given the template, for each blending mode, prediction is performed by blending the predictions from planar and the two HoG derived intra modes.
  The best blending mode is selected based on the SATD cost between prediction and reconstruction samples within the template.
  Does not add additional full RDO checks at encoder
  Dimd_flag signaling is the same as ECM1.0, no need to signal the blending mode. .
 | DIMD blend mode
1 | Blend predictions of Mode1, Mode2 and Planar(wP = 1/3) , i.e. the existing blending mode in ECM1.0
2 | Blend predictions of Mode2 and Planar (wP = 1/3)
3 | Blend predictions of Mode1 and Mode2

## Slide 5: Experimental Results & Conclusion
Implemented on top of ECM1.0, and also based on EE2-2.2 and 2.1 code
Small gain of 0.04% in AI, little encoding time change, 12% decoding time increase
 | All Intra Main10 |  |  |  | 
 | Over ECM1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | 0.00% | -0.11% | 101% | 107%
Class A2 | -0.02% | -0.03% | -0.05% | 101% | 110%
Class B | -0.04% | 0.00% | -0.07% | 101% | 111%
Class C | -0.01% | -0.03% | -0.11% | 102% | 119%
Class E | -0.11% | -0.20% | -0.03% | 102% | 114%
Overall | -0.04% | -0.04% | -0.08% | 101% | 112%
Class D | 0.00% | -0.22% | 0.08% | 102% | 122%
Class F | 0.05% | -0.02% | 0.03% | 100% | 106%
 | Random Access Main 10 |  |  |  | 
 | Over ECM1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.10% | -0.13% | 100% | 101%
Class A2 | 0.00% | 0.01% | -0.13% | 99% | 99%
Class B | -0.03% | 0.00% | 0.01% | 99% | 100%
Class C | -0.01% | 0.08% | -0.27% | 100% | 101%
Class E |  |  |  |  | 
Overall | -0.01% | 0.00% | -0.12% | 100% | 100%
Class D | -0.02% | 0.03% | 0.07% | 100% | 101%
Class F | 0.05% | -0.29% | -0.05% | 99% | 100%
Conclusion:
  Presented a method to implicitly derive the DIMD blending modes using template-based method.
  Result shows small gain, little encoding time change, with some decoding time increase.
  Would like further study on this.