## Slide 1: JVET-W0128: AHG12: Alternative classifiers for ALF
Nan Hu, Vadim Seregin, Marta Karczewicz

## Slide 2: Luma ALF in ECM-1.0
F0, F1
  Fixed filters
C0, C1
  Classifiers for fixed filters
F2
  Signaled luma filters
C2
  2x2 block, Laplacian-based classifier for F2
  Class index and geometric transformation are determined

## Slide 3: Proposed methods
C2’
  Alternative classifier for signaled filters
  One bit is signaled per luma filter set
  Disable geometric transformation when C2’ is applied
Different versions of C2’ are tested
 | All intra |  |  | Random access |  |  | Low delay B |  | 
 | BD-rate Y | EncT | DecT | BD-rate Y | EncT | DecT | BD-rate Y | EncT | DecT
Test 1 | -0.05% | 100% | 97% | -0.18% | 99% | 99% | -0.29% | 102% | 98%
Test 2 | -0.09% | 105% | 96% | -0.30% | 103% | 99% | -0.44% | 110% | 101%
Test 3 | -0.11% | 100% | 97% | -0.26% | 100% | 99% | -0.44% | 100% | 99%
Test 4 | -0.14% | 106% | 97% | -0.36% | 104% | 99% | -0.60% | 110% | 98%
Test4 fast | -0.14% | 102% | 97% | -0.35% | 101% | 100% | Around -0.60% | Around 100% | Around 100%
Test 5 | -0.22% | 101% | 96% | Around -0.40% | Around 100% | Around 100% | Around -0.70% | Around 100% | Around 100%

## Slide 4: Test 1
C2’
  Class index is always 0
 | All Intra Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.03% | -0.03% | 104% | 99%
Class A2 | 0.00% | -0.01% | -0.01% | 102% | 97%
Class B | -0.03% | -0.06% | -0.06% | 99% | 95%
Class C | -0.17% | -0.03% | -0.03% | 98% | 95%
Class E | -0.05% | -0.05% | -0.05% | 100% | 99%
Overall | -0.05% | -0.04% | -0.04% | 100% | 97%
Class D | -0.03% | -0.02% | -0.02% | 99% | 98%
Class F | -0.04% | -0.05% | -0.05% | 99% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.13% | -0.15% | -0.02% | 101% | 99%
Class A2 | -0.02% | 0.02% | 0.02% | 101% | 99%
Class B | -0.32% | 0.00% | 0.03% | 99% | 99%
Class C | -0.17% | -0.01% | -0.16% | 97% | 97%
Class E |  |  |  |  | 
Overall | -0.18% | -0.03% | -0.03% | 99% | 99%
Class D | -0.05% | 0.04% | 0.14% | 98% | 98%
Class F | -0.07% | -0.13% | -0.03% | 102% | 98%
 | Low delay B Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.41% | -0.19% | -0.34% | 103% | 101%
Class C | -0.22% | -0.44% | -0.18% | 98% | 96%
Class E | -0.21% | -0.07% | -0.43% | 105% | 95%
Overall | -0.29% | -0.24% | -0.31% | 102% | 98%
Class D | 0.03% | 0.07% | -0.23% | 102% | 103%
Class F | -0.17% | 0.07% | -0.41% | 103% | 97%

## Slide 5: Test 2
C2’
  Class index is derived as C2
 | All Intra Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | 0.00% | 0.00% | 108% | 99%
Class A2 | -0.01% | 0.00% | 0.00% | 103% | 101%
Class B | -0.11% | 0.02% | 0.02% | 105% | 96%
Class C | -0.19% | 0.00% | 0.00% | 103% | 92%
Class E | -0.08% | 0.01% | 0.01% | 108% | 97%
Overall | -0.09% | 0.01% | 0.01% | 105% | 96%
Class D | -0.03% | 0.00% | 0.00% | 108% | 98%
Class F | -0.13% | 0.03% | 0.03% | 104% | 104%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.21% | -0.15% | -0.01% | 102% | 100%
Class A2 | -0.18% | 0.08% | 0.03% | 102% | 100%
Class B | -0.51% | 0.13% | 0.16% | 104% | 100%
Class C | -0.20% | 0.08% | -0.07% | 105% | 98%
Class E |  |  |  |  | 
Overall | -0.30% | 0.05% | 0.04% | 103% | 99%
Class D | -0.07% | 0.16% | 0.13% | 111% | 96%
Class F | -0.11% | -0.05% | 0.10% | 107% | 98%
 | Low delay B Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.61% | -0.20% | 0.15% | 106% | 102%
Class C | -0.27% | -0.55% | -0.27% | 110% | 101%
Class E | -0.37% | -0.34% | -0.02% | 115% | 100%
Overall | -0.44% | -0.35% | -0.03% | 110% | 101%
Class D | 0.01% | 0.04% | 0.02% | 117% | 99%
Class F | -0.22% | -0.80% | -0.63% | 110% | 96%

## Slide 6: Test 3
C2’
  2x2 block based, 8-band classifier
  class_index = (sum * 8) >> (sample bit depth + 2).
 | All Intra Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.08% | -0.01% | 0.00% | 104% | 97%
Class A2 | -0.03% | -0.02% | -0.02% | 101% | 96%
Class B | -0.11% | -0.02% | -0.02% | 99% | 96%
Class C | -0.16% | -0.02% | -0.02% | 99% | 97%
Class E | -0.11% | 0.04% | 0.04% | 102% | 102%
Overall | -0.11% | -0.01% | -0.01% | 100% | 97%
Class D | -0.03% | 0.00% | 0.00% | 99% | 100%
Class F | -0.08% | -0.02% | -0.03% | 100% | 101%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.23% | 0.05% | -0.09% | 101% | 99%
Class A2 | -0.15% | 0.07% | 0.03% | 101% | 99%
Class B | -0.41% | 0.05% | 0.02% | 100% | 99%
Class C | -0.17% | 0.01% | -0.16% | 100% | 100%
Class E |  |  |  |  | 
Overall | -0.26% | 0.04% | -0.05% | 100% | 99%
Class D | -0.09% | 0.05% | 0.16% | 99% | 97%
Class F | -0.12% | -0.08% | 0.06% | 103% | 99%
 | Low delay B Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.68% | -0.39% | -0.21% | 101% | 100%
Class C | -0.20% | -0.31% | -0.31% | 100% | 98%
Class E | -0.35% | -0.75% | -0.15% | 108% | 101%
Overall | -0.44% | -0.45% | -0.23% | 102% | 100%
Class D | -0.07% | 0.77% | 0.19% | 103% | 104%
Class F | -0.41% | 0.12% | -0.11% | 101% | 94%

## Slide 7: Test 4
C2’
  2x2 block based, 25-band classifier
  class_index = (sum * 25) >> (sample bit depth + 2).
 | All Intra Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.14% | 0.04% | 0.04% | 108% | 98%
Class A2 | -0.09% | 0.03% | 0.03% | 104% | 98%
Class B | -0.16% | 0.04% | 0.04% | 104% | 96%
Class C | -0.18% | 0.00% | 0.00% | 106% | 97%
Class E | -0.12% | 0.06% | 0.06% | 110% | 97%
Overall | -0.14% | 0.03% | 0.03% | 106% | 97%
Class D | -0.03% | 0.00% | 0.00% | 109% | 101%
Class F | -0.17% | 0.07% | 0.07% | 106% | 103%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.29% | -0.01% | 0.00% | 102% | 100%
Class A2 | -0.29% | 0.08% | 0.06% | 102% | 99%
Class B | -0.55% | 0.10% | 0.23% | 103% | 100%
Class C | -0.21% | 0.01% | -0.11% | 106% | 99%
Class E |  |  |  |  | 
Overall | -0.36% | 0.05% | 0.06% | 104% | 99%
Class D | -0.09% | -0.04% | 0.19% | 113% | 99%
Class F | -0.21% | 0.00% | 0.13% | 110% | 99%
 | Low delay B Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.91% | -0.30% | -0.35% | 106% | 99%
Class C | -0.29% | -0.56% | -0.14% | 110% | 97%
Class E | -0.49% | 0.11% | -0.12% | 116% | 99%
Overall | -0.60% | -0.28% | -0.22% | 110% | 98%
Class D | -0.08% | 0.48% | 0.17% | 120% | 102%
Class F | -0.47% | -0.12% | -0.55% | 114% | 99%

## Slide 8: Test 4 - fast
C2’
  2x2 block based, 25-band classifier
  class_index = (sum * 25) >> (sample bit depth + 2).
Encoder speed up is applied to clipping parameter derivation
 | All Intra Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.14% | 0.04% | 0.04% | 105% | 99%
Class A2 | -0.09% | 0.03% | 0.03% | 102% | 97%
Class B | -0.16% | 0.04% | 0.04% | 101% | 98%
Class C | -0.18% | 0.00% | 0.00% | 100% | 96%
Class E | -0.12% | 0.06% | 0.06% | 101% | 98%
Overall | -0.14% | 0.03% | 0.03% | 102% | 97%
Class D | -0.03% | 0.00% | 0.00% | 98% | 97%
Class F | -0.16% | 0.07% | 0.07% | 101% | 100%
 | Random access Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.29% | -0.02% | -0.02% | 103% | 102%
Class A2 | -0.29% | 0.10% | 0.12% | 102% | 101%
Class B | -0.54% | 0.14% | 0.17% | 101% | 100%
Class C | -0.21% | 0.01% | -0.09% | 100% | 99%
Class E |  |  |  |  | 
Overall | -0.35% | 0.07% | 0.05% | 101% | 100%
Class D | -0.09% | -0.03% | 0.19% | 96% | 97%
Class F | -0.21% | -0.02% | 0.03% | 103% | 98%
 | Low delay B Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | ####### | ####### | ####### | #NUM! | #NUM!
Class C | -0.29% | -0.62% | -0.20% | 100% | 101%
Class E | -0.48% | 0.15% | -0.19% | 106% | 99%
Overall | ####### | ####### | ####### | #NUM! | #NUM!
Class D | -0.07% | 0.35% | 0.25% | 98% | 102%
Class F | -0.49% | -0.06% | -0.34% | 102% | 98%

## Slide 9: Test 5
C2’
  Sample based, 25-band classifier
  class_index = (sample value * 25) >> (sample bit depth).
Encoder speed up is applied to clipping parameter derivation
 | All Intra Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.23% | 0.06% | 0.06% | 104% | 96%
Class A2 | -0.16% | 0.04% | 0.04% | 101% | 99%
Class B | -0.25% | 0.08% | 0.08% | 100% | 96%
Class C | -0.21% | 0.01% | 0.01% | 99% | 93%
Class E | -0.25% | 0.14% | 0.13% | 101% | 97%
Overall | -0.22% | 0.06% | 0.06% | 101% | 96%
Class D | -0.06% | 0.03% | 0.03% | 97% | 99%
Class F | -0.90% | 0.30% | 0.30% | 101% | 99%
 | Random access Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | ####### | ####### | ####### | #NUM! | #NUM!
Class A2 | ####### | ####### | ####### | #NUM! | #NUM!
Class B | -0.66% | 0.32% | 0.33% | 100% | 99%
Class C | -0.23% | 0.07% | 0.06% | 98% | 98%
Class E |  |  |  |  | 
Overall | ####### | ####### | ####### | #NUM! | #NUM!
Class D | -0.08% | 0.30% | 0.26% | 94% | 98%
Class F | -0.89% | 0.19% | 0.22% | 101% | 97%
 | Low delay B Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | ####### | ####### | ####### | #NUM! | #NUM!
Class C | -0.32% | -0.43% | -0.08% | 96% | 91%
Class E | -0.64% | -0.10% | -0.37% | 103% | 95%
Overall | ####### | ####### | ####### | #NUM! | #NUM!
Class D | -0.21% | -0.16% | 0.11% | 94% | 101%
Class F | -1.10% | -0.57% | -0.31% | 100% | 98%