## Slide 1: JVET-W0129: AHG10: Using original samples for ALF optimization
Nan Hu, Dmytro Rusanovskyy, Vadim Seregin, Marta Karczewicz

## Slide 2: SAO/BIF/ALF optimization when MCTF is applied
Align sample usage for difference reference software platforms
  Using MCTF filtered samples for SAO and BIF
  Using unfiltered samples for ALF
  No change for HM and ECM
Informal subjective test
  SDR: no subjective differences between the anchor and the tests were observed
Reference software | Samples used for SAO/BIF optimization | Samples used for ALF optimization
HM-16.23 | MCTF filtered samples | N/A
VTM-13.0 | MCTF filtered/unfiltered samples (configurable) | MCTF filtered/unfiltered samples (configurable)
ECM-1.0 | MCTF filtered samples | unfiltered samples

## Slide 3: VTM-13.0: SDR
SAO: Unfiltered samples
ALF: Unfiltered samples
SAO: Filtered samples
ALF: Unfiltered samples
 | Random Access Main 10 |  |  |  | 
 | Over VTM-13.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.21% | -0.13% | -0.12% | 101% | 100%
Class A2 | -0.02% | 0.04% | 0.09% | 100% | 100%
Class B | -0.11% | 0.05% | -0.15% | 101% | 102%
Class C | -0.54% | -0.29% | -0.45% | 100% | 101%
Class E |  |  |  |  | 
Overall | -0.23% | -0.08% | -0.18% | 100% | 101%
Class D | -0.81% | -0.82% | -0.66% | 99% | 100%
Class F | 0.00% | 0.00% | 0.00% | 100% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-13.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.23% | -0.07% | 0.10% | 104% | 103%
Class A2 | -0.07% | 0.05% | 0.16% | 103% | 103%
Class B | -0.16% | 0.14% | 0.03% | 103% | 107%
Class C | -0.51% | -0.28% | -0.52% | 99% | 101%
Class E |  |  |  |  | 
Overall | -0.25% | -0.03% | -0.08% | 102% | 104%
Class D | -0.86% | -0.61% | -0.68% | 98% | 96%
Class F | 0.00% | 0.00% | 0.00% | 100% | 100%

## Slide 4: VTM-13.0: HDR
SAO: Unfiltered samples
ALF: Unfiltered samples
SAO: Filtered samples
ALF: Unfiltered samples
 | Random Access |  |  |  |  |  |  |  |  | 
 | Over VTM-13.0 |  |  |  |  |  |  |  |  | 
 |  |  | wPSNR |  |  | PSNR |  |  |  | 
 | DE100 | PSNR-L100 | Y | U | V | Y | U | V | EncT | DecT
Class H1 | 0.00% | -0.16% | -0.15% | -0.04% | 0.41% | -0.15% | -0.15% | 0.40% | 100% | 99%
Class H2 |  |  |  |  |  | 0.02% | 0.08% | 0.60% | 100% | 100%
Overall | 0.00% | -0.16% | -0.15% | -0.04% | 0.41% | -0.09% | -0.07% | 0.48% | 100% | 99%
 | Random Access |  |  |  |  |  |  |  |  | 
 | Over VTM13.0 |  |  |  |  |  |  |  |  | 
 |  |  | wPSNR |  |  | PSNR |  |  |  | 
 | DE100 | PSNR-L100 | Y | U | V | Y | U | V | EncT | DecT
Class H1 | 0.04% | -0.17% | -0.19% | 0.00% | 0.26% | -0.18% | -0.12% | 0.29% | 100% | 99%
Class H2 |  |  |  |  |  | -0.03% | 0.10% | 0.48% | 100% | 100%
Overall | 0.04% | -0.17% | -0.19% | 0.00% | 0.26% | -0.12% | -0.04% | 0.36% | 100% | 100%

## Slide 5: VTM-13.0: HBD (HDR 12 bits)
SAO: Unfiltered samples
ALF: Unfiltered samples
SAO: Filtered samples
ALF: Unfiltered samples
 | Random Access |  |  |  |  |  |  |  |  | 
 | Over VTM-13.0 |  |  |  |  |  |  |  |  | 
 |  |  | wPSNR |  |  | PSNR |  |  |  | 
 | DE100 | PSNR-L100 | Y | U | V | Y | U | V | EncT | DecT
Class H1 | 0.22% | -0.23% | -0.19% | 0.24% | 0.44% | -0.17% | 0.19% | 0.36% | 102% | 101%
Class H2 |  |  |  |  |  | 0.01% | 0.41% | 0.59% | 104% | 104%
Overall | 0.22% | -0.23% | -0.19% | 0.24% | 0.44% | -0.08% | 0.30% | 0.47% | 103% | 102%
 | Random Access |  |  |  |  |  |  |  |  | 
 | Over VTM-13.0 |  |  |  |  |  |  |  |  | 
 |  |  | wPSNR |  |  | PSNR |  |  |  | 
 | DE100 | PSNR-L100 | Y | U | V | Y | U | V | EncT | DecT
Class H1 | 0.19% | -0.22% | -0.19% | 0.05% | 0.54% | -0.16% | 0.07% | 0.49% | 101% | 99%
Class H2 |  |  |  |  |  | -0.13% | 0.01% | 0.36% | 101% | 100%
Overall | 0.19% | -0.22% | -0.19% | 0.05% | 0.54% | -0.14% | 0.04% | 0.43% | 101% | 100%